## Slide 1
Cryptanalysis
Error Correcting Codes
John Manferdelli
JohnManferdelli@hotmail.com
© 2004-2008, John L. Manferdelli.
This material is provided without warranty of any kind including, without limitation, warranty of non-infringement or suitability for any purpose. This material is not guaranteed to be error free and is intended for instructional use only.

## Slide 2: Binary symmetric channel (BSC)
Each bit transmitted has an independent chance of being received correctly with probability p and incorrectly received with probability q=1-p.
0
1
Transmitted
Received
0
1
p
p
q
q
Can we transmit m bits more reliably over this channel if we have spare bandwidth?

## Slide 3: Error Detection
Suppose we want to transmit 7 bits with very high confidence over a binary symmetric channel. Even if p>.99, we occasionally will make a mistake.
We can add an eight bit, a check sum, which makes any valid eight bit message have an even number of 1’s.
We can thus detect a single bit transmission error. Now the probability of a relying on a “bad” message is Perror=1-(p8+8p7(1-p)) instead of Perror=1-p8. If p=.99, Perror drops from about 7% to .3%.
This allows us to detect an error and hopefully have the transmitter resend the garbled packet.
Suppose we want to avoid retransmission?

## Slide 4: Error Correction
We can turn these “parity checks” which enable error detection to error correction codes as follows. Suppose we want to transmit b1b2b3b4. Arrange the bits in a 2 x 2 rectangle:
b1 | b2 | c1=b1+b2
b3 | b4 | c2=b3+b4
c3=b1+b3 | c4=b2+b4 | c5=b1+b2+b3+b4
We transmit b1b2b3b4c1c2c3c4c5.
The receiver can detect any single error and locate its position.
Another simple “encoding scheme” that corrects errors is the following. We can transmit each bit three times and interpret the transmission as the majority vote. Now the chance of correct reception is Pcorrect=p3+3p2q>p and the chance of error is Perror=3pq2+q3<q. For p=.99, Perror= 0.000298 and Pcorrect= .999702.

## Slide 5: Codewords and Hamming distance
To correct errors in a message “block,” we increase the number of bits transmitted per block. The systematic scheme to do this is called a code, C.
If there are M valid messages per block (often M=2m) and we transmit n>lg(M) bits per block, the M “valid” messages are spread throughout the space of 2n elements.
If there are no errors in transmission, we can verify the message is equal to a codeword with high probability.
If there are errors in the message, we decode the message as the codeword that is “closest” (i.e.-differs by the fewest bits) from the received message.
The number of differences between the two nearest codewords is called the distance of the code or d(C).

## Slide 6: Hamming distance
The best decoding strategy is to decode a message as the codeword that differs least from a codeword. So, for a coding scheme, C, if d(C)=2t+1 or less bits, we can correct t or less errors per block.
If d(C)=s+1, we can detect s or fewer errors.
The Hamming distance, denoted Dist(v, w), between two elements v, w𝝴GF(2)n is the number of bits they differ by. The Hamming distance satisfies the usual conditions for a metric on a space.
The Hamming weight of a vector v𝝴GF(2)n , denoted, ||v|| is the number of 1’s.
If v, w𝝴GF(2)n, Dist(v, w)= ||v⊕w||.

## Slide 7: Definition of a Code
In the case of the “repeat three times” code, Crepeatx3, M=1 and n=3. There are two “codewords,” namely 111 and 000. d(Crepeatx3)=3, so d=2t+1 with t=1.
In general, a C(n,M,d) denotes a code in GF(2)n with M codewords with d(C)=d the minimum distance, n is dimension.
As discussed, such codes can correctly decode transmissions containing t errors or less.
The rate of the code is (naturally) R=lg(M)/n.
Error correcting codes strive to find “high rate” codes that can efficiently encode and decode messages with acceptable error.

## Slide 8: Example rates and errors
Code | n | M | d | R | p1 | p2 | P1,e | P2,e
Repetition x 3 | 3 | 2 | 3 | 1/3 | 3/4 | 7/8 | 0.156 | 0.043
Repetition x 5 | 5 | 2 | 5 | 1/5 | 3/4 | 7/8 | 0.103 | 0.016
Repetition x 7 | 7 | 2 | 7 | 1/7 | 3/4 | 7/8 | 0.071 | 0.006
Repetition x 9 | 9 | 2 | 9 | 1/9 | 3/4 | 7/8 | 0.049 | 0.004
Hamming(7,4) | 7 | 16 | 3 | 4/7 | 3/4 | 7/8 | 0.556 | 0.215
Golay(24,12,8) | 24 | 4096 | 17 | 1/2 | 3/4 | 7/8 |  | 
Hadamard (64,32,16) | 64 | 32 | 16 | 3/16 | 3/4 | 7/8 |  | 
RM(4,2) | 16 | 11 | 4 |  |  |  |  | 
BCH[7,3,4] | 7 | 8 | 4 | 3/7 |  |  |  | 

## Slide 9: Shannon
Source Coding Theorem: The n random variables can be encoded by nH bits with negligible information loss.
Channel Capacity: C= maxP(x)(H(I|O)-H(I)). For a DMC, BSC with error rate p, this implies CBSC(p)= 1+plg(p)+q lg(q). So for BSC R= 1-H(P).
Channel Coding Theorem: For all R<Cmax, 𝜖>0, C(n,M,d) of length n with M codewords: M≥2[Rn] and P(i)error≦𝜖 for i=1,2,…,M.
Translation: Good codes exist that permit transmission near the channel capacity with arbitrarily small error.

## Slide 10: The Problem of Coding Theory
Despite Shannon’s fundamental results, this is not the end of the coding problem!
  Shannon’s proof involved random codes
  Finding the closest codeword to a random point is the shortest vector problem, so “closest codeword” decoding is computationally difficult. Codes must be systematic to be useful.
  The Encoding Problem: Given an m bit message, m, compute the codeword, t (for transmitted), in C(n,M,d).
  The Decoding Problem: Given an n bit received word, r=t+e, where e was the error, compute the codeword in C(n,M,d) closest to r.
  General codes are hard to decode

## Slide 11: Bursts
Bursty error correction: Errors tend to be “bursty” in real communications.
Burst error correcting codes can be constructed by “spreading out codewords”. Let cwi[j] mean bit j of codeword i. Transmit cw1[1] , cw2[1] ,…, cwk[1], cw1[2] ,… where k is the size of a “long” error.
Some specific codes (RS, for example) are good at bursty error correction.

## Slide 12: Channel capacity for Binary Symmetric Channel
Discrete memory-less channel: Errors independent and identically distributed according to channel error rate. (No memory).
Rate for code, RC= lg(M)/n.
Channel capacity intuition: How many bits can be reliably transmitted over a BSC?
  The channel capacity, c, of a channel is c= supX I(X;Y), where X is the transmission distribution and Y is the reception probability
  Shannon-Hartley: c= Blg(1+S/N), B is the bandwidth, S is the signal power and N is the noise power.
  Information rate, R=rH.

## Slide 13: How much information can be transmitted over a BSC with low error?
How many bits can be reliably transmitted over a BSC? Answer (roughly): The number of bits of bandwidth minus the noise introduced by errors.
Shannon’s channel coding theorem tells us we can reliably transmit up to the channel capacity.
However, good codes are hard to find and generally computationally expensive.

## Slide 14: Calculating rates and channel capacity
For single bit BSC, C=1+plg(p)+qlg(q).
Recall c= supX I(X;Y).
The distribution P(X=0)=P(X=1)=1/2 maxmizes this.
c= 1/2+1/2+plg(p)+qlg(q)

## Slide 15: Linear Codes
A [n,k,d] linear code is an k-subspace of an n-space over F (usually GF(2)) with minimum distance d.
  An [n,k,d] code is also a (n, 2k,d) code
Standard form for generator is G= (Ik|A) with k message bits, n codeword bits. Codeword c=mG.
For a linear code, d=minu≠0, u𝝴C {wt(u)}.
  Proof: Since C is linear, dist(u, w)= dist(u-w,0)=wt(u-v). Since the code is linear, u-v 𝝴 C. That does it.
Parity check matrix is H: v 𝝴 C iff vHT=0.
If G is in standard form, H=[-AT|In-k]. Note that GH=0.
Example: Repetition code is the subspace in GF(2)3 generated by (1,1,1).

## Slide 16: G and H and decoding
Let r=c+e, where r is the received word, c is the transmitted word and e is the error added by the channel.
Note codewords are linear combinations of rows of G and rHT=cHT+eHT=eHT.
Coset leader table
  Minimum weight
  Coset leader Error Syndrone
  c1 c2 c3 … cM 0 0=0HT
  c1+e1 c2+e1 c3+e1 … cM+e1 e1 e1HT
  c1+e2 c2+e2 c3+e2 … cM+e2 e2 e2HT
  … …. … ….
  c1+eh-1 c2+eh-1 c3+eh-1 … cM+eh-1 eh-1 eh-1HT

## Slide 17: Syndrome and decoding Linear Codes
S(r)= rHT is called the syndrone.
A vector having minimum Hamming weight in a coset is called a coset leader.
Two vectors belong to the same coset iff they have the same syndrone.
Now, here’s how to systematically decode a linear code:
  Calculate S(r).
  Find coset leader, e, with syndrone S(r).
  Decode r as r-e.
This is more efficient than searching for nearest codeword but is only efficient enough for special codes.

## Slide 18: Syndrone decoding example (H[7,4])
1 0 0 0 1 1 0 1 1 0 1 1 0 0 1 1 0
G= [I4|A]= 0 1 0 0 1 0 1 = [-AT|I3], H= 1 0 1 1 0 1 0, HT= 1 0 1
0 0 1 0 0 1 1 0 1 1 1 0 0 1 0 1 1
0 0 0 1 1 1 1 1 1 1
1 0 0
0 1 0
0 0 1
Message: 1 1 0 0.
Codeword transmitted: 1 1 0 0 0 1 1.
Received: 1 1 0 0 0 0 1. (Error in 6th position)

## Slide 19: Syndrone decoding example (H[7,4])
Coset table (Left)
Syn Coset Leader
000 0000000 1000011 0100101 1100110 0010110 1010101 0110011 1110000
110 0000001 1000010 0100100 1100111 0010111 1010100 0110010 1110001
101 0000010 1000001 0100111 1100100 0010100 1010111 0110001 1110010
011 0000100 1000111 0100001 1100010 0010010 1010001 0110111 1110100
111 0001000 1001011 0101101 1101110 0011110 1011101 0111011 1111000
100 0010000 1010011 0110101 1110110 0000110 1000101 0100011 1100000
010 0100000 1100011 0000101 1000110 0110110 1110101 0010011 1010000
001 1000000 0000011 1100101 0100110 1010110 0010101 1110011 0110000
(1 1 0 0 0 1 ) HT= (0 1 0) which is the syndrone of the seventh row whose coset leader is e= (0 0 0 0 0 1 0).
Decode message as (1 1 0 0 0 1) + (0 0 0 0 0 1 0) = (1 1 0 0 1 1).

## Slide 20: Syndrone decoding example (H[7,4])
Coset table (Right)
Syn
0001111 1001100 0101010 1101001 0011001 1011010 0111100 1111111
0001110 1001101 0101011 1101000 0011000 1011011 0111101 1111110
0001101 1001110 0101000 1101011 0011011 1011000 0111110 1111101
0001011 1001000 0101110 1101101 0011101 1011110 0111000 1111011
0000111 1000100 0100010 1100001 0010001 1010010 0110100 1110111
0011111 1011100 0111010 1111001 0001001 1001010 0101100 1101111
0101111 1101100 0001010 1001001 0111001 1111010 0011100 1011111
1001111 0001100 1101010 0101001 1011001 0011010 1111100 0111111

## Slide 21: Bounds: How good can codes be?
Let Aq(n, d) denote the largest code with minimum distance d.
Sphere Packing (Hamming) Bound: If d=2e+1, Aq(n,d)≦∑k=0e nCk(q-1)k ≦ qn.
  Proof: Let l be the number of codewords. l(1+(q-1)nC1+(q-1)2nC2+…+(q-1)enCe) ≦ qn because the e-spheres around the codewords are disjoint.
GSV Bound: There is a linear [n, k, d] code satisfying the inequality: Aq(n,d)≥qn/(1+(q-1) nC1+(q-1)2nC2+…+(q-1)d-1nCd-1)
  Proof: The d-1 columns of the check matrix are linearly independent iff the code has distance d. So qn-k³(1+(q-1) nC1+(q-1)2nC2+…+(q-1)d-1nCd-1)
Singleton Bound: M≦qn-d+1, so R≦1-(d-1)/n.
  Proof: Let C be a (n,M,d) code. Since every codeword differs by at least d-1 positions, qn-(d-1)≥M.

## Slide 22: MDS
Singleton Bound: M≦qn-d+1, so R≦1-(d-1)/n.
Code meeting Singleton bound is an MDS code.
If L is an MDS code so it L⟂.
If L is an [n,k] code with generator G, L is MDS iff there are k linearly independent columns.
Binary 3-repetition code is an MDS

## Slide 23: Hamming
A Hamming code is a [n,k,d] linear code with
  n= 2m -1,
  k= 2m -1 -m
  d=3.
To decode r=c+e:
  Calculate S(r)= rHT.
  Find j which is the column of H with the calculated syndrome.
  Correct position j.

## Slide 24: [7,4] Hamming code
The [7,4] code has encoding matrix G, and parity check H where:
1 0 0 0 1 1 0 1 1 0 1 1 0 0
  G= 0 1 0 0 1 0 1 H= 1 0 1 1 0 1 0
  0 0 1 0 0 1 1 0 1 1 1 0 0 1
  0 0 0 1 1 1 1
The code words are:
0000000, weight: 0
1000011, weight: 3
0100101, weight: 3
1100110, weight: 4
0010110, weight: 3
1010101, weight: 4
0110011, weight: 4
1110000, weight: 3
0001111, weight: 4
1001100, weight: 3
0101010, weight: 3
1101001, weight: 4
0011001, weight: 3
1011010, weight: 4
0111100, weight: 4
1111111, weight: 7

## Slide 25: Decoding Hamming code
1 0 0 0 1 1 0 1 1 0 1 1 0 0 1 1 0
G= [I4|A]= 0 1 0 0 1 0 1 = [-AT|I3], H= 1 0 1 1 0 1 0, HT= 1 0 1
0 0 1 0 0 1 1 0 1 1 1 0 0 1 0 1 1
0 0 0 1 1 1 1 1 1 1
1 0 0
0 1 0
0 0 1
Message: 1100  1100011.
Received as 1100001.
1100001 HT= 010 which is sixth row of HT. Error in sixth bit.
1100001+0000010= 110011

## Slide 26: Dual Code
If C is an [n,k] linear code, then C⟂ = {u: u·c=0, c𝝴C} is an [n, n-k] linear code called the dual code.
The parity check matrix, H, of a code, C, is the generator of its dual code.
A code is self-dual if C= C⟂.
Weight enumerator: Let Ai be the number of codewords in C of weight i, then A(z)= ∑i Aizi is the weight enumerator.

## Slide 27: Example: dual code of (7,4) Hamming code
G= 1101100
1011010
0111001
Codewords:
0000000 0111001
1101100 1010101
1011010 1100011
0110110 0001111

## Slide 28: Hadamard Code
Hadamard Matrix: H HT=nIn. If H is Hadamard of order m, J=
    H H
    H -H
  is Hadamard of order 2m.
Hadamard code uses this property. Generator matrix for this code is G= [H|-H]T. For message I, 0≦<2i send the row corresponding to i.
  Used on Mariner spacecraft (1969).
To decode, a 2i bit received word, r, compute di= r×Ri, where Ri is the 2i bit row i.
  If there are no errors, the correct row will have di= 2i-1 and all other rows will have di=0.
  If one error, di= 2i-2 (all dot products but 1 will be ±2), etc.

## Slide 29: Hadamard Code example
Let hij= (-1)a0 b0 + ... + a4 b4, where a and b index the rows and columns respectively. This gives a 32 times 32 entry matrix, H.
H(64, 32, 16): 64=26 bit codewords, 6 messages. First 32 rows:
00000000000000000000000000000000 00
01010101010101010101010101010101 01
00110011001100110011001100110011 02
01100110011001100110011001100110 03
00001111000011110000111100001111 04
01011010010110100101101001011010 05
00111100001111000011110000111100 06
01101001011010010110100101101001 07
00000000111111110000000011111111 08
01010101101010100101010110101010 09
00110011110011000011001111001100 10
01100110100110010110011010011001 11
00001111111100000000111111110000 12
01011010101001010101101010100101 13
00111100110000110011110011000011 14
01101001100101100110100110010110 15
00000000000000001111111111111111 16
01010101010101011010101010101010 17
00110011001100111100110011001100 18
01100110011001101001100110011001 19
00001111000011111111000011110000 20
01011010010110101010010110100101 21
00111100001111001100001111000011 22
01101001011010011001011010010110 23
00000000111111111111111100000000 24
01010101101010101010101001010101 25
00110011110011001100110000110011 26
01100110100110011001100101100110 27
00001111111100001111000000001111 28
01011010101001011010010101011010 29
00111100110000111100001100111100 30
01101001100101101001011001101001 31

## Slide 30: Hadamard Code example
Last 32 rows:
11111111111111111111111111111111 32
10101010101010101010101010101010 33
11001100110011001100110011001100 34
10011001100110011001100110011001 35
11110000111100001111000011110000 36
10100101101001011010010110100101 37
11000011110000111100001111000011 38
10010110100101101001011010010110 39
11111111000000001111111100000000 40
10101010010101011010101001010101 41
11001100001100111100110000110011 42
10011001011001101001100101100110 43
11110000000011111111000000001111 44
10100101010110101010010101011010 45
11000011001111001100001100111100 46
10010110011010011001011001101001 47
11111111111111110000000000000000 48
10101010101010100101010101010101 49
11001100110011000011001100110011 50
10011001100110010110011001100110 51
11110000111100000000111100001111 52
10100101101001010101101001011010 53
11000011110000110011110000111100 54
10010110100101100110100101101001 55
11111111000000000000000011111111 56
10101010010101010101010110101010 57
11001100001100110011001111001100 58
10011001011001100110011010011001 59
11110000000011110000111111110000 60
10100101010110100101101010100101 61
11000011001111000011110011000011 62
10010110011010010110100110010110 63

## Slide 31: Hadamard Code example
Suppose received word is:
  11001100110011000011001100110001
Dot product with rows of matrix is:
00: 002, 01: 002, 02: -02, 03: -02, 04: -02, 05: -02, 06: 002, 07: 002.
08: -02, 09: -02, 10: 002, 11: 002, 12: 002, 13: 002, 14: -02, 15: -02.
16: -02, 17: -02, 18: -30, 19: 002, 20: 002, 21: 002, 22: -02, 23: -02.
24: 002, 25: 002, 26: -02, 27: -02, 28: -02, 29: -02, 30: 002, 31: 002.
32: -02, 33: -02, 34: 002, 35: 002, 36: 002, 37: 002, 38: -02, 39: -02.
40: 002, 41: 002, 42: -02, 43: -02, 44: -02, 45: -02, 46: 002, 47: 002.
48: 002, 49: 002, 50: 030, 51: -02, 52: -02, 53: -02, 54: 002, 55: 002.
56: -02, 57: -02, 58: 002, 59: 002, 60: 002, 61: 002, 62: -02, 63: -02.
So we decode as 50 and estimate 1 error.

## Slide 32: The amazing Golay code
Golay Code G24 is a [24, 12, 8] linear code.
G= [I12|C0|N] = [I12|B]
  C0 = (1,1,1,1,1,1,1,1,1,1,1,0)T .
  N is formed by circulating (1, 1, 0, 1, 1, 1, 0, 0, 0, 1, 0) 11 times and appending an row of 11 1's.
The first row of N corresponds to the quadratic residues (mod 11).
Note that wt(r1+r2)= wt(r1)+wt(r2)-2[r1·r2], all codewords have weight divisible by 4 and d(C)=8.
G24 = G24⟂. To decode Golay, write G= [I12|B] and BT= (b1, b2 , ..., b12) with bi a column vector.

## Slide 33: G for G(24,12, 8)
1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19 20 21 22 23 24
1 1 0 0 0 0 0 0 0 0 0 0 0 1 1 1 0 1 1 1 0 0 0 1 0
2 0 1 0 0 0 0 0 0 0 0 0 0 1 0 1 1 0 1 1 1 0 0 0 1
3 0 0 1 0 0 0 0 0 0 0 0 0 1 1 0 1 1 0 1 1 1 0 0 0
4 0 0 0 1 0 0 0 0 0 0 0 0 1 0 1 0 1 1 0 1 1 1 0 0
5 0 0 0 0 1 0 0 0 0 0 0 0 1 0 0 1 0 1 1 0 1 1 1 0
6 0 0 0 0 0 1 0 0 0 0 0 0 1 0 0 0 1 0 1 1 0 1 1 1
7 0 0 0 0 0 0 1 0 0 0 0 0 1 1 0 0 0 1 0 1 1 0 1 1
8 0 0 0 0 0 0 0 1 0 0 0 0 1 1 1 0 0 0 1 0 1 1 0 1
9 0 0 0 0 0 0 0 0 1 0 0 0 1 1 1 1 0 0 0 1 0 1 1 0
10 0 0 0 0 0 0 0 0 0 1 0 0 1 0 1 1 1 0 0 0 1 0 1 1
11 0 0 0 0 0 0 0 0 0 0 1 0 1 1 0 1 1 1 0 0 0 1 0 1
12 0 0 0 0 0 0 0 0 0 0 0 1 0 1 1 1 1 1 1 1 1 1 1 1

## Slide 34: Properties of the Golay code
The Golay code G(24,12, 8) is self dual. Thus, GGT=I+BBT=0
Other properties:
  Non-zero positions form a (24, 8, 5) Steiner system.
  Weights are multiples of 4.
  Minimum weight CW is 8 (hence d=8).
  Codewords have weights 0, 8, 12, 16, 24.
  Weight enumerator is 1+(759)x8+(2576)x12+(759)x16+x24.
Voyager 1, 2 used this code.
Get G(23,12, 7) is obtained by deleting last column. It is a remarkable error correcting code. 7= 2x3+1, so it corrects 3 errors. It does this “perfectly.”

## Slide 35: The Golay code G(23,12, 7) is perfect!
There are 212 code words or sphere centers.
There are 23C1=23 points in Z23 which differ by one bit from a codeword.
There are 23C2=253 points in Z23 which differ by two bits from a codeword.
There are 23C3=1771 points in Z23 which differ by two bits from a codeword.
212 (1+23+253+1771)= 212(2048)=212x211= 223.
23 bit strings which differ by a codeword by 0,1,2 or 3 bits partition the entire space.
The three sporadic simple Conway’s groups are related to the lattice formed by codewords and provided at least one Ph.D. thesis.

## Slide 36: Decoding G(24,12, 8)
Suppose r=c+e is received. G= [I12 | B]=[c1, c2, …, c24] and BT= [b1, b2, …, b12].
To decode:
  Compute s= rGT, sB, s+ciT, 1 ≦ i ≦ 24 and sB+bjT, 1 ≦ j ≦ 12.
  If wt(s)≦3, non-zero entries of s correspond to non-zero entries of e.
  If wt(sB)≦3, there is a non-zero entry in the k-th position of sB if the k+12-th position of e is non-zero.
  If wt(s+ciT) ≦ 2, for some j, 13 ≦ j ≦ 24 then ej=1 and non-zero entries of s+ejT are in the same positions as non-zero entries of e.
  If wt(sB+bjT) ≦ 2, for some j, 1 ≦ j ≦ 12 then ej=1 and non-zero entries of sB+bjT at position k correspond to non-zero entries of ek+12.

## Slide 37: Decoding G(24,12, 8) example
G is 12 x 24. G=[I12|B]= (c1, c2, …, c24).
BT=(b1, b2, …, b12).
m=(1,1,0,0,0,0,0,0,0,0,0,1,0).
mG=(1,1,0,0,0,0,1,0,1,0,1,1,0).
r=(1,1,0,1,0,0,0,0,0,0,1,0,1,0,0,0,0,1,0,0,0,0,1,0).
s=(011110110010).
sB=(101011001000).
Neither has wt≦3, so we compute s+cjT, sB+bjT.
s+b4T=(0,0,0,0,0,0,0,1,0,1,0,0)
c= r+(0,0,0,1,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,1,0,1,0,0)
c= (1,1,0,0,0,0,0,0,0,0,1,0,1,0,0,0,0,1,0,1,0,1,1,0)
m=(1,1,0,0,0,0,0,0,0,0,0,1,0).

## Slide 38: Cyclic codes
A cyclic code, C, has the property that if (c1, c2, ... , cn)𝝴C then (cn, c1, ... , cn-1) 𝝴 C.
Remember polynomial multiplication in F[x] is linear over F.
Denoting Un(x)= xn-1 we have
Theorem: C is a cyclic code of length n iff its generator g(x)= a0+a1x+ ... +an-1xn-1|Un(x) where codewords c(x) have the form m(x) g(x). Further, if Un(x)= h(x)g(x), c(x) in C iff h(x)c(x)= 0 (mod Un(x)).

## Slide 39: Cyclic codes
Let C be a cyclic code of length n over F, and let a=(a0, a1, … , an-1) 𝝴 C be associated with the polynomial pa(x)=a0+a1x+ … +an-1xn-1. Let g(x) the polynomial of smallest degree over such associated polynomials the g(x) is the generating polynomial of C and
    g(x) is uniquely determined.
    g(x)|xn-1
    C: f(x)g(x) where deg(f(x))≦n-1-deg(g)
    If h(x)g(x)=xn-1, m(x)C iff h(x)m(x)=0 (mod xn-1).
The associated matrices G and H are on the next slide.

## Slide 40: G, H for cyclic codes
Let g(x) be the generating polynomial of the cyclic code C.
  G= g0 g1 g2 … … … … gk 0 0 0 0
  0 g0 g1 g2 … … … … gk 0 0 0
  0 0 g0 g1 g2 … … … … gk 0 0
  … … … …
  0 … 0 0 g0 g1 g2 … … … … gk
  H= hl hl-1 hl-2 … … … … h0 0 0 0 0
  0 hl hl-1 hl-2 … … … … h0 0 0 0
  … … … …
  0 0 0 0 hl hl-1 hl-2 … … … … h0

## Slide 41: Cyclic code example
g(x)= 1+x2+x3, h(x)= 1+x2+x3+x4, g(x)h(x)= xn-1, n=7.
Message 1010 corresponds to m(x)= 1+x2.
g(x)m(x)=c(x)= 1+x3+x4+x5, which corresponds to the codeword 1001110.
G, H are
Codewords are
  1011000 0101100 0010110 0001011 1110100 0111010 0011101 1001110
  0100111 1100010 0110001 1101001 1010011 1000101 1101001 1111111

## Slide 42: BCH Codes
Cyclic codes; so generator, g(x) satisfies g(x)|xn–1.
Theorem: Let C be a cyclic [n, k, d] code over Fq, q=pm. Assume p does not divide n and g(x) is the generator. Let a be a primitive root of xn-1 and suppose that for some l, d, we have g(al)= g(al+1)= … = g(al+d)=0, then d³d+2.
Constructing a BCH code:
  Factor xn-1= f1(x) f2(x)…fr(x), each fi(x), irreducible.
  Pick a, a primitive root of 1.
  xn-1= (x- a)(x- a2)…(x- an-1) and fi(x)= ∏t(x-aj(t)).
  qj(x)= fi(x), where fi(a)= 0. qj(x) are not necessarily distinct.
  BCH code at designed distance d has generator g(x)=LCM[qk+1(x),…, qk+d-1(x)].
Theorem: A BCH code of designed distance d has minimum weight ³d. Proof uses theorem above.

## Slide 43: Example BCH code
F=F2, n=7.
x7-1=(x-1)(x3+x2+1)(x3+x+1)
We pick a, a root of (x3+x+1) as a primitive element.
Note that a2 and a4 are also primitive roots of (x3+x+1), so x3+x+1=(x-a)(x- a2)(x- a4) and x3+x2+1=(x- a3)(x- a6)(x- a6)
q0(x)=x-1, q1(x)= q2(x)= q4(x)= x3+x2+1.
k= -1, d=3, g(x)=[x-1, x3+x2+1]= x4+x3+1.
This yields a [7,3,4] linear code.

## Slide 44: Decoding BCH Codes
For r=c+e:
  Compute (s1, s2)= rHT,
  If s1= 0, no error,
  If s1≠0 put s2/s1= aj-1, error is in position j (of p≠2, ei= s1/a(j-1)(k+1),
  c=r-e.

## Slide 45: Example Decoding a BCH Code
x7-1, a, a root of x3+x+1=0. This is the 7-repetition code.
rHT= (1,1,1,1,0,1,1,1) HT=(a+a2, a)
H= 1, a, a2, a3, a4, a5, a6
1, a2, a4, a6, a8, a10, a12
s1= a+a2 =1+a+a2+a3+a4+a5+a6
s2= a=1+a2+a4+a6+a8+a10+a12
s1/s2=a4 , j-1=4, j=5, e=(0,0,0,0,1,0,0).
s1= eja(j+1)(k+1)
s2= eja(j+1)(k+2)

## Slide 46: Reed Solomon
Reed-Solomon code is BCH code over Fq with n= q-1. Let 𝛼 be a primitive root of 1 and choose d: 1≦d<n with g(x)= (x-𝛼) (x-𝛼2) ... (x- 𝛼d-1).
  Since g(𝛼) = g(𝛼2) = … =g(𝛼d-1)=0, BCH bound shows d(C)≥d.
  Codewords are g(x)f(x), deg(f(x))≦n-d. There are qn-d+1 such polynomials so qn-d+1 codewords.
  Since this meets the Singleton bound, the Reed Solomon code is also an MDS code.
  The Reed Solomon Code is an [n, n-d+1, d] linear code for these parameters

## Slide 47: Reed Solomon example
Example:
  F=GF(22)={0,1,w,w2}
  n=q-1=3, a= w.
  Choose d=2, g(x)= (x-w).
  G= w 1 0
  0 w 1
Code consists of all 16 linear combinations of the rows of G.
For CD’s:
  F=GF(28), n= 28-1=255, d=33.
  222 information bytes.33 check bytes.
  Codewords have 8 x 255 = 2040 bits.

## Slide 48: Polynomials and RM codes
R(r,m) has parameters [n=2m , k= 1 + mC1 + ... + mCr d=2m-r], it consists of boolean functions whose polynomials are of degree ≦ m.
RM(r,m)^ = RM(m-r-1,m).
RM(0,m)= {0 , 1}, RM(r+1, m+1)= RM(r+1, m)*R(r, m).
RM(n,0) is a repetition code with rate 1/n.
Min distance in R(r,m)= 2m-r.
G(r+1,m) G(r+1,m)
G(r+1, m+1)= 0 G(r,m)

## Slide 49: RM(4,0) and RM(4,1)
n=24=16.
Constants
  0000 0000 0000 0000, 1111 1111 1111 1111.
Linear
  1010 1010 1010 1010, 0101 0101 0101 0101,
  0000 1111 0000 1111, 0000 0000 1111 1111

## Slide 50: RM(r,4) code example
1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1
x4 0 0 0 0 0 0 0 0 1 1 1 1 1 1 1 1
x3 0 0 0 0 1 1 1 1 0 0 0 0 1 1 1 1
x2 0 0 1 1 0 0 1 1 0 0 1 1 0 0 1 1
x1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
x3x4 0 0 0 0 0 0 0 0 0 0 0 0 1 1 1 1
x2x4 0 0 0 0 0 0 0 0 0 0 1 1 0 0 1 1
x1x4 0 0 0 0 0 0 0 0 0 1 0 1 0 1 0 1
x2x3 0 0 0 0 0 0 1 1 0 0 0 0 0 0 1 1
x1x3 0 0 0 0 1 0 1 0 0 0 0 0 0 1 0 1
x1x2 0 0 0 1 0 0 0 1 0 0 0 1 0 0 0 1
x2x3x4 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1 1
x1x3x4 0 0 0 0 0 0 0 0 0 0 0 0 0 1 0 1
x1x2x4 0 0 0 0 0 0 0 0 0 0 0 1 0 0 0 1
x1x2x3 0 0 0 0 0 0 0 1 0 0 0 0 0 0 0 1
x1x2x3x4 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1

## Slide 51: McEliece Cryptosystem
Bob chooses G for a large [n, k, d] linear code, we particularly want large d (for example, a [1024, 512, 101] Goppa code which can correct 50 errors in a 1024 bit block). Pick a k x k invertible matrix, S, over GF(2) and P, an n x n permutation matrix, and set G1=SGP. G1 is Bob’s public key; Bob keeps P, G and S secret.
To encrypt a message, x, Alice picks an error vector, e, and sends y=xG1+e (mod 2).
To decrypt, Bob, computes y1=yP-1 and e1=eP-1, then y1=xSG+e1. Now Bob corrects y1 using the error correcting code to get x1. Finally, Bob computes x=x1S-1.
Error correction is similar to the “shortest vector problem” and is believed to be “hard.” In the example cited, a [1024, 512, 101] Goppa code, finding 50 errors (without knowing the shortcut) requires trying 1024C50>1085 possibilities.
A drawback is that the public key, G1, is largest.

## Slide 52: McEliece Cryptosystem example - 1
Using the [7, 4] Hamming code, G=
    1 0 0 0 1 1 0
    0 1 0 0 1 0 1
    0 0 1 0 0 1 1
    0 0 0 1 1 1 1
m=1011.
S= 1 0 0 1 P= 0 0 1 0 0 0 0
1 1 0 1 1 0 0 0 0 0 0
0 1 0 1 0 0 0 0 1 0 0
1 1 1 0 0 0 0 0 0 1 0
0 0 0 0 0 0 1
0 1 0 0 0 0 0

## Slide 53: McEliece Cryptosystem example - 2
G1=
    0 0 1 1 0 1 0
    1 0 1 0 0 1 1
    1 1 0 0 0 1 0
    1 0 1 0 1 0 0
e= (0 1 0 0 0 0 0)
y1= yP-1= (0 0 1 0 0 0 1)
x1= (0 0 1 0 0 1 1)
x0= (0 0 1 0)
x= x0S-1= (1 0 1 1)

## Slide 54: End