## Slide 1
Cryptanalysis
Elliptic Curves and Lattices
John Manferdelli
JohnManferdelli@hotmail.com
© 2004-2020, John L. Manferdelli.
This material is provided without warranty of any kind including, without limitation, warranty of non-infringement or suitability for any purpose. This material is not guaranteed to be error free and is intended for instructional use only.

## Slide 2: Elliptic Curves
Motivation:
  Full employment act for mathematicians
  Elliptic curves over finite fields have an arithmetic operation
  Index calculus doesn’t work on elliptic curves.
  Even for large elliptic curves, field size is relatively modest so arithmetic is faster
  .
Use this operation to define a discrete log problem.
To do this we need to:
  Define point addition and multiplication on an elliptic curve
  Find an elliptic curve whose arithmetic gives rise to large finite groups with elements of high order
  Figure out how to embed a message in a point multiplication.
  Figure out how to pick “good” curves.

## Slide 3: Rational Points
Bezout
Linear equations
  Disconnected:
  Connected: a= 7, b=-10
  Troublesome: a=3, b=-2
Arithmetic
D= 4a3-27b2
Genus, rational point for g>1
Mordell
,

## Slide 4: Equation solving in the rational numbers
Linear case: solve or, find the rational points on the curve .
  Clearing the fractions in x and y, this is equivalent to solving the equation in the integers. Suppose (a,b)=d, there are :. If say c=d’d, a(d’x)+b(d’y)=d’d=c and we have a solution. If d does not divide c, there isn’t any. We can homogenize the equation to get ax+by=cz and extend this procedure, here, because of z, there is always a solution.
Quadratic (conic) case: solve or find the rational points on the curve .
  . Let (x,y) be another rational point and join the two by a line: y= m(x+1). Note m is rational. Then and . Completing the square and simplifying we get . So, and substituting in the linear equation, . These are all the solutions.
Cubic case is more interesting!

## Slide 5: Bezout’s Theorem
Let be be homogeneous polynomials with deg(f(x,y,z))=m and deg(g(x,y,z))=n . Let C1 and C2 be the curves in, defined by:
  C1 = {(x,y,z): f(x,y,z)=0}; and,
  C2 = {(x,y,z): g(x,y,z)=0}.
If f and g have no common components and , then .
I is the intersection multiplicity. This is a fancy way of saying that (multiple points aside), there are mn points of intersection between C1 and C2. There is a nice proof in Silverman and Tate, Rational Points on Elliptic Curves, pp 242-251. The entire book is a must read.
A consequence of this theorem is that two cubic curves intersect in nine points.

## Slide 6: Elliptic Curve Preliminaries -1
Let K be a field. char(K) is the characteristic of K which is either 0 or pn for some prime p, n>0.
is a general cubic.
F(x,y) is non-singular if Fx(x,y) or Fy(x,y)  0.
If char(K)2,3, F(x,y)=0 is equivalent to which is denoted by and is called the Weierstrass equation.
Note that the intersection of a line (y=mx+d) and a cubic, EK(a,b) is 1, 2 or 3 points.
Idea is: given 2 points, P,Q on a cubic, the line between P and Q generally identifies a third point on the cubic, R.
Two identical points on a cubic generally identify another point which is the intersection of the tangent line to the cubic at the given point with the cubic.
The last observation is the motivation for defining a binary operation (addition) on points of a cubic.

## Slide 7: Elliptic Curve Preliminaries - 2
We are most interested in cubics with a finite number of points.
Cubics over finite fields have a finite number of points (duh).
EK(a,b) is an elliptic equation over the “affine plane.”
It is often easier to work with elliptic equations over the “projective plane”. The projective plane consists of the points (a,b,c) (not all 0) and (a,b,c) and (ad,bd,cd) represent the same point.
  The map (x,y,1)(xz,yz,z) sets up a 1-1 correspondence between the affine plane (plus the “infinities”) and the projective plane.
  EK(a,b) is zy2= x3+axz2+bz3. Note these are homogeneous equations.
  The points (x,y,0) are called the line at infinity.
  The point at infinity, (0,1,0) is the natural “identity element” O and its introduction is less “ad hoc.”

## Slide 8: Elliptic Curves
A non-singular Elliptic Curve is a curve, having no multiple roots, satisfying the equation: .
  The points of interest on the
  curve are those with rational coordinates which can be combined using the “addition” operation.
  These are called “rational points.”
Graphic by Richard Spillman

## Slide 9: Multiple roots
Here is the condition that the elliptic curve, , does not have multiple roots.
Set .
  At a double point, ; so . Thus and 0=(3x2+a) have a common zero.
  Substituting , we get 0=x3-3x3+b, b= 2x3, b2=4x6. Cubing, a= -3x2, we get a3= -27x6. So b2/4=a3/(-27) or 27b2+4a3=0. Thus, if, then ER(a, b) does not have multiple roots.
We define the “discriminant” as .

## Slide 10: Elliptic curve addition
The addition operator on a non-singular elliptic curve maps two points, P and Q, into a third “P+Q”. Here’s how we construct “P+Q” when PQ .
Construct straight line through P and Q which hits E at R.
P+Q is the point which is the reflection of R across the x-axis.
P
Q
P+Q
Graphic by Richard Spillman
R

## Slide 11: Addition for points P, Q in ER(a, b) - 1
Suppose we want to add two distinct points P and Q lying on the curve , where and ) with, then .
Suppose , here is the computation: Join P and Q by the line
  Substituting for y into we get
  .
  are the roots of this equations so .
To summarize, if (and ):

## Slide 12: Multiples in Elliptic Curves 1
P+P (or 2P) is defined in terms of the tangent to the cubic at P.
Construct tangent to P and reflect the point in y at which it intercepts the curve (R) to obtain 2P.
P can be added to itself
k times resulting in a point Q = kP.
P
P+P= 2P
R
Graphic by Richard Spillman

## Slide 13: Addition for points P, Q in ER(a, b) - 2
Suppose we want to add two distinct points P and Q lying on the curve , where and and .
Case 1, : In this case, and the line between P and Q “meet at infinity,” this is the point we called and we get . Note so .
Case 2, so : The slope of the tangent line to at is . Differentiating , we get , so . The addition formulas on the previous page still hold.

## Slide 14: Addition in - summary
Given two points P and Q lying on the curve , where and with then where:
    If , and
    If and , then and
    If and , then , and

## Slide 15: Point multiplication in ER(a, b)
By using the doubling operation just defined, we can easily calculate P, 2P, 4P, 8P ,…, 2eP and by adding appropriate multiples calculate nP for any n.
If nP=O, and n is the smallest positive integer with this property, we say P has order n.
Example:
  The order of P=(2,3) on ER(0,1) is 6.
  2P=(0,1), 4P= (0,-1), 6P=O.

## Slide 16: Example of Addition and Element Order
.
    .
    .
2P=(25/4,-35/8)
Note growth of denominators

## Slide 17: Proof of group laws
From the formulas and definitions, it is easy to see the operation “+” is commutative, O acts like an identity and if P= (x,y), -P= (x,-y) with P+(-P)= O.
Associativity is the only law that’s hard to verify. We could use the formulas to prove it but that’s pretty ugly.
  There is a shorter proof that uses the following result: Let C, C1, C2 be three cubic curves. Suppose C goes through eight of the nine intersection points of C1∩C2, then C also goes through the ninth intersection point.

## Slide 18: Associativity
If P and Q are points on an elliptic curve, E, let P*Q denote the third point of intersection of the line PQ and E.
Now let P, Q, R be points on an elliptic curve E. We want to prove (P+Q)+R=P+(Q+R). To get (P+Q), form P*Q and find the intersection point, between P*Q and E and the vertical line through P*Q; this latter operation is the same as finding the intersection of P*Q, O (the point at infinity) and E. To get (P+Q)+R, find (P+Q)*R and the vertical line, the other intersection point with E is (P+Q)+R. A similar calculation applies to P+(Q+R) and it suffices to show (P+Q)*R=P*(Q+R). O,P,Q,R, P*Q, P+Q, Q*R, Q+R and the intersection of the line between (P+Q), R and E lie on the two cubics:
  C1: Product of the lines [(P,Q), (R,P+Q), (Q+R, O)]
  C2: Product of the lines [(P,Q+R), (P+Q,O), (R,Q)]
The original curve E goes through eight of these points, so it must go through the ninth [ (P+Q)*R]. Thus, the intersection of the two lines lies on E and (P+Q)*R= P*(Q+R).
This proof will seem more natural if you’ve taken projective geometry. You could just slog out the algebra though.

## Slide 19: Mordell and Mazur
Mordell: Let E be the elliptic curve given by the equation and suppose that . There exist r points such that all rational points on E are of the form where .
Mazur: Let C be a non-singular rational cubic curve and C(Q) contain a point of order m, then or . In fact, the order of the group of finite order points is either cyclic or a product of a group of order 2 with a cyclic group of order less than or equal to 4.

## Slide 20: Fermat’s Last Theorem
has no non-trivial solutions in Z for n>2.
It is sufficient to prove this for n=p, where p is an odd prime.
Proof (full version will be on HW):
  Suppose .
  Wiles: is modular.
  Ribet: is too weird to be modular.
  Fermat was right.

## Slide 21: Why elliptic curves might be valuable in crypto
Consider . Let Pn=(An/Bn, Cn/Dn) be a rational point on E. Define ht(Pn)= max(|An|, |Bn|).
Define P1= (2,3), P2= (-1,4) and Pn+1= Pn + P1.
n | ht(Pn)
1 | 2
2 | 1
3 | 4
4 | 2
5 | 4
6 | 106
7 | 2228
n | ht(Pn)
8 | 76271
9 | 9776276
10 | 3497742218
20 | 8309471981636130322638066614339972215969861310
In fact, ht(Pn)≅(1.574)ns, ns=n2.
Example from Silverman, A Friendly Introduction to Number Theory.

## Slide 22: Points on elliptic curves over Fq
The number of points N on Eq(a,b) is the number of solutions of y2=x3+ax+b.
For each of q x’s there are up to 2 square roots plus O, giving a maximum of 2q+1. However, not every number in Fq has a square root. In fact, N= q+1+x(x3+ax+b), where  is the quadratic character of Fq.
Hasse’s Theorem: |N–(q+1)|2q where N is the number of points
Eq(a,b) is supersingular if N= (q+1)-t, t= 0,q, 2q, 3q or 4q.
The abelian group formed by addition in Eq(a,b) does not need to be cyclic, although it often is; it can always be decomposed into cyclic groups. In fact, if G is the Elliptic group for Eq(a,b).
Theorem: G=Zp x Z/Zpa x Z/Zqb .
Example: E71(-1,0). N= 72, G is of type (2,4,9).

## Slide 23: E71(-1, 0) – Spot the Group
There are 72 points on the curve. Can you spot (2, 4, 9). Points:
Order Point
[ 1] O
[ 2] ( 0, 0)
[ 2] ( 1, 0)
[ 9] ( 2, 19)
[ 9] ( 2, 52)
[ 18] ( 3, 38)
[ 18] ( 3, 33)
[ 9] ( 4, 42)
[ 9] ( 4, 29)
[ 18] ( 5, 7)
[ 18] ( 5, 64)
[ 6] ( 9, 62)
[ 6] ( 9, 9)
[ 36] (12, 56)
[ 36] (12, 15)
[ 4] (13, 14)
[ 4] (13, 57)
[ 18] (14, 23)
Order Point
[ 18] (14, 48)
[ 3] (19, 38)
[ 3] (19, 33)
[ 36] (21, 62)
[ 36] (21, 9)
[ 18] (23, 28)
[ 18] (23, 43)
[ 36] (27, 42)
[ 36] (27, 29)
[ 12] (32, 54)
[ 12] (32, 17)
[ 36] (33, 7)
[ 36] (33, 64)
[ 18] (35, 58)
[ 18] (35, 13)
[ 9] (37, 8)
[ 9] (37, 63)
[ 12] (40, 42)
Order Point
[ 12] (40, 29)
[ 36] (41, 62)
[ 36] (41, 9)
[ 18] (42, 8)
[ 18] (42, 63)
[ 36] (43, 21)
[ 36] (43, 50)
[ 36] (45, 49)
[ 36] (45, 22)
[ 36] (46, 37)
[ 36] (46, 34)
[ 18] (47, 51)
[ 18] (47, 20)
[ 18] (49, 38)
[ 18] (49, 33)
[ 12] (51, 16)
[ 12] (51, 55)
[ 18] (53, 47)
Order Point
[ 18] (53, 24)
[ 36] (54, 28)
[ 36] (54, 43)
[ 12] (55, 31)
[ 12] (55, 40)
[ 6] (56, 41)
[ 6] (56, 30)
[ 4] (60, 10)
[ 4] (60, 61)
[ 36] (61, 2)
[ 36] (61, 69)
[ 6] (63, 8)
[ 6] (63, 63)
[ 36] (64, 27)
[ 36] (64, 44)
[ 36] (65, 28)
[ 36] (65, 43)
[ 2] (70, 0)

## Slide 24: Addition for points P, Q in Ep(a, b)
P+O=P
If P=(x, y), then P+(x, -y)=O. The point (x, -y) is the negative of P, denoted as –P.
If P=(x1, y1) and Q=(x2, y2) with P≠Q, then P+Q=(x3, y3) is determined by the following rules:
  x3 =λ2–x1–x2 (mod p)
  y3 =λ(x1–x3)–y1 (mod p)
  λ=(y2-y1)/(x2-x1) (mod p) if P≠Q
  λ=(3(x1)2+a)/(2y1) (mod p) if P=Q
The order of P is the smallest positive number n: nP=O

## Slide 25: Point multiplication in Ep(a, b)
Note:
  932= 233+17=64 (101)
  742= 543+17=22 (101)
  412= 293+17=65 (101)
  372= 413+17=56 (101)
  882= 353+17=64 (101)
E: y2= x3+17 (mod 101) or E101(0,17)
  x3 =m2 – x1 – x2 (mod p)
  y3 =m( x1 – x3) – y1 (mod p)
  m=(y2-y1)/(x2-x1) (mod p) if P≠Q
  m=(3(x1)2+a)/(2y1) (mod p) if P=Q
(23,93)+(54,74)= (29, 41)
  m= (74-93)/(54-23) = -19/31= 82 x 88 = 45
  x3 = 452-23-54= 29 (101)
  y3 =45 x (23-29)-93)= 41
2 x (41, 37)= (35, 88)
  m= (3 x 412 + 0)/(2 x 37)= 94/74=94 x 86 =4
  x3 = 42- 82= 35
  y3 =4 x (41-35)-37= -13= 88 (101)

## Slide 26: Elliptic Curve (Characteristic = 2)
For K of characteristic 2, define j(E) = (a1)1/2/
If j(E)  0:
  -P = (x1, y1+x1)
  P+Q = (x3, y3)
  P  Q
    x3= ((y1+y2)/(x1+x2))2+(y1+y2)/(x1+x2)+x1+x2+a,
    y3 = ((y1+y2)/(x1+x2))(x1+x3) + x3 + y1
  P = Q
    x3 = x12+b/x12,
    y3 = x12+(x1+y1/x1)x3+x3
If j(E) = 0:
-P = (x1, y1+c)
P+Q = (x3, y3)
P  Q
  x3= ((y1+y2)/(x1+x2))2 +x1+x2
  y3 = ((y1+y2)/(x1+x2))(x1+x3)+c+ y1
P = Q
  x3 = (x14+a2)/ c2, P = Q
  y3 = ((x12+a)/c)(x1+x3)+c+y1

## Slide 27: Structure of the Elliptic Curve Group on Ep(a,b) - 1
E11(1, 6)[ y2= x3 + 1 x + 6 (mod 11)]. D: -7, 2 is primitive (mod 11). D=4a3+27b2 (mod p). 13 points on curve; G, cyclic.
Order Point
  [ 1] O
  [13] ( 2, 4)
  [13] ( 2, 7)
  [13] ( 3, 5)
  [13] ( 3, 6)
  [13] ( 5, 2)
  [13] ( 5, 9)
  [13] ( 7, 2)
  [13] ( 7, 9)
  [13] ( 8, 8)
  [13] ( 8, 3)
  [13] (10, 2)
  [13] (10, 9)
Powers
  ( 1) ( 5, 2)
  ( 2) (10, -9)
  ( 3) ( 7, 9)
  ( 4) ( 3, 5)
  ( 5) ( 8, 8)
  ( 6) ( 2, 4)
  ( 7) ( 2, 7)
  ( 8) ( 8, 3)
  ( 9) ( 3, 6)
  (10) ( 7, 2)
  (11) (10, 9)
  (12) ( 5, 9)
  (13) O

## Slide 28: Structure of the Elliptic Curve Group on Ep(a,b) - 2
E31(1, 6). D: -23, 3 is primitive (31). 32 points on curve. Not cyclic!
Order Point Order Point
[ 1] O
[16] ( 1, 16)
[16] ( 1, 15)
[ 8] ( 2, 27)
[ 8] ( 2, 4)
[ 4] ( 3, 25)
[ 4] ( 3, 6)
[ 2] ( 9, 0)
[16] (12, 17)
[16] (12, 14)
[ 8] (14, 25)
[ 8] (14, 6)
[16] (17, 10)
[16] (17, 21)
[16] (18, 20)
[16] (18, 11)
[16] (19, 8)
[16] (19, 23)
[ 4] (20, 20)
[ 4] (20, 11)
[16] (21, 9)
[16] (21, 22)
[16] (24, 20)
[16] (24, 11)
[16] (25, 30)
[16] (25, 1)
[ 2] (26, 0)
[ 2] (27, 0)
[ 8] (28, 10)
[ 8] (28, 21)
[ 8] (30, 29)
[ 8] (30, 2)

## Slide 29: Structure of the Elliptic Curve Group on - 3
Cyclic
E29(0, 17). D: -3, <2> (29). 30 points. G: ( 2,24).
E31(0, 17). D: -11. <3> (31). 43 points. G: ( 1, 24).
E101(0, 17). D: -12. <2> (101). 102, points. G: ( 4, 9).
E311(0, 17). D: -137. <17> (311). 312 points. G: (14, 133).
E29(1, 6). D: -14. <2> (29). 38 points. G: ( 2, 4).
E47(1, 6). D: -12. <5> (47). 52 points. G: ( 0, 10).
E101(1, 6). D: -62. <2> (101). 112 points. G: ( 0, 39).
E1217(0, 17). D: -714. <3> (1217). 1218 points. G: ( 2, 5).
Not cyclic
E31(1, 6). D: -23. <3>(31). 32 points. (1, 6) has order 16.

## Slide 30: Group order and Hasse
. Used proving endomorphisms.
Let E be an elliptic curve over K and n a positive integer. If char(K) does not divided n or is 0, then .
Twist: .

## Slide 31: Point counting
Group order calculations are critical for curve selection and algorithm safety. The number of points on the curve is the size of the group so counting points is important. There are several methods:
  Baby Step Giant Step: Explained in next slide.
  Schoof: O(lg8(p)). Beyond the scope of this lecture.
    Determines t (mod l) for l, prime and , where Pl l >4√p.
  SEA: Schoof-Elkies-Atkins. Further beyond the scope of this lecture.

## Slide 32: Elliptic Curve Discrete Log Problem
Let C be an elliptic curve, , over a finite field K with elliptic group, G. Given P, Q in the group with P=nQ, find n.
Elliptic Curve crypto system is precisely analogous to discrete log systems using arithmetic over finite fields.
  Discovered by Koblitz and Miller
Note in computing kP over we can write k as powers of 2 and multiply P by k in time. For example, .

## Slide 33: Baby step, giant step
Want to find m: O= [m]P. There is a general attack just like in DLP called the Baby Step – Giant Step Attack. It takes O(√n) where n is the order of the group.
The attack:
    M=ceiling(√n). m=aM+b is the order of P.
    To find a, b note (O-[b]P)=[a][M]P.
    Compute Rb= O-[b]P, b=1,2,…,M. Store (b, O-[b]P) sorted by second element.
    Giant step: Sa= [a][M]P, a= 1,2,…,M check table if
    Sa=Rb, m=aM+b.

## Slide 34: Special Attacks on discrete log in
MOV Attack (Menezes, Okamoto, Vanstone).
  Idea: map the ECDLP to the DLP in an extension field.
In the case of MOV, if n is the order of a point (hence it divides the number of points on the curve) and n|qk-1, the ECDLP can be mapped into the DLP in GF(qk).
  To avoid this attack, we need to make sure the DLP in GF(ql) is as hard as the ECDLP in Eq(a,b). This is guaranteed to happen of l>k2/(lg(k)2), so we can avoid this attack if the smallest l: ql=1 (mod n) satisfies l>k2/(lg(k)2).
Another attack: An anomalous curve satisfies #Eq(a,b)=q. This group is cyclic and allows an easy embedding in the DLP problem in the additive group of Fq. To avoid this, make sure the number of points on the elliptic curve is not q.

## Slide 35: Diffie Hellman over ECC
Alice and Bob chose a finite field Fq and an elliptic curve E
The key will be taken from a random point P over the elliptic curve (e.g. - the x coordinate).
Alice and Bob choose a point B that does not need to be secret
  B must have a very large order
Alice chooses a random a and compute aBE
Bob chooses a random b and compute bBE
Alice and Bob exchange the computed values
Alice, from bB and a can compute P= abB
Bob, from aB and b can compute P= abB

## Slide 36: Elliptic curve El Gamal
There are several ways in which the ECDLP can be embedded in a cipher system.
  One method begins by selecting an Elliptic Curve, Ep(a,b), a point G on the curve and a secret number k which will be the private key.
  The public key is andwhere Think of G as the generator in the discrete log problem.
  A message is encrypted by converting the plaintext into a number m, selecting a random number r, and finding a point on the curve corresponding to m. We explain how to do this in the next slide.
  The ciphertext consists of two points on the curve
  To decipher, multiply the first point by k and subtract the result from the second point:.

## Slide 37: Embedding m in Eq(a,b)
There is no deterministic way.
Assume q= pr and we want to embed with a probability of failure not to exceed 2-k.
Message is m and 0m<M. q>M𝜅.
For ar-1pr-1+…+a1p+a0=xa= m𝜅+j.
For j= 0, try to solve y2=xa3+axa+b by evaluating Legendre symbol. Can do this with probability ½. If this succeeds, use it. Otherwise try j=1 ,…
Given xa, we can recover m by writing and discarding j.

## Slide 38: Putting it all together: EC El Gamal
Curve:
Bob sends Alice:
Alice decrypts as:

## Slide 39: Putting it all together: ECDH
Curve:
Alice picks a=12 sends
Bob picks b= 23, sends
Bob computes
Alice computes

## Slide 40: Picking Curves
Curves are selected at random subject to resistance to known attacks like Hellman-Pohlig-Silver and Pollard rho.
    #E(Fq) should be divisible by a large prime, n.
    #E(Fq) should not be q
    n should not divide qk-1
Method of selecting curves
  Select a,b at random with
  Calculate N= #E(Fq).
  Factor N and verify 1, 2, 3 above.
  If the coefficients are selected at random, the order of the curves are uniformly distributed (Lenstra).

## Slide 41: Curve selection
Given p and a parameter S, generate an acceptable E.
  Generate random a,b𝝴Fp.
  If 𝛥=0 go to 1.
  Determine N= #Ep(a,b)
  If Ep(a,b) is anomolous (p=N), go to 1.
  If Ep(a,b) is subject to MOV attack, there is an l<lg(p)2/(lg(lg(p))2: pl=1 (mod N), go to 1.
  Factor N, if it takes too long, go to 1.
  If N=sxr, s≦S return Ep(a,b)
  Go to 1.

## Slide 42: ECC Point Operation Costs and modular operations
Parameters
I= inverse cost in GF(p).
S= square cost GF(p).
M= multiply cost GF(p)
Op | Cost | Modular Op | Cost
2P | I+2S+2M | Add, Sub | O(lg(n))
P+Q | I + S+ 2M | Multiply | O(lg(n)2)
2P+Q | 2I + 2S + 2M | Invert | O(lg(n)2)
P+Q, P-Q | I+2S+4M | Exp | O(lg(n)3)

## Slide 43: ECC vs RSA performance analysis
(for EC), N= [lg(p)] for DLP.
The cost to break DLP with best known algorithm (IC) is
The cost to break ECDLP with best known algorithm (IC) is .
The number of key bits (for equivalent security) in the DLP case grows as the cube of the number of bits for the ECDLP case. This has a key size and performance implication.

## Slide 44: Pollard Rho Method for ECC vs. Factoring by Number Field Sieve
Key size MIPS-Years
150 bits 3.8x1010
205 bits 7.1x1018
234 bits 1.6x1028
Elliptic Curve Logarithms Using Pollard Rho Method
Key size MIPS-Years
512 bits 3x104
768 bits 2x108
1024 bits 3x1011
1280 bits 3x1014
1536 bits 3x1016
2048 bits 3x1020
Integer Factoring Using Number Field Sieve
This slide came from someone else

## Slide 45: Observations on ECC
Asymmetry between encryption and decryption is reduced (4:1)
NIST recommendations for key size to provide “equivalent” security (bits in key).
ECC | RSA | AES
163 | 1024 | 
256 | 3072 | 128
384 | 7680 | 192
521 | 15360 | 256

## Slide 46: NIST Curves
Use prime fields with or binary fields with q= 2163, 2233, 2283, 2409, 2571.
and t is called the trace of E. has rank 1 or 2, that is: Eq(a,b) ~ Zn[1]xZn[2] and n[2] | n[1], n[2] | (q-1).
If n[2] =1, Eq(a,b) ~ Zn1= {kP: 0<k<n[1]} and P is a generator.
if and .
is supersingular if p|t. Field represented as polynomial or normal basis.

## Slide 47: El Gamal Signature
Bob has a private key x and a public key in a group G. To sign m, given a map f: G  Z|G|:
  Bob generates a random .
  Bob computes .
  SigBob(m)= (A,B)
To verify check that the signature is right, verify that .

## Slide 48: EC El Gamal Signature
Bob has a private key x and a public key in a group G. To sign m, given a map f: G  Z|G|:
  Bob generates a random .
  Bob computes .
  SigBob(m)= (A,B)
To verify check that the signature is right, verify that .

## Slide 49: Factoring using Elliptic Curves
Let be an elliptic curve with and let be two rational points whose denominators are prime to n. Then has denominators prime to n iff there is no prime such that .
Lenstra’s Algorithm. Choose 2 bounds B, K.
    (n,6)=1, nmr
    Choose random b, x1, y1 between 1 and n
    k= LCM(1,2,…,K)
    Compute , if at any point can’t succeed, n is composite.
    . If D=1, go to 5 and bump K or go to 2 and select new curve.

## Slide 50: Factoring using elliptic curves - example
Factor n=4453.
Use E: y2 = x3+10x-2 (mod m).
Initial point: P1= (1,3).
2P=(4332, 3230).
To calculate 3P:
  m=(3230-3)/(4332-1)=3227/4331.
(4331, 4453)=61.
4453= 61x73.

## Slide 51: Factoring using elliptic curves - example
Factor m=1938796243.
Use
Initial point: P1= (1,1), Pn+1= (n+1)Pn.
For A=7, (w16, m)= 37409. m= 37409 x 51827.
,

## Slide 52: Divisors
D= ∑j aj[Pj], aj 𝝴 Z
deg(D)= ∑j aj
sum(D)= ∑j ajPj
sum: Div0(E)  E(K).
f= uPr g: ordP(f)=r, div(f)= SP𝝴E(K) ordP(f) [P]
Div0(E)/(principal divisors) is isomorphic to E(K)
Let E be an elliptic curve and f a function on E that is ≠0 then
  f has only finitely many poles and zeros
  deg(div(f))=0
  If f has no poles or zeros it is constant

## Slide 53: Pairings
E[n]⊆E(K), en: E[n] x E[n]  𝜇n
T𝝴E[n], f: div(f)= n[T]-n[∞]
Choose T’𝝴E[n2]: nT’=T: div(g)= SR𝝴E[n]([T’+R]-[R])
div(f°n)=div(gn)
Let S𝝴E[n], P𝝴E(K) then g(P+S)n= f(n(P+S))=f(nP)=g(P)n
  Thus g(P+S)/g(P) 𝝴 𝜇n and is independent of P.
Define en(S,T)= g(P+S)/g(P), then
  en: E[n] x E[n]  𝜇n
  en is binlinear, non-degenerate.
  en(𝜎S, 𝜎T)= 𝜎en(S,T)
  en(𝛼S, 𝛼T)= en(S,T)deg(𝛼) if a is separable.

## Slide 54: Lattices
The set where are linearly independent is called a lattice.
, where are the generators of . Note that any set of generators will do since they are related by uni-modular transformations.
Let be a lattice
  The CVP problem is: Find
  The problem is: Find )

## Slide 55: Definitions
Hermite Normal Form (HNF)

## Slide 56: Minkowski’s Theorem
Let be a lattice in and suppose is a convex, centrally symmetric region. If ) then S has a non-zero lattice point of .
  Suppose first that is the simple lattice generated by . Represent a point as with and , for . Define . If , . So, if has the property that , then . Note that . So, if , there are at least two points where for some . Since is centrally symmetric, finally, note that . Similarly, if , there are at least points with for at least two, say and all corresponding coordinates in and are equal Thus, . But since is convex, So, the result holds for the simple lattice. Suppose now that is genetated by and put . so and the simple lattice result thus implies the general theorem.

## Slide 57: q-ary lattices and other definitions
Definition: If , a lattice, , is called -ary if .
Suppose , . Note is -ary.
|
, where is a set of linearly independent vectors,
Solving CVP in when is chosen uniformly at random is as hard as worse case CVP.

## Slide 58: Some simple results
Remember is centrally symmetric if implies , and is convex if implies . We used this in proving Minkowski’s Theorem.
Theorem:
  Let be a ball centered at having radius . Let be the coordinates of a vector , with respect to the basis generating the lattice , if for , . So and as well as the line joining them are in so and the result follows from Minkowski’s theorem.

## Slide 59: Reduced Basis
<v1, v2> is reduced if
  ||v2||≦|v1||; and,
  -1/2||v1||2 ≦(v1, v2) ≦ 1/2||v1||2 .
v1
v2
Reduced
v1
v2
Not

## Slide 60: Good basis and Gram-Schmidt Orthogonalization
Good basis for lattices are orthonormal when that is possible. If a basis, for , is orthonormal, then, for example, ) =
The orthogonality defect of a basis is
Given a space generated by can also be generated by a set of vectors ,…, with the property that . Th Gram-Schmidt orthogonalization procedure computes this.
  GSO, given, , compute ,…,
    put .
    for

## Slide 61: Size Reduction
Definition: A basis is size reduced if , in the Gram-Schmidt orthogonalization procedure.
If is a basis for in general, ,…, is not also a lattice basis because is generally not an integer. We can find a “nearly” orthogonal set of vectors in by rounding the is also a basis for the lattice and has the same gram Schmidt basis, ,…, When performing GSO on this reduced basis, .
Size-reduction
  for ,
    for ,
      for

## Slide 62: Size reduction and basis reordering
Let be a basis for and ,…, the resulting GSO basis. Let . Then satisfies the Lovasz condition with factor if it is size reduced and . The LLL algorithm calculates such a basis.
LLL Algorithm
  Given generating calculate the LLL reduced basis
  Reduce the basis with the size reduction algorithm and calculate ,…, and
  Compute ,
  for
    If (
      Swap and
      Go to 1
  return

## Slide 63: Example (LLL including GSO)
LLL ()
, , .
  GSO: , ,, , .
  Size reduction: last change is
  Now, , , .
  , , . Lovasz condition is not satisfied for : since . So swap and .
  Applying GSO we get and
  Size reduction produces: and . and don’t change.
From Heiko Knopse

## Slide 64: Example (LLL including GSO) - continued
Now Lovasz condition is satisfied for since . but not since . swap and
  Now, , , . , , . GSO coefficients are and. Applying size reduction does not affect or . , . Both Lovasz conditions now hold.
  LLL basis is thus , , . Notice is actually the shortest vector in .
From Heiko Knopse

## Slide 65: LLLProperties
Suppose we apply LLL to a lattice basis for and defined as above, we have:
    If and <1, LLL runs in time
    If
    )
If is a vector in and the lattice basis for is with the coefficients for are . is not necessarily in the lattice but if we take each element in and round it, . This is Babai rounding.

## Slide 66: Attack on RSA using LLL
Attack applies to messages of the form "M xxx" where only "xxx" varies (e.g.- "The key is xxx") and xxx is small.
From now on, assume M(x)=B+x where B is fixed
  |x|<Y.
  Not that
  f(x)= (B+x)3-c= x3+a2x2+a1x+a0 (mod n).
We want to find , a solution to this, m, will be the corresponding plaintext.

## Slide 67: Attack on RSA using LLL
To apply LLL, let:
  v1= (n, 0, 0, 0),
  v2= (0, Yn, 0, 0),
  v3= (0, 0, Y2n, 0),
  v4= (a0 , a1Y, a2Y2, a3Y3)
When we apply LLL, we get a vector, b1:
  ||b1|| ≦ 2(3/4) |det(v1, v2, v3, v4)| = 2(3/4) n(3/4) Y(3/2) …. Equation 1.
Let b1= c1v1 + …+ c4v4= (e0, Ye1, Y2e2, Y3e3). Then:
  e0 = c1n+c4a0
  e1 = c2n+c4a1
  e2= c3n+c4a2
  e3 = c4

## Slide 68: Attack on RSA using LLL
Now set g(x)= e3x3+e2x2+e1x+e0.
From the definition of the ei, c4 f(x)= g(x) (mod n), so if m is a solution of f(x) (mod n), g(m)= c4 f(m)= 0 (mod n).
The trick is to regard g as being defined over the real numbers, then the solution can be calculated using an iterative solver.
If Y<2(7/6)n(1/6), |g(x)| ≦ 2||b1||.
So, using the Cauchy-Schwartz inequality, ||b1||≦2-1n.
Thus |g(x)|<n and g(x)=0 yielding 3 candidates for x.
Coppersmith extended this to small solutions of polynomials of degree d using a d+1 dimensional lattice by examining the monic polynomial f(T)= 0 (mod n) of degree d when |x|≦n1/d.

## Slide 69: Example attack on RSA using LLL
p= 757285757575769, q= 2545724696579693.
n= 1927841055428697487157594258917.
B= 200805000114192305180009190000.
.
  a2= 602415000342576915540027570000
  a1= 1123549124004247469362171467964
  a0= 587324114445679876954457927616
  v1= (n,0,0,0)
  v2= (0,100n,0,0)
  v3= (0,0,104n,0)
  v4= (a0, a1100, a2104,106)

## Slide 70: Example attack on RSA using LLL
Apply LLL, b1=
  308331465484476402v1 + 589837092377839611v2 +
  316253828707108264v3 + (-1012071602751202635)v4 =
  (246073430665887186108474, -577816087453534232385300,
    405848565585194400880000, -1012071602751202635000000)
g(x)= (-1012071602751202635) t3 + 40584856558519440088 t2 +
  (-57781608745353442323853) t +246073430665887186108474.
Roots of g(x) are 42.0000000, (-.9496±76.0796i)
The answer is 42.

## Slide 71: GGH Public Key System
Pick and is “small”, say
Plaintext:
Cipherspace:
Lattice based but not used.
Gen:
  Choose with small entries
  Check is invertible. is the secret key.
Enc
  For , choose uniformly at random
Dec
  Babai round

## Slide 72: GGH Example
, H,
,
,
From Heiko Knopse

## Slide 73: LWE
Based on solving noisy linear equations . Choose uniformly at random. is a secret and approximate equations Errors, are chosen from distribution . Reduces to LWE. Chris Peikert et. al.
Search LWE problem: Given the above, find .
Decision LWE: Distinguish with non-negligible probability, between + and chosen uniformly at random given
Regev’s results show it is possible to pick parameters so that solving the cipher is equivalent to solving worst-case LWE

## Slide 74: LWE cryptosystem
Given where is a probability distribution message space is and cipher space is .
Key Gen
  Choose , uniformly from the distribution .
  Choose , and uniformly from the distribution
  Private key is , public key is
Enc
  For choose , uniformly at random
  ))
Dec
  Compute
Decryption may have errors. Suppose is a discrete Gaussian Then has magnitude with high probability. Error occurs if . One can show that for any , such that the error is small and the underlying LWE problem is hard.

## Slide 75: LWE example
,
,
From Heiko Knopse

## Slide 76: LWE example
, ,
From Heiko Knopse

## Slide 77: LWE example
Encrypt , using
Decrypt:
  ,
From Heiko Knopse

## Slide 78: LWE example
Encrypt , using
Decrypt:
  ,
From Heiko Knopse

## Slide 79: LWE/Ring-LWE parameters
Ring-LWE cuts ciphertext by factor of n
Level | n | q | s | P | P&A | c | Exp
Low | 128 | 4093 | 8.87 |  |  |  | 30
High | 320 | 4093 | 8 |  |  |  | 42
Level | n | q | s | P | P&A | c | Exp
Low | 128 | 4093 | 8.87 |  |  |  | 30
High | 320 | 4093 | 8 |  |  |  | 42

## Slide 80: Ring-LWE
Put , . , generates ideal corresponding to a -ary ideal lattice.
Ring LWE: Given , and , for find .
Solving R-LWE is at least as hard as solving on arbitrary ideal lattices

## Slide 81: NTRU Public Key System
NTRU is a ring lattice-based system.
, ,
, where
is the set of “ternary” polynomials of degree , having coefficients equal to , having coefficients equal to , and remaining coefficients equal to
Pick prime and , , .

## Slide 82: NTRU Public Key System
KeyGen
  Pick .
  Find .
  Public key is private key is .
Plaintext is , ciphertext is
Encryption
  Chose random .
Decryption
  Compute
  Plaintext is .
  Verify that .

## Slide 83: NTRU Example
We check in
From Heiko Knopse

## Slide 84: Some NIST Round 3 entries
Public-Key Encryption/KEMs
  Classic McEliece
  CRYSTALS-KYBER
  NTRU
  SABER
Digital Signatures
  CRYSTALS-DILITHIUM
  FALCON
  Rainbow
Public-Key Encryption/KEMs (Alternates)
  BIKE;
  FrodoKEM
  HQC
  NTRU Prime
  SIKE
Digital Signatures
  GeMSS
  Picnic
  SPHINCS+
Winner: Dilithium (signing), Kyber (key-encapsulation)

## Slide 85
Some common features of Dilithium and Kyber
Ring is in both cases
  for Kyber
  for Dilithium
  So, the same modular arithmetic we all grew up with.
For , there is a primitive (and hence 128 primitive) 256th roots of unity (You are not expected to understand this).
    As a result, factors into coprime 128 quadratics
    Allows us to perform a “Number Theory Transform” that turns convolution into pointwise multiplication for ring operations giving a nice speedup
For , there is a primitive (and hence 256 primitive) 512th roots of unity
  As a result, factors into coprime 256 linear polys
    Allows us to perform a “Number Theory Transform” that turns convolution into pointwise multiplication for ring operations giving a nice speedup

## Slide 86
Useful definitions
,
means and , if is even; , if is odd
  if
    ,
  else
  return

## Slide 87
Useful definitions
  return
  return
  return

## Slide 88
Examples
examples (second shows roundoff edge case)
17 | 8 | 5 | -3 | 8 | -3 | 1
17 | 8 | 15 | -1 | 16 | -2 | 0
3329 | 104 | 50 | 50 | 0 | 50 | 0
3329 | 104 | 100 | -4 | 104 | -4 | 1
17 | 8 | 5 | -3 | 8 | -3 | 1
17 | 8 | 15 | -1 | 16 | -2 | 0
3329 | 104 | 50 | 50 | 0 | 50 | 0
3329 | 104 | 100 | -4 | 104 | -4 | 1

## Slide 89
SHAKE-256/SHAKE-128
Note

## Slide 90
For has primitive root of unity ( and no root of unity, so factors into coprime quadratic factors of the form , .
In fact, . simply reverses the bit order in a 7-bit byte, .
For , is a primitive 512th root of unity
Because of this, an analog of the Chinese remainder theorem holds in .
Number Theory Transform (NTT)

## Slide 91
Dilithium (simplified)
Remember is generated randomly from .
is a vector of dimension with entries from has random coefficients
Sign
  return()
Verify
  Check AND

## Slide 92
Dilithium (less simplified)
Parameters:
KeyGen
  , selected from random distribution over
  , selected at random, consists of elements of with coefficients
  Set
  Public key is , Private key is
  For the sake of compression is generated from a seed and SHAKE-256

## Slide 93
Dilithium
Sign(pk, sk, M) --- simplified
  while (
  if () OR then
  }
  Signature is
Real Dilithium uses a number of functions to generate A from a seed. It also has a hedged version and a deterministic version. The hedged version avoids some possible side channels.

## Slide 94
Dilithium
Verify(pk, M,z, c) --- simplified
  Return true if AND , otherwise return false

## Slide 95
Useful definitions
// Calculate c(x), coefficients are 1, -1 or 0
  ; k=8;
      k++
  return c

## Slide 96
Useful definitions
u
  If and then return
  If and then return
  return
  return

## Slide 97
Useful definitions
// returns NTT polynomial
  ;
  while ()
    If () then
  return
  ;
  while ()
    If ()
        ;
    If ( and )
        ;
  return

## Slide 98
Useful definitions
  (r=0; r<l; r++)
    ,…, )
  return s

## Slide 99
NTT for Dilithium
--- outputs
      while (
        for(

## Slide 100
NTT for Dilithium
    while (
      for(

## Slide 101
Dilithium, unedited, motivation
Basic scheme is Fiat-Shamir MSA-DL with aborts.
Classic version with discrete log is:
  Prover and verifier know Prover knows .
  Prover generates , sends commitment .
  Verifier sends
  Prover returns .
  Verifier can check
Non interactive version replaces with hash of

## Slide 102
Dilithium, unedited, motivation
Preliminary lattice version is
  Prover generates: with short coefficients and computes . Public key is . Private key is
  Prover generates with “small coefficients”. Sends commitment as
  Verifiers sends challenge with small coefficients
  Prover returns .
  Verifier checks coefficients of are small and that
To avoid having leak , signer applies rejection sampling to .
Dilithium
  Uses elements of rather than
  Uses a seed, to generate
  Compresses t by dropping low order bits
  Signs a message representative, , which is a hash of the public key and the message
  Uses a rounded version of , .
  Provides a hint, , to help reconstruct from

## Slide 103
Dilithium parameters for security category 5
Parameter | Meaning | Value
 | modulus | 8380417
 | # dropped bits from t | 13
 | # s in | 60
 | Collision strength | 256
 | Coefficient range of | 
 | Low order rounding range | 
 | Dimensions of | 
 | Private key range | 2
 |  | 120
 | Max # of 1’s in hint | 75
Parameter | Meaning | Value
 | modulus | 8380417
 | # dropped bits from t | 13
 |  | 60
 | Collision strength | 256
 | Low order rounding range | 
 | Private key range | 2
 |  | 120
 | Max # of 1’s in hint | 75
ML-DSA-87 | Private | Public | Sig
Size (Bytes) | 4864 | 2592 | 4595

## Slide 104
Dilithium, Keygen
Keygen
  (random)
  , (256, 512, 256) bits respectively
  return

## Slide 105
Dilithium, Sign
Sign
  , ,
  while(1) {
    ,
    first 256 and last bits
    ;
    ; ;
    )
    If ( or then continue
    ;
    If and # 1’s in then break
  }

## Slide 106
Dilithium, Verify
Verify
  first 256 and last bits
  )
  return and and # 1’s in

## Slide 107
Useful Kyber definitions
and are different for Kyber and Dilithium
Kyber is based on the Fujisak-Okamoto transform

## Slide 108
Useful definitions
--- samples from distribution
    ;
    return
For central binomial distribution with , , is CDF for normal distribution
--- samples uniformly from
    If (
      ;
    If ( and
      ;
  return

## Slide 109
Useful definitions
,

## Slide 110
NTT for Kyber
  ;
  for()
    for()
    ;
    for()
  return()

## Slide 111
NTT for Kyber
  ;
  for()
    for()
    ;
    for()
  return()

## Slide 112
Useful definitions
, is an array of length 256, ,
    for (i = 0; i < 256; i++)
      ]
      for (j=0; j < d; j++)
  return bits-to-bytes(b)
, is a byte array of length ,
  for (i=0; i < 256; i++)
  return

## Slide 113
Parameters: ,
Make public key
  , generate a Dilithium-like key (see full version)
  , is generated from seed
[ is generated from , is generated from ]
  ,
  ,
  return
  return
Kyber (simplified a little)

## Slide 114
Kyber simplified a little
  (random)
  ()
  ;
  return )
  is a random 32-byte value
  return
  If () return K else error (Note: failure rate is for ML-KEM-1024)

## Slide 115
Kyber parameters
ML-KEM-1024 is security category 5
Alg |  |  |  |  |  |  |  | Strength
KEM-512 | 256 | 3329 | 2 | 3 | 2 | 10 | 768 | 128
KEM-768 | 256 | 3329 | 3 | 2 | 2 | 10 | 1088 | 192
KEM-1024 | 256 | 3329 | 4 | 2 | 2 | 11 | 1568 | 256
Alg |  |  |  |  |  |  |  | Strength
KEM-512 | 256 | 3329 | 2 | 3 | 2 | 10 | 768 | 128
KEM-768 | 256 | 3329 | 3 | 2 | 2 | 10 | 1088 | 192
KEM-1024 | 256 | 3329 | 4 | 2 | 2 | 11 | 1568 | 256
Type | Encap-key | Decap-key | Ciphertext | Key
KEM-512 | 800 | 1632 | 768 | 32
KEM-768 | 1184 | 2400 | 1088 | 32
KEM-1024 | 1568 | 3168 | 1568 | 32
Size in bytes

## Slide 116
Full Kyber
  , random
  ;
  ;
  ;
  return

## Slide 117
  ;
  ,
  ,
  return
Full Kyber

## Slide 118
  ;
  return
Full Kyber

## Slide 119
  , is generated from seed
  return
Full Kyber

## Slide 120
Full Kyber
  is a random 32-byte value
  return

## Slide 121
Full Kyber
  :
  If () return K else error

## Slide 122: End

## Slide 123: Endomorphisms
Endomorphisms are homomorphisms from E(K)  E(K) that can be represented by rational functions.
  If .
  The endomorphism, a, is separable, if .
    If a is separable deg(a)= #ker(a).
    If a is not separable deg(a)> #ker(a).
If fp is the Frobenius map, it is an endomorphism of degree p and fp is not separable.
  . fp-1 is a separable endomorphism.
  Let E be an elliptic curve over . .

## Slide 124: Shanks and Menstre
Input: Eq(a,b), #Eq(a,b)=q+1-t, |t|≦4<q.
Output: Bound on t. O(q1/4+e).
    Pick random point P on Eq(a,b), |P|>4<q.
    Q=[q+1]P
    Q1= Q+ floor[2q]P
    t’= t+ floor[2q], note 0≦t’ ≦4q
    m= ceiling(2q1/4)
    Baby step: [j]P
    Giant step: Q1-[i][m]P
    t’= im+j, i,j<m. This bounds #Eq(a,b).
Menstre: either a curve or its twist has a point with order >4q

## Slide 125: Endomorphisms continued
Endomorphism are maps that preserve the “addition” operation between an elliptic curve group and itself. That We care about endomorphisms that preserve O: j (O)= O. These are called isogonies.
There are two very important endomophisms:
  Frobenius:
  Point multiplication:
For EK(a,b), define (For singular curves 𝛥=0) and define the j-invariant Ep(a,b), .

## Slide 126: Isomorphic Curves and the j-invariant
Let K be a field and K* its algebraic closure. and are isomorphic if r,s,t 𝝴 K, u 𝝴 K*: the transformations (x,y)  (x’,y’) given by , take EK(a,b) to EK(a’,b’).
Recall . (For singular curves 𝛥=0) and define the j-invariant Ep(a,b), j(E)= 1728/𝛥.
Theorem: Let E1=EK(a,b) and E2=EK(a’,b’) be two ellliptic curves.
  If E1 and E2 are isomorphic, they have the same j-invariant.
  If j(E1)=j(E2), there is a m: a2= 𝜇4a1, b2= 𝜇6b1.
  If two curves have the same j-invariant, they are isomorphic over the algebraic closure, K*.

## Slide 127: The Division Polynomials
[m] (x,y)= (qm(x,y)/ym(x,y)2, wm(x,y)/y(x,y)3)
We can calculate these polynomials recursively:
  y0(x,y)= 0; y1(x,y)= 0.
  then y2m+1(x,y)= ym+2(x,y)ym3+ym-1(x,y)ym+13.
  fm=xym2-ym+1ym-1
  wm= 1/(4y)(ym+2ym-12–ym-2ym+12)
Let E be an elliptic curve, the endomorphism of E given by multiplication by n has degree n2.
(x,y)=P 𝝴 E[m] is the subgroup of torsion points whose order divides m: [m]P=0.

## Slide 128: Preliminary DSA
Bob has a private key x and a public key <g,X>: X= gx in a group G. To sign m, given a map f: G  Z|G|:
  Bob generates a random a: 1≦a<|G|. A= ga.
  Bob computes B𝝴Z|G|: m= -xf(A)+Ba (mod |G|).
  SigBob(m)= (A,B)
To verify compute u= mB-1 (mod |G|), v=f(A)B-1 (mod |G|) and w=guXv. Verify that w=A.

## Slide 129: ECDSA
D=(q, a,b,P,n,h). nh= #Eq(a,b). Private key d, message m.
Signature (r,s)
  Select k𝝴[1,n-1]
  Compute kP=(x1, y1). Convert x1 to integer x1.
  Compute r= x1 (mod n). If r=0 goto 1.
  Compute e=H(m).
  s= k-1(e+dr) (mod n). If s=0, goto 1.
Verify
  Check r,s [1,n-1]. Compute e=H(m).
  Compute w= s-1 (mod n). u1= ew (mod n). u2= rw (mod n).
  Compute X= u1 P+ u2 Q. If X= O, reject.
  Convert x1 of X to integer x1. Compute v= x1 (mod n).
  If (v=r) accept signature.

## Slide 130: ECIES
Input D=(q, a, b, P, n, h), public key Q, plaintext m.
ENC, MAC, DEC are standard “symmetric key” functions. KDF is key derivation function (also standard).
    Pick k𝝴[1, n-1].
    Compute R= kP, Z=hkQ. If Z=O, go to 1.
    (k[1], k[2]) = KDF(xZ, R).
    c= ENCk1(m), t= MACk[2](c).
    return (R, c, t)

## Slide 131: LLL Theorem
Let L be the n-dimensional lattice generated by <v1, …, vn> and l the length of the shortest vector in L. The LLL algorithm produces a reduced basis <b1, …, bn> of L.
    ||b1|| ≦ 2(n-1)/4D1/n.
    ||b1|| ≦ 2(n-1)/2l.
    ||b1|| ||b2|| … ||bn|| ≦ 2n(n-1)/4D.
If ||bi||2≤C algorithm takes O(n4 lg(C)) .

## Slide 132: Gauss again
Let <v1, v2> be a basis for a two-dimensional lattice L in R2. The following algorithm produces a reduced basis.
  for(;;) {
    if(||v1||>||v2||)
      swap v1 and v2;
    t= [(v1, v2)/(v1, v1)]; // [] is the “closest integer” function
    if(t==0)
      return;
    v2 = v2-tv1;
    }
<v1, v2> is now a reduced basis and v1 is a shortest vector in the lattice.

## Slide 133
Useful definitions

## Slide 134
Useful definitions
makehint
MultiplyNTT
BaseCaseMultiply