## Slide 1: Internet of Things: Electronics
John L. Manferdelli
johnmanferdelli@hotmail.com
Nov 16, 2020, 18:00

## Slide 2: Guide
This is a rather condensed introduction to electronics mainly to give a sense of scope and establish terminology. There’s more in my “Electronics of Radio” notes.
A full treatment of this material could be a full time and rewarding hobby; in fact, many people have this hobby, see, for example, http://www.arrl.org.
You should consult some standard works like the Radio Amateurs Handbook and Make Electronics by Charles Platt as well as the SparkFun Tutorials which are online.
A basic background in physics would help a lot. See, for example:
  Feynman’s Lectures on physics.
  Berkeley physics course volumes 1, 2, 3.
  Any standard two-year physics course textbook (e.g.- Sears, Zemansky and Young).
  Schaum’s outline in Physics for Engineering and Science.
  Griffiths, Introduction to Electrodynamics.
  Scherz, Practical Electronics for Inventors. This book bridges theory and practice and is a bargain.

## Slide 3: Electronics part 1, charge, current potential and circuits
Charge and forces on charged particles are the basis for electronics. There are four things we can measure related to this. You should be able to define them and say how to measure them.
  Electric field (E)
  Magnetic field (B)
  Current (I)
  Voltage (V)
How do you process electrical signals to produce useful output?
  Currents and potentials are affected by “lumped components” like resistors, capacitors and transistors. You should know what they are and model their effect.
  Circuits: Lumped components can be connected to implement complex relationships between input currents and potentials and output currents and potentials. You should be able to draw circuit diagrams (showing how the components are connected) and analyze the circuit.
  Analyzing circuits: You should know what phasors are and model complex circuits using Thevenin and Norton equivalent circuits.
Power
  You should be able to define and calculate electrical power in a circuit.

## Slide 4: Current and potential
A principled understanding of electronics requires an understanding of Maxwell’s equations but that is not easy. We’ll get into Maxwell’s equations later, but it will likely not mean anything unless you have the right background. I’ll start out here in the middle of the story with an “artzy-craftzy” description of charge and potential but let me say, if you’re willing to start in the middle, you’re a better person than I am.
First, you need to accept the concept of an electric field, E(r,t). Bold means a vector in three space. Electric fields are created by charged particles. Charged particles come in two flavors, -, like an electron and +, like a proton. Charged particles experience a force when placed in an electric field. This force is proportional to their charge, namely F(r,t) = q E(r,t), where q is the charge. Accelerating charges, produce special electric fields that radiate. Electric fields have companion fields called magnetic fields. Magnetic fields are produced by moving charges. Moving charged particles also experience a force when placed in a magnetic field. In fact, the full force law is
  F(r,t) = q (E(r,t) + v × B(r,t)), where × is the vector cross product.
Charge is measured in Coulombs (C). One coulomb has the same (negative) charge as 6.24 × 1018 electrons.

## Slide 5: Current and potential (continued)
Current is the measure of charge flow through a a surface per unit time. One amp of current through a surface means one coulomb flows through the surface per second.
Electric potential (V) represents the work done per unit charge when a particle accelerates in an electric field. It corresponds to the gravitation potential for the work done accelerating a particle with mass in a gravitational field except that voltage, like charge, can be positive or negative. The unit of potential is a volt. One volt is 1 kg-m2/amp-sec3.
You can measure current or voltage with a volt-ohm meter.
The potential between two points is not, in general, a constant and can vary with time. A simple potential source is an ideal battery which does have constant potential between its two “terminals.”
One basic law in electronics is ohm’s law which says
  , or more generally, where R stands for resistance and Z stands for impedance.
The power consumed by a current, I travelling between a potential difference of V is .
Until we talk about radiation (radios), most electronic ideas can be phrased in terms of I, V and Z.

## Slide 6: Circuit diagrams and lumped circuits
At low frequencies, circuits can be analyzed as “lumped devices” with terminals wired together.
The components (resistors, transistors, … ) correspond to the nodes of a graph and the wires correspond to edges.
There are potential differences between any two points and current flowing through edges. Each component has a recognizable symbol (see later) ; when drawn this way, we call the graph-like representation a circuit diagram.
Here is an example:
Common emitter amp
RC
R1
Ci
CE
R2
RE
vs
VCC
vs
Cout

## Slide 7: Circuit symbols
PNP
NPN
Photo transistor
Switches
SPST
SPDT
DPST
Symbols from http://www.eehomepage.com/symbols.ppt. Copyright 2008 by EE HomePage.com. These symbols may be freely reused.
PNP BJT
NPN BJT
Microphone
Speaker
Resistor
Op amp
Inductor
Capacitor
Transformer
Diode
Battery
Voltage source
Ground symbols

## Slide 8: Capacitors
Symbol Electrolytic capacitor +
Unit: farads. Usually capacitor values vary from microfarads (𝝁F) to nano-farads (nF) to picofarads (pF). 1 𝝁F= 10-6 F, 1 nF = 10-9 F, 1 pF=10-12 F.
Law connecting charge (on a plate) and potential between plates: q = CV.
The “impedance” version of this is
Stored energy in a capacitor:

## Slide 9: Resistors
R
Symbol
fixed variable
Unit: ohms (𝝮). Usually resistor values vary from ohms to kilo-ohms (103 𝝮) to megaohms (106 𝝮).
The resistor value (in ohms) is indicated by colored bands around the resistor.
The inverse of resistance is conductance, .
Dissipated energy:
Credit: Make Electronics

## Slide 10: Inductors
Symbol
Unit: henries. Usually inductor values vary from microhenries to millihenries.
Stored energy:
Wikipedia

## Slide 11: Transformers
Symbol
AC only: =
Electronics hub

## Slide 12: Impedance
Impedance captures both pure resistance and complex “reactance” effects like capacitance and inductance.
ZR = R. ZC = -i/(𝜔C), ZL = -i𝜔L
Here, 𝜔, is the angular frequency of the signal and 𝜔 = 2𝜋f
The inverse of impedance is admittance, Y = Z-1.
Z1
Z2
Z1
Z2
Zeq = Z1 + Z2
1/Zeq = 1/Z1 + 1/Z2

## Slide 13: Kirchhoff
There are two Kirkoff’s laws, one describes voltages the other describes currents.
i1
i2
i3
i4
i5
i6
V1
V2
V3
V4
V5
V6
i1 + i2 + i3 + i4 + i5 + i6 = 0
(V2 - V1) + (V3 – V2) + (V4 - V3) + (V5 – V4) + (V6 - V1) + (V1 – V6 )= 0

## Slide 14: Thevenin and Norton
Thevenin: Any combination of linear sources and passive elements terminating in two terminals is equivalent to a pure voltage source in series with an impedance
Norton: Any combination of linear sources and passive elements terminating in two terminals is equivalent to a pure current source in parallel with an conductance
Similar theorems for two terminal input and output linear devices (with transfer function)
ZTh
VTh
GTh
IN

## Slide 15: Thevenin example: a real battery
Real batteries have a Thevenin equivalent of an ideal battery in series with a pure resistance, Ri, called the internal resistance.
The equivalent resistance is sometimes called the “lookback” resistance.
Ri

## Slide 16: Phasors
Phasors are complex number-based representations of signals without the frequency component.
If the signal is A cos(𝜔t+𝜙), the phasor representation is composed of, A, ⦣A where ⦣A= 𝜙 represented by Aei𝜙. By the way, sometimes we use i (and sometimes j) to represent . Neither is great since i can be confused with current and j with current density. Both can be confused with indexes. Oh well.
We recover the frequency by multiplying by ei𝜔t.
So, when representing a voltage, in phasor notation by V= V0ei𝜙, we recover the actual wave form as Re(Vei𝜔t).
Average power can be calculated from the phasor representation of a cosine wave as VI*/2. Here * means complex conjugate.
Where does the “2” come from?
  Answer we need to integrate over the current and voltage cycle.
  If “peak” voltage is V0, the “average” voltage is 0 but we care about the magnitude, so we average over the square of the voltage and take the square root. This is called the “root mean square” voltage and is denoted Vrms. Incidentally, your “house” voltage of 120 VAC is actually the root mean square voltage.

## Slide 17: Diodes
Symbol
Diodes are devices that allow current to flow only in one direction. Silicon diodes, for example have, essentially infinite resistance if Vac<0, that is if the cathode is at a higher potential than the anode and very low resistance if Vac> .7V.
The cathode is usually labelled with a band.
There are several types of diodes (e.g.-Zener) with slightly different characteristics.
One recently popular diode (the last symbol above) is the light emitting diode which is a very efficient light source.
Cathode
Anode
vac
Credit: Make Electronics
Sparkfun

## Slide 18: Bipolar Junction Transistors (BJT)
Symbol PNP NPN
Transistors are 3 terminal non-linear devices. They are constructed of one thin layer of semiconductor (Si) sandwiched by two thicker layers. In the case of an NPN transistor the middle layer is “doped” to have a slight excess of hole (positive charge carriers) and the outer layers are doped to have an excess of electrons (negative charge carriers).
BJT’s have three operating regions that depend on the potential differences between the terminals.
Emitter (e)
Collector (c)
Base (b)
Emitter (e)
Collector (c)
Base (b)
Region | Vbe | Vbc | Vce | ic
Active | ≧Vf | <Vf | >Vs | 𝛽ib
Reverse active | <Vf | ≧Vf | <-Vs | -(𝛽r+1)ib
Saturated | ≧Vf | ≧Vf | >-Vs <Vs | >-(𝛽r+1)ib <𝛽ib
Off | <Vf | <Vf | * | 0
For silicon resistors (e.g.-2N3904): Vf ∼ .7v, Vs ∼ .2v, 𝛽 ∼ 100, 𝛽r ∼ 10
ic
ib
vbe

## Slide 19: BJTs - continues
We really care about two regions: the active region where the collector current is proportional to the base current (when Vbe > Vf) and the cutoff region where there is no current flow.
The transistor acts as a switch and is the basis of digital electronics where we care if it’s “off” or “on” but don’t care how on it is.
Transistors can also be used as linear amplifiers when biased (when Vbe>Vf) so that they are always in the active region.
Transistors can be modeled at low frequencies by the following parameters you will find in their specs,
iC = 𝛼iE
iC= 𝛽iB
𝛽 = 𝛼/(1- 𝛼)
𝛽 ∼ 100
Many transistors have a rounded back and a flat front. Looking from the front the terminals are, in order, emitter, base, collector.
There are other types of transistors with slightly different symbols: FET’s, MOSFETS, …
Bipolar source model
RS
vs
Bipolar terminal model
rp
b
e
𝛽ib
c
Credit: Make Electronics

## Slide 20: Analysis: Voltage divider
Very commonly used e.g.: provide transistor bias
V0 = V1-V3
𝛥V1=V1-V2
𝛥V2=V2-V3
𝛥V1= iR1, 𝛥V2= iR2, so 𝛥V1 = 𝛥V2
(+1) 𝛥V2= V0 or 𝛥V2 = V0 and 𝛥V1 = V0
V1
V2
V3
V0

## Slide 21: Analysis: RC circuit
Switch set in position 1
VR=V3-V2
VC=V2-V1
V0= VR + VC
I = C VC =
V0 = RC VC + VC
Solution to RC VC + VC = 0 is V0 exp() so
Solution to RC VC + VC = V0 is V0 (1-exp())
V1
V2
V3
SPDT
Position 1
Position 2
V0
C
R

## Slide 22: Analysis: RL circuit
Switch set in position 1
VR=V3 - V2
VL=V2 - V1
V0= VR + VL
Solution is
V1
V2
L
R
V3
V0

## Slide 23: Analysis: Resonance
Vin = V0 sin(𝜔t)
VC, VL, VR as usual
I(t)= sin(𝜔t-𝜙)
Z is the impedance of the equivalent circuit
and
𝜙 is the phase angle
Z is minimum (so current is maximum) when XL = XC
Or, equivalently when , or when

## Slide 24: Subsystem components and integrated circuits
Miniaturization has allowed us to cram a lot of components into a small package called an integrated circuit or IC.
We’ll use the NEC 555 timer later, this is an analog IC with a small number of integrated devices (transistors, resistors, capacitors). Small scale integration components include operational amplifiers (e.g.-741, 358), audio amps (386), mixers (NEC-602), phase lock loops, and many others.
An Intel processor has billions of transistors crammed onto a single die with feature sizes around 14 nm (1 nm = 10-9 meters).
We’ll be using ICs extensively, especially in digital electronics. The Arduinos and Raspberry Pi processors have millions of transistors on a tiny die and cost peanuts.

## Slide 25: BJT amplifiers
Here’s how to design a common emitter amplifier. We use a 2n3904 transistor with 𝛽=150. This circuit will work! Build it.
Pick the supply voltage Vcc=12V.
Choose a gain (amplification factor), A = 5.
Choose the “Q point” of the conducting transistor (4mA).
Vcc = (ic∙RC) + Vce + ie RE ∼ ie∙ (RC+RE) +Vce with ic=4mA. We get (RC+RE) = (Vcc - Vce)/(4mA) =1.75 k𝝮.
Since A = 5 and A=RC/RE, RC= 5 RE so RE ∼ 270 𝝮 (this is a standard resistor value) and RC= 1.5k𝝮.
ib = 4mA/𝛽 = 27 𝝁A.
Since Vbe must be greater than .7V throughout the input signal range, we want the voltage across R2 to satisfy Vbe + icRE = 1.8V.
We insert a voltage divider consisting of R1 and R2, so that R1= (12-1.8)/270 𝝁A ∼ 39 k𝝮.
Co and Ci are picked to offer small resistance to the frequency range we’re interested in and Co = Ci = 5 𝝁F.
I haven’t explained why we want RE but it provides thermal stability for the transistor over the range we care about. The fact that A=RC/RE can be calculated using Kirchhoff’s laws.
Common emitter amp
RC
R1
Ci
Co
R2
RE
vs
VCC
vs
Credit: Ward, Hands on Radio.

## Slide 26: Filters
Filters attenuate signals over unwanted frequency ranges and preferentially pass signals in wanted frequency ranges.
High pass filters pass frequencies over some threshold.
Low pass filters pass frequencies under some threshold.
Band pass filters pass frequencies within a lower and higher frequency range.
Here are some sample filters. You can calculate, H, the transfer function using Kirchhoff’s laws.
RC Band-pass filter
RC-high pass filter
RC low pass filter
R
C
R
C
R= 60W
C=120mF
L=500mH
H= (1-j/(𝜔RC))-1 = (j𝜔t)/(1+j𝜔t), t= RC
H= R(1+j/(𝜔RC))-1
H= R(R+j(𝜔L-1/(𝜔C)))-1

## Slide 27: Oscillators
Oscillators are a combination of amplifiers and filters.
The output of an amplifier is fed back to the input through a filter or resonance circuit so that the desired frequency output is favored.
The output rapidly settles on a clean signal with the right frequency
The Clapp Oscillator on the right uses a balanced resonant circuit to pick the desired frequency.
Crystals can also be used to obtain very precise frequency selection that does not change as circuit elements heat up.
820
8.2K
68K
RFC
20 𝜇H
100 nF
.1 𝜇F
.01 𝜇F
5000 pF
+12V
5000 pF
.01 𝜇F

## Slide 28: Power, SNR and bandwidth
Relative power, like the power of an input signal compared to an output signal is often measured in dB.
dB= 10 log(). 3dB loss is equivalent to loss of half the original power.
Filters performance is often measured in dB. A good filter will often have relative power (in dB) between the “passband” and the “rejection band” of a factor of more than 10.
At any temperatures higher than 0K, there is ambient noise and a critical metric is the relative power of the signal you want and the noise. This parameter (measured in dB) is called the Signal to Noise ration (SNR).
Bandwidth is a confusing term.
  Most computer scientists use the term refer to the speed with which data can be transmitted or received.
  Analog engineers usually use the term to refer to “passband width.”
  These two are related: a wide passband can pass modulated information encoded at high data rates. Voice transmission require a passband of only about 20 KHz. High speed optical links have passbands of GHZ.

## Slide 29: More circuits
Differential amp
Multi-vibrator
Common emitter as audio amp
Build this and try 100 𝝁F capacitors.
How often do the LED’s blink?
Diagram credit: Sparkfun

## Slide 30: More Circuits
SB
RB
Q
QB
1
10K
10K
Debounce
C= 1000 pf
RL
Power supply
LM7805
.33 +
.1
+
Voltage regulator

## Slide 31: Electronics part 2, digital circuits
You should understand what integrated circuits (IC’s) are and be able to describe, model and use:
  Timers (like the 555 timer)
  Op Amps (like the 741)
  Digital circuits are clocked circuits that implement operation on binary values in clock cycles.
  You should understand how digital memories are implemented and be able to describe two: SRAM and DRAM as well as their characteristics.

## Slide 32: IC’s: 555 Timer
Package: 8 pin dual inline package (“DIP”)
  Pin 1: -Vs
  Pin 8: +Vs
  Pin 2 (Trigger): Out HIGH if V < VCC/3. Pin 2 has control over pin 6. If pin 2 is LOW, and pin 6 LOW, output goes and stays HIGH. If pin 6 HIGH, and pin 2 goes LOW, output goes LOW while pin 2 LOW. This pin has a very high impedance (about 10M) and will trigger with about 1uA.
  Pin 3 (Output): (Pins 3 and 7 are "in phase.") Goes HIGH (about 2v less than rail) and LOW (about 0.5v less than 0v) and will deliver up to 200mA.
  Pin 4 (Reset): Internally connected HIGH via 100k. Must be taken below 0.8v to reset the chip.
  Pin 5 (Control): A voltage applied to this pin will vary the timing of the RC network (quite considerably).
  Pin 6 (Threshold): HIGH if > 2 VCC /3, make output LOW only if pin 2 is HIGH. Pin 6 has very high impedance (~10M) and will trigger with about 0.2uA.
  Pin 7 (Discharge): Pin 7 is equal to pin 3 but pin 7 does not go high - it goes OPEN. When LOW it sinks about 200mA.
Credit: Make Electronics

## Slide 33: Lab: Using the 555 to generate a clock
We use the 555 in astable mode
Try
  R1 = R2 = 10K
  C1= 10
  C2= .1
  Freq: ∼50/sec
Try
  C1= 1 what happens to the frequency
+
SPST
555
1
1
2
3
4
8
7
6
5
out
9V
C1
C2
R1
R2

## Slide 34: Lab: Using the 555 to clock a counter
555 in astable mode used as counter
Same passive values as previously
+
SPST
555
1
1
2
3
4
8
7
6
5
5V
C1
C2
R1
R2
CD4029
1
9 EN
16 Vcc
8
15 CNT
13 J3
10 UP
11 Q2
12 J2
14 Q3
5V
5V
5V
NC
NC
Q4 2
J3 3
J2 4
CO 7
Q1 6
CI 5
NC
NC
NC
NC
1K
1K
1K
1K

## Slide 35: Lab: Using the 555 to generate a pulse
Try
  R1 = R2 = 10K
  C1= 100𝜇F
  C2= .1
If you build this and connect an oscilloscope, you’ll notice the wave isn’t perfectly square. As the pulse rises, you get some overshoot and on discharge there is undershoot. What happens if connect a RC circuit at the output with C around .1 𝝁F. You can also use a Schmidt trigger to clean up messy waveforms.
Pulse length time is secs
SPST
555
1
1
2
3
4
8
7
6
5
out
5V
C1
C2
R1
set
10K
+
reset

## Slide 36: Logic symbols, flip flops, latches and shift registers
We can build circuits that implement logic operations. For example, the and below will output a 1 (5V) only if both inputs are 1.
We can combine these elements together with a clock to build important digital building blocks.
The circuit on the right is an S-R flip flop. QB = ¬Q, always. If EN=0, i1=i2=1 and the other NAND input will be Q will get ¬Q and Q will keep whatever value it had. If EN=1, S=1 and R=0, Q=1 and QB=0. If EN=1, S=0 and R=1, Q=0 and QB=1. The output is undefined if EN=1, and S and R have the same value.
We can also build memory elements, arithmetic elements, and comparators from these elements.
S
R
Q
QB
EN
and
or
not and
not or
i1
i2

## Slide 37: Digital signals and synchronous circuits
Digital signals have two level, on (say 5V) and off (say 0V).
Digital circuits are clocked meaning there is a clock signal pictured below.
A value is calculated by combinatorial logic (and’s or’s,…) with and memory elements and moved into storage elements (registers) on each clock cycle.
In a microcontroller or computer, a program which consists of binary instructions and on each cycle, the instruction selects the logic connecting input registers, the particular logic required by an instruction and an output register.
A program moves from one instruction to the next each clock cycle although some instructions may cause a change in program flow by “jumping” to an earlier or later instruction based, say on some test condition (e.g. jump if the value of register 1 > the value of register 2).
Digital circuits are pretty simple but when so many of them are composed, the processing power is formidable; it has changed our lives.

## Slide 38: SRAM and DRAM
Binary values can be stored in and retrieved from computer memory.
Computer memory comes in two types: Static random-access memories (SRAM) retain the storage value with no intervention and have very fast access times. The registers and caches in your computer are based on SRAM.
Dynamic random-access elements retain values for brief periods of time and must be “refreshed” regularly. The main memory in your PC is built on DRAM.
You can see how DRAM and SRAM are built below.
Data in/out
Bit select
Data-in
¬Data-in
Select
Vcc
DRAM
SRAM

## Slide 39: Circuit tools
In addition to the sort of analysis we’ve done, there are many computer aided design tools. Here are two:
  SPICE: This is a famous device/ circuit analysis tools.
  EagleCAD PCB files on GitHub: This is a cad system to lay out printed circuit boards.

## Slide 40: Electronics part 3: Maxwell and Electromagnetic radiation
See my “Electronics of Radio” Notes for this.

## Slide 41: Exercises
10K pull-up resistor and 5 v power. What is the power drain when we connect it to ground?
Build some of the circuits in this lecture, analyze them with Kirchhoff’s laws and measure (with an oscilloscope) input and outputs.
Estimate the power at reception of a GPS signal.
Use a multimeter
Use an oscilloscope

## Slide 42: Electronics part 4: Computers and computer architecture
Programmable electronics
  Digital electronics can be used to build computers which execute binary instructions in digital memory on data in digital memory to compute results or control equipment.
  Computers are connected to peripherals (sensors, keyboards, displays, speakers) to collect or transmit data to people or other devices.
You should understand basic computer architecture and how the elements below achieve programmability.
  CPU’s
  Memory
  Busses
  I/O – Serial communication
You should understand some important elements of IoT architecture like
  SoC’s
  IoT busses: SPI, I2C

## Slide 43: Computer processor architecture
CPU’s
Memory (registers, SRAM, DRAM)
MMU’s
Busses
Rings and privilege separation
Virtual memory
Devices, interrupts, memory mapped I/O
Programs
Inter-computer communication
GPU’s and FPGA’s

## Slide 44: Computer processor architecture
x
Computers are often described in terms of their architecture.
Architectures focus on the high level interaction of components rather than low level schematics.
Architecture represents the “systems programmer’s” view of the computer.
It was popularized by the deservedly admired “Principles of Operation” describing the IBM /360.
Computers execute digitally encoded instructions which can be loaded at will into a computer. They are “von Neuman” machines.
The diagram above is a generic computer architecture. The one on the right is an Intel based computer.
The major blocks are the CPU, clock, memory subsystem (MMU, cache, DRAM), inter-block bus interfaces and I/O subsystem (busses, interrupt processing).

## Slide 45: Computer processor architecture
A computer is a “clocked” electronic system. Each computer operation is simple and occurs in a clock “cycle.” The clock cycle of modern computers vary from “millions of cycles per second” to “billions of cycles per second.” The faster, the better.
CPU, clock
  The CPU fetches instructions from memory and executes them.
    In a simple processor, a single instruction is executed each cycle; in a complex processor, a single instruction might take several cycles and many instructions may be executing, in different execution units, simultaneously.
  A typical instruction might be “add memory location a to memory location b.”
  Normally, instructions are executed sequentially but there are three ways to change control flow.
    First, unconditional jumps or conditional jumps can synchronously change control flow. For example, an unconditional jump might be “jump to the instruction at memory location m” while a conditional jump might be “jump to the instruction at memory location m if the value at memory location a is bigger or equal to the value at memory location b.” This allows program “loops.”
    Second, interrupts (from clocks or devices) can instruct the processor to start executing instruction streams at different locations.
    Third, error conditions that occur in user mode processing can cause “exceptions” that trap into the OS. An example may be dividing by 0 or attempting to execute a privileged instruction.

## Slide 46: Computer processor architecture
Instructions and data are stored in binary form, i.e. as a series of 1’s and 0’s.
Binary values are organized into bytes (8 bit values) and “words” varying from 2 bytes to 8 bytes.
Words represent numerical values (12, 2324241) and addresses.
Addresses are unsigned integers and are represented in the usual binary form.
  1 is 0000000000000001
  18 is 0000000000010010
Signed integers are usually represented in “two’s complement notation:”
  Positive integers have high order bit of 0, the remainder of the word is the ordinary unsigned binary form.
  0 is all 0 bits.
  Negative numbers have a high order bit of 1 and are arranged so that using the “standard” unsigned addition circuits x + (-x) = 0.
  A simple algorithm for turning a positive binary number into its corresponding negative is to flip each bit in the original representation and use unsigned arithmetic to “add 1.”
  Try it.

## Slide 47: Computer processor architecture
Memory subsystem
  Memory systems store binary values organized as 8 bit bytes. Bytes are organized into words and instructions can refer to either “byte sized” data values or “word sized” data values.
  Most systems are addressable on byte boundaries and at the very lowest level, memory is accessed by “physical addresses” starting at 0 and ending at the size of the memory - 1.
  Programs can be loaded into memory at different locations at different times. As a convenience, most systems have MMU’s which allow a supervisor program to map memory from physical addresses to virtual addresses. Virtual addresses give the program the illusion that memory for their program always starts at 0. The MMU translates virtual addresses into physical addresses.
  Actually, memory is usually arranged into a “hierarchy.”
  CPU’s have internal memory called registers which can be accessed in a single cycle.
  “Main memory” consists of DRAM which (depending on the clock rate of the CPU) can take hundreds of cycles to access.
  In between the CPU and main memory is “cache memory” built from SRAM which contains copies of main memory locations. Cache memory can be accessed in a few cycles maybe even one.

## Slide 48: Computer processor architecture
Memory subsystem
  When a main memory location is accessed and it is not in cache, the value at the location and several sequential locations are loaded into cache. Subsequent accesses are fast.
  Cache and main memory contents must be coherent, that is at well understood times the values must be consistent.
  After a while, under OS control, cache values are evicted and reside only in main memory.
Inter-block bus interfaces
  These are fixed width control lines connecting the CPU and its subsystems. Busses have protocols which dictate the manner in which a device “addresses” another device, puts binary values onto the bus for reading or writing and arbitrates access.
I/O subsystem (busses, interrupt processing).
  I/O busses are similar to inter-block buses but are usually slower. When devices use the bus and want the attention of the CPU, the bus protocol causes a processor interrupt.
  Some devices can read and write main memory without interrupting the CPU. This is called DMA and it is mediated by the MMU.

## Slide 49: Computer processor architecture
There are a few hardware features that greatly simplify programming when many programs are being run. They also provide protection and isolation between programs. Usually there is a single “supervisor” program which manages a computer: this is the operating system “kernel.” Here are some hardware enabled “sharing” features:
  Rings of privilege: Most processors have two or more processor modes (ring 0, 1, 2, 3) or supervisor mode and user mode.
  The operating system kernel runs in supervisor mode. In supervisor mode, a program can execute any instruction, access any memory location, program any peripheral or dependent system (like the MMU). Kernels set up user address spaces for user programs (operating in user mode) by setting up virtual memory maps (page tables) which cannot be accessed by user programs. Supervisor mode instructions and memory are not visible to user mode programs. Usually, the instructions and memory of one user mode program is not accessible to another user mode program (two different programs can share some memory under kernel control). This prevents one program from interfering with another program. Interrupts are set up to “trap” into supervisor mode and are serviced by the kernel. This allows different user programs to safely share devices like displays, USB devices and disks.
  When a user mode program needs a kernel “service,” like writing a file or starting another program, it formats the request and makes a “supervisor call” which traps into the kernel. Base on the arguments and the user mode program privileges, the supervisor performs the service and returns to the user program in user mode.

## Slide 50: SoC’s
With miniaturization, most or all the computer subsystems can be placed on a single integrated circuit or “die” called a “system on a chip” or “SoC.”
The die pictured on the right is an example with an ARM CPU, MMU, cache, read only memory (ROM), several specialized processors like an AES accelerator which can encrypt data at high speed.
DRAM is usually on a separate chip as are I/O devices.
This processor also has “GPIO” pins which can be connected to external circuits and can be controlled by instructions from the CPU.
Most IoT devices consist of one or more “SoC’s.”
Integration of many devices (billions of transistors) is at the heart of the digital revolution. It’s amazing.

## Slide 51: Electronics part 5, Hands on IoT
In this section you will learn to use a simple (and cheap) microcontroller. We will learn:
  How to program them.
  How to interface a wide variety of sensors, devices and transducers using GPIO pins.
  How to communicate with it via the I/O busses (and monitor them).
We’ll do the same for the “Raspberry Pi,” a cheap, but full featured computer which shares the Arduino’s ability to use GPIO but runs a full OS and networking stack.
Arduino and Raspberry Pi represent typical IoT processors.
You will learn the nuts and bolt of connecting Arduino’s and Raspberry Pi with components using perf-boards and how to obtain all these components and design experiments with them.

## Slide 52: Serial Communication
We need a way to communicate between digital devices and perhaps the easiest method is via an asynchronous serial port.
Universal Asynchronous Receiver/Transmitters (UARTs) are integrated electronics packages (diagram lower right) that implement the serial protocol (next page).
The signals can be carried on a simple pair of wires.
You can interface a UART to a computer using a “badge”. I use an Attify Badge which can interface with UART, JTAG and SPI protocols. Another option is an FT232RL FTDI USB to TTL Serial Adapter Module for Arduino Mini Port. Well demonstrate this later.
LSB is transmitted first usually.

## Slide 53: Serial Communication
The UART serial protocol allows two communicating endpoints wired together to send and receive sequentially transmitted digital data bits at speeds (baud rate) known in advance. Each end has a receive pin (RX) and a transmit pin (TX). Data is transmitted in frames consisting of Data bits, Synchronization bits, Parity bits, and Baud rate:
  Start bit (0), data, transmitted least significant bit (LSB) first, a parity bit and a stop bit (1).
  The start bit is LOW telling the receiver that data is coming, then data bits are sent, after 9 bits TX goes HIGH marking the end. 8 bits of data requires 10 bits transmit/received.
  The most common version of this protocol is 9600N1: 9600 baud, no parity, 1 stop bit.
  Data bits, Synchronization bits, Parity bits, and Baud rate.
  The start bit is always indicated by an idle data line going from 1 to 0, while the stop bit(s) will transition back to the idle state by holding the line at 1.

## Slide 54: SPI
A collection of signals shared by two or more endpoints is called a bus.
The SPI bus has a single master device and several slave devices. It is full duplex (meaning the master both transmits and receives data).
Transmission speed agreed in advance. Communications is full duplex.
The SPI bus signals are:
  Master clock (SCLK)
  Master output to slave input (MOSI)
  Master input to slave output (MISO)
  Slave select (SS). This pin on slave is pulled low to select a device)
Sample on rising or falling edge
Arduino and Raspberry Pi have SPI libraries
See https://en.wikipedia.org/wiki/Serial_Peripheral_Interface

## Slide 55: I2C
The I2C bus, like SPI, uses clock information but also allows multiple addressable devices on the same wire bus. The I2C bus consists of the following signals:
  SCL
  SDA
  GND
I2C devices can communicate at 100kHz or 400kHz.
I2C bus drivers are “open drain”, meaning that they can pull the corresponding signal line low, but cannot drive it high. Thus, there can be no bus contention where one device is trying to drive the line high while another tries to pull it low, eliminating the potential for damage to the drivers or excessive power dissipation in the system. Each signal line has a pull-up resistor on it, to restore the signal to high when no device is asserting it low.

## Slide 56: I2C
The protocol is:
  In the normal state SDA, SCL are high
  To begin, the bus master pulls SCL high and SDA low (transition is start condition).
  The master then sends the address of device (MSB first) being addressed and the R(1)/W(0) bit
  The slave pulls SDA low to acknowledge (ACK).
  The master or slave sends data (MSB, first)
  The master generated stop condition by pushing SDA high with SCL high (transition from low to high is stop condition)
For a 7-bit address, the address is clocked out most significant bit (MSB) first, followed by a R/W bit indicating whether this is a read (1) or write (0) operation. The 9th bit of the frame is the NACK/ACK bit. This is the case for all frames (data or address). Once the first 8 bits of the frame are sent, the receiving device is given control over SDA.

## Slide 57: IoT Sensors and Arduino
Cameras and CCD’s
IMUs
Temp, humidity, infrared detectors
GPS
Radar, lidar
RF receivers, transmitters
Sound, vibration detection
Barometer (altimeter)

## Slide 58: Arduino
The Arduino is a microcontroller development board. It costs about $15.
When the Arduino “wakes up,” it checks the serial connection for a program to be downloaded. If one is present, the Arduino downloads it. If there is no new program or the download is complete, it runs the last loaded program.
Arduino has about 30 “GPIO” pins you can connect to. Some are connected to analog to digital converters (ADC) and digital converters (DAC) so you can read and write analog signals. Some are digital pins you can connect to other digital devices.
Your program can read to write data to the I/O pins.
The heart of the Arduino is a simple microcontroller (e.g. - ATMega-328).
You can supply external power (5V) or it can be powered through the serial interface (3.3V).
There is a complete program development environment available here, as well as tons of sample code for use with sensors (see references).

## Slide 59: Arduino Bootloader
In IDE, select the board definition for your target Arduino from Tools > Board. Then select the programmer that you are using under Tools > Programmer (if you are using the Arduino as ISP you will also need to select the COM port that the Arduino as ISP is connected to). Finally, select Burn Bootloader. This will take the board you selected and look up the associated bootloader in the board.txt file. Then, it will find the bootloader in the bootloader folder and install it. This only works if the board is installed correctly in the IDE and you have the correct bootloader.

## Slide 60: Arduino
You can connect a lot of devices via the GPIO pins to the Arduino including programs that implement the asynchronous serial interface, SPI, and I2C, as well as digital sensors, memory, actuators like robot arms and radios.
We’ll demonstrate
  Reading and writing analog signal
  Reading and writing a read only memory (ROM) chip
  Reading and writing an SD card
  Reading sensor data from thermometers, gyros, accelerometers and infrared detectors
Connecting other devices is very similar.

## Slide 61: ESP32
Another microcontroller is the ESP32, released in 2016.
This uses the Xtensa architecture
It has built in wifi and blue-tooth (the Arduino doesn’t).
The documentation is here.
You can use the Arduino IDE to program the ESP32 and the same sample code should work.

## Slide 62: Information and Stuff
Here are some datasheets for the hardware and some software we’ll use:
  ADXL345 Accelerometer Datasheet
  L3G4200D Gyroscope Datasheet
  MC5883L Magnetometer Datasheet
  DHT Datasheet
  Ping sensor Datasheet
  MPU-6050 Datasheet
  Barometer (BMP-280) Datasheet
  I2C EEPROM Datasheet
  GPS module Datasheet
  24AA515 EEPROM Datasheet
  Microchip 93c66b EEProm Datasheet
  You will need to get the DHT library and the Arduino development environment.
You can buy all the hardware (including Arduino) at Sparkfun or on Amazon.
You can buy kits with Arduinos, wires and discrete components and lots of sensors from Egloo, Sparkfun and lots of other places. A basic kit is about $50.

## Slide 63: Raspberry Pi
Raspberry Pi computers come with a full CPU, an ARM microprocessor, (not just a microcontroller) and have memory and I/O ports (USB, Ethernet).
It runs a standard operating system like Linux.
Chromebooks are built using these sort of ARM chips.
ARM processors can be 16, 32 or 64 bit and can run fairly powerful software.
The Pi’s also have the GPIO pins just like an Arduino does.
It costs about $35.
Its an amazing amount of technology for so little money.
You can do all the projects we do with the Arduino on a Raspberry Pi and send data over a local network or “log on” via a console interface directly.
You can buy them at the same places you buy Arduinos.

## Slide 64: Raspberry Pi

## Slide 65: Raspberry Pi GPIO pins
PWM (pulse-width modulation)
  Software PWM available on all pins
  Hardware PWM available on GPIO12, GPIO13, GPIO18, GPIO19
SPI
  SPI0: MOSI (GPIO10); MISO (GPIO9); SCLK (GPIO11); CE0 (GPIO8), CE1 (GPIO7)
  SPI1: MOSI (GPIO20); MISO (GPIO19); SCLK (GPIO21); CE0 (GPIO18); CE1 (GPIO17); CE2 (GPIO16)
I2C
  Data: (GPIO2); Clock (GPIO3)
  EEPROM Data: (GPIO0); EEPROM Clock (GPIO1)
Serial
  TX (GPIO14); RX (GPIO15)
Pin 1
Pin 3
Pin 2
Pin 4

## Slide 66: Raspberry Pi 3 pins
There are three different numbering schemes for:
  The pin ordering on the J8 header
  The pin number used by wiringPi (which we use)
  The BCM (GPIO HW interface) from Broadcom
Note: even numbered header pins are near edge of Raspberry Pi.

## Slide 67: Raspberry Pi
Unlike the Arduino, we need to install an OS (Linux) on the Raspberry Pi to use it. Once you do, you can develop, compile and run the IoT programs on the device.
You’ll load the OS and other files on a FAT-32 formatted SD card with at least 4 GB of capacity (I use 32 GB). Download the installer zip file at http://raspberrypi.org/downloads. Unzip it onto the SD card. You should notice the file bootloader.bin on the SD card. Plug the SD card into the pi and boot.
Many of the Raspberry pi sensor examples are in python. For C++ examples, see here, here, here, here (accelerometers, gyros, compasses) and here. We use WiringPi almost exclusively to program GPIO pins. WiringPi supports SPI and I2C interfaces; it is here and is pre-installed on newer Raspberry Pi OS images. Read the reference!
Unlike the Arduino, Raspberry Pi GPIO pins do not natively support analog signals. I use the Adafruit MCP4725 Breakout Board - 12-Bit DAC w/I2C Interface [ADA935] and the Microchip MCP3008-I/P 10-Bit ADC with SPI to interface analog connections.

## Slide 68: Labs
Most of the rest of this section is lab exercises to get you used to IoT wiring and programing. We do some circuits and connect and program a number of sensors to Arduino’s, Raspberry Pi’s and in one case, directly to the USB port of a Linux machine. There’s a partial list below. You should do as many of these as you can. Here, “A” means Arduino, “R” means Raspberry Pi and “L” means linux desktop.
Goal | Parts | Device
Simple GPIO IF | LED, resistors | A, R
Analog interface | Variable resistor PCF8591 for R | A, R
Ultrasonic measurement | HC-SR04 | A, R
Digital temperature | DHT-11 | A, R
Digital acceleration/gyro | MPU-6050 | A, R
Read/write EEprom | 24FC515 | A, R
UART | FDTI1232 for linux | A, R
Digital GPS | ATGM336H-5N | A, R, L
Segment display, encoder | SN595 SR | A
Keypad interface |  | A
Goal | Parts | Device
SPI interfacing |  | R
TFT(screen) | ILI9341 240X320 | A
Digital pressure | BMP-180/280 | A, R
Magnetic field | Hall sensor | A, R
Vibration, tilt |  | A, R
LCD (direct and I2C) | LCD-1602 | A, R
RFID | RC522 rfid card | A
Stepper |  | A
Infrared |  | A
Radio | HC-12 | A, RP

## Slide 69: Lab: turn on an LED
Wire the ground of the Arduino to.
The code is in the appendix.
Arduino
5V
Gnd
A0
680𝞨
1K𝞨

## Slide 70: Arduino code for LED
// turn LED on and off
// Manferdelli
const int switchPin= 4;
const int oscDelay= 500;
const int analogOn= 255;
const int analogOff= 0;
void setup() {
pinMode(switchPin, OUTPUT);
}
void loop() {
for(;;) {
analogWrite(switchPin, analogOff);
delay(oscDelay);
analogWrite(switchPin, analogOn);
delay(oscDelay);
}
}

## Slide 71: Raspberry Pi code for LED
#include <stdio.h>
#include <stdint.h>
#include <wiringPi.h>
#include <wiringPiI2C.h>
// turn LED on and off
// Manferdelli
const int switchPin = 0;
const int measurementDelay = 500;
const int loopCount = 250;
int main(int an, char** av) {
wiringPiSetup ();
pinMode (switchPin, OUTPUT);
for (int i = 0; i < loopCount; i++) {
digitalWrite(switchPin, HIGH);
delay(measurementDelay);
digitalWrite(switchPin, LOW);
delay(measurementDelay);
}
return 0;
}
Raspberry Pi
5V, header pin 2
GPIO0, HDR pin 11
680𝞨
1K𝞨
Gnd, HDR pin 6

## Slide 72: Lab: Measure voltage output
Suppose you have a voltage output from a device that is proportional to some physical quantity (like the speed of a motor) between 0 and 5V, sampling the value on the pins of the Arduino lets you display or use that value in a control system.
Let’s simulate such source using the circuit on the right, varying the resistance will change data values. Wire the ground of the Arduino to the circuit as indicated.
The code is in the appendix.
Output (varying potentiometer)
  ADC value:955, Voltage:4.67
  ADC value:1021, Voltage:4.99
  ADC value:988, Voltage:4.83
  ADC value:876, Voltage:4.28
  ADC value:726, Voltage:3.55
  ADC value:638, Voltage:3.12
  ADC value:596, Voltage:2.91
  ADC value:457, Voltage:2.23
  ADC value:357, Voltage:1.74
10K𝛺
Arduino
5V
Gnd
A0

## Slide 73: Arduino code for voltage measurement
// Measure analog level
// Manferdelli
const int inputPin= A0;
const int pinDelay= 500;
const double maxVoltage= 5.0;
const double maxRange= (double)1024;
void setup() {
pinMode(inputPin, INPUT);
Serial.begin(9600);
Serial.print("Maximum voltage: ");
Serial.print(maxVoltage);
Serial.print(", Maximum range: ");
Serial.print(maxRange);
Serial.println("");
}
void loop() {
int x;
double y;
for(;;) {
delay(pinDelay);
x= analogRead(inputPin);
y= maxVoltage * ((double)x)/maxRange;
Serial.print("Voltage: ");
Serial.print(y);
Serial.println("");
}
}

## Slide 74: Voltage measurement on Raspberry Pi
The Raspberry Pi does not have analog pins. You must use an ADC/DAC to get analog values.
We will use a popular ADC/DAC called the PCF8591 which has an I2C interface.
We use the wiringPiI2C library to interface to I2C.
The code is the same for all analog interfacing.
Note: You must enable the Raspberry Pi I2C kernel module or it won’t work. To do this, run raspi-config and use the interfacing option.
The connection to the PCF8591 are:
    PCF RP
    1(ain0) analog-signal
    5, 6, 7, 8 gnd (pin 6)
    16 3.3 (pin 1)
    14 3.3v
    13 gnd
    12 gnd
    10(scl) rp pin 5 (scl)
    9(sda) rp pin 3 (sda)

## Slide 75: PCF8591 pinout and connections
The PCF8591 which employs a I2C interface to the Raspberry Pi.
Pin 1 – Ain0
Pin 2 – Ain1
Pin 3 – Ain2
Pin 4 - Ain3
Pin 5 – A0
Pin 6 – A1
Pin 7 – A2
Pin 8 - VSS
Pin 16 - VDD
Pin 15 - Aout
Pin 14 - VREF
Pin 13 - AGND
Pin 12 - EXT
Pin 11 - OSC
Pin 10 - SCL
Pin 9 – SDA
Raspberry Pi connections
  SDA (PCF8591)  SDA
  SCL  SCL
  3.3V  VCC
  GND  GND
  Ain0  measured quantity
  Ground A0, A1, A2, VSS
  Aout  through diode and 1K resistor
  AGND, EXT  GND
  Use SCL to SDA through pull-up (10K)

## Slide 76: Voltage measurement on Raspberry Pi
// Manferdelli
// Raspberry Pi analog read
#include <stdio.h>
#include <wiringPi.h>
#include <pcf8591.h>
const int base = 120;
const int i2c_address = 0x48;
int main(int an, char** av) {
int v = 0;
if (wiringPiSetup() < 0) {
printf("Can't initialize wiringPi\n");
return 1;
}
pcf8591Setup(base, i2c_address);
for(;;) {
v = analogRead(base);
delay(10);
printf("Voltage: %d\n", v);
}
return 0;
}
Raspberry Pi
3.3 V, HDR pin 1
SDA, HDR pin 3
Gnd, HDR pin 6
PCF8591
Gnd
  SCL, HDR pin 5
SCL
SDA
Ain0
Vcc
10K𝛺

## Slide 77: Lab: Measure Distance
Wire the the Arduino to the “ping” sensor (HC-SR04) as indicated.
The Ping sensor only works up to about 1 meter.
The code is in the appendix. The output below was obtained moving an object at varying distances from the sensor. Distance is in cm.
Arduino
5V
Gnd
D8
Ping
Vcc
Trig
Echo
Gnd
D7
5V
7
6
10
15
21
26
30
31
24
33
10
9
5
14
22
25
30
33
36
38
24
13
5
3
4
3
108
107

## Slide 78: Arduino code for measure distance
// Measure distance with ping sensor
// Manferdelli
const int triggerPin= 8;
const int echoPin= 7;
const int measurementDelay= 500;
const int pingDelay= 5;
const double temp = 20; // C
const double soundSpeed = 331.5 + .6 * temp; // m/s
void setup() {
Serial.begin(9600);
Serial.println("Ping sensor test");
pinMode(triggerPin, OUTPUT);
pinMode(echoPin, INPUT);
}
// pulseIn reads a pulse (either HIGH or LOW) on a pin. If value is HIGH,
// pulseIn() waits for the pin to go from LOW to HIGH to starts timing,
// it then waits for the pin to go LOW and stops timing.
// Returns the length of the pulse in microseconds.

## Slide 79: Arduino code for measure distance
void measure_distance() {
digitalWrite(triggerPin, LOW);
delayMicroseconds(3);
digitalWrite(triggerPin, HIGH);
delayMicroseconds(5);
digitalWrite(triggerPin, LOW);
double return_time_microsecs = pulseIn(echoPin, HIGH);
double one_way_return_time = return_time_microsecs / 2e6;
double d = soundSpeed * one_way_return_time * 100.0; // cm
Serial.print("Measured distance (cm): ");
Serial.println(d);
}
void loop() {
for(;;) {
delay(measurementDelay);
measure_distance();
}
}

## Slide 80: Ping sensor and raspberry pi
Use gpio 7 (pin 7) and gpio 27 (pin 36).
Wiring below. Sensor pins are vcc, trigger, echo gnd (left to right from front)
Vcc
trigger
echo
gnd
Raspberry Pi
5.0 V, HDR pin 2
Gnd, HDR pin 6
  GPIO7, HDR pin 7
  GPIO27, HDR pin 36
Ping Sensor
Vcc
Trig
Echo
Gnd

## Slide 81: RP code for measure distance
// Manferdelli
// Raspberry Pi, ping sensor
#include <stdio.h>
#include <stdlib.h>
#include <stdint.h>
#include <wiringPi.h>
#ifndef byte
typedef unsigned char byte;
#endif
// Connections
// Ping RP
// trigger gpio 7 (pin 7)
// echo gpio 27 (pin 36)
// vcc 5v
// gnd gnd
// I had to use a scope to check,
// RP pin numbering is mysterious.
// Look at the ifdef'd code below
// to see it.
const int trigger_pin = 7;
const int echo_pin = 27;
const int max_distance = 500; // cm
long unsigned time_out_period;
const double sound_speed = 340.0; // speed sound(m/s)
long pulseIn(int pin, int value, int time_out) {
pinMode(echo_pin, INPUT);
long unsigned start = micros();
while(digitalRead(pin) != value) {
if ((micros() - start) > time_out_period)
return 0;
}
long unsigned set = micros();
while(digitalRead(pin) == value) {
if ((micros() - set) > time_out_period)
return 0;
}
long unsigned end = micros();
printf("pulseIn, end: %d, start: %d\n",
end, start);
return end - set;
}

## Slide 82: RP code for measure distance
double getDistance() {
#if 1
pinMode(trigger_pin, OUTPUT);
pinMode(echo_pin, OUTPUT);
digitalWrite(trigger_pin, LOW);
delayMicroseconds(5);
digitalWrite(trigger_pin, HIGH);
delayMicroseconds(10);
digitalWrite(trigger_pin, LOW);
#else
// Find pins
pinMode(trigger_pin, OUTPUT);
pinMode(echo_pin, OUTPUT);
for(;;) {
digitalWrite(trigger_pin, LOW);
delayMicroseconds(1000);
digitalWrite(trigger_pin, HIGH);
delayMicroseconds(1000);
digitalWrite(echo_pin, LOW);
delayMicroseconds(1000);
digitalWrite(echo_pin, HIGH);
delayMicroseconds(1000);
}
#endif
long unsigned ping_time = pulseIn(echo_pin, HIGH,
time_out_period);
double d = (((double)ping_time) * sound_speed) / 20000.0;
return d;
}
int main(int an, char** av) {
if (wiringPiSetup() < 0) {
printf("Can't initialize Wiring Pi\n");
return 1;
}
time_out_period = ((max_distance*20000)/sound_speed)+1;
double d;
for(;;) {
d = getDistance();
printf("Target distance is %8.2lf cm\n", d);
delay(1000);
}
return 0;
}

## Slide 83: DHT11 & DHT22 Temperature Sensors
The DHT22 temperature measuring range is from -40 to +125 degrees Celsius +-0.5 degree. Humidity: from 0 to 100% with 2-5% accuracy.
DHT11 temperature range is 0 to 50 degrees Celsius with +-2 degrees. Humidity: from 20 to 80% with 5% accuracy.
Operating voltage of both sensors is from 3 to 5 volts.
Humidity sensor has two electrodes with moisture holding substrate between them. Conductivity of the substrate changes and the resistance between these electrodes changes. This change in resistance is measured.
Temperature sensor is NTC (negative temperature coefficient) thermistor made by sintering of semiconductive materials such as ceramics or polymers in order to provide large changes in the resistance with just small changes in temperature.

## Slide 84: Lab: Measure Temperature
Wire the Arduino as shown to the DHT-11 sensor.
The code is in the appendix. Output taken in my apartment. I guess I need to turn up the heat.
Output
  Humidity: 20%
  Temperature: 17C
  Temperature: 62.60F
  Humidity: 20%
  Temperature: 17C
  Temperature: 62.60F
Arduino
5V
Gnd
D7
DHT-11
Vcc
Signal
not used
Gnd
Freenove
Vcc
Sig
Gnd
1K

## Slide 85: Arduino code for measure temperature
// Measure temperature and humidity with DHT-11
// Manferdelli
const int dataPin= 8;
const int measurementDelay= 500;
typedef uint8_t byte;
void setup() {
Serial.begin(9600);
}
void clear_buf(byte* p, int size) {
for (int i = 0; i < size; i++)
p[i] = 0;
}
const int initReadDelay = 18;
void start_measurement() {
pinMode(dataPin, OUTPUT);
digitalWrite(dataPin, LOW);
delay(initReadDelay);
digitalWrite(dataPin, HIGH);
}

## Slide 86: Arduino code for measure temperature
const int packetSize = 40; // bits
const int pulseOneLength = 40; // pulse length to be 1
const int pulseDelay= 18;
int measure_th(int* t, int* h) {
byte buf[8];
clear_buf(buf, 8);
byte byte_index = 0;
byte bit_cnt = 7;
pinMode(dataPin, INPUT);
delayMicroseconds(pulseDelay);
pulseIn(dataPin, HIGH);
// Collect each data bit
int time_out = 10000;
for (int i = 0; i < packetSize; i++) {
while (digitalRead(dataPin) == LOW) {
if (time_out-- <= 0)
return -1;
}
time_out = 10000;
unsigned long t = micros();

## Slide 87: Arduino code for measure temperature
while (digitalRead(dataPin) == HIGH) {
if (time_out-- <= 0)
return -1;
}
if ((micros() - t) > pulseOneLength) {
buf[byte_index] |= 1 << bit_cnt;
}
if (bit_cnt == 0) {
byte_index++; // next byte
bit_cnt = 7; // MSB
} else {
bit_cnt--;
}
}
*t = buf[2];
*h = buf[0];
if ((buf[0] + buf[2]) != buf[4])
return -1;
return 0;
}

## Slide 88: Arduino code for measure temperature
void read_dht11(int* t, int* h) {
start_measurement();
if (measure_th(t, h) < 0) {
*t = 0.0;
*h= 0.0;
return;
}
}
void loop() {
int temperature, humidity;
for(;;) {
delay(measurementDelay);
read_dht11(&temperature, &humidity);
Serial.print("Temp (C): ");
Serial.print(temperature);
Serial.print(", Temp (F): ");
double temp_F = ((double) temperature) * 9.0 / 5.0 + 32.0;
Serial.print(temp_F);
Serial.print(", Humidity (%): ");
Serial.print(humidity);
Serial.println("");
}
}

## Slide 89: Raspberry Pi code for measure temperature
// Manferdelli
// Raspberry Pi interface to dht11
#include <stdio.h>
#include <stdlib.h>
#include <stdint.h>
#include <wiringPi.h>
#ifndef byte
typedef unsigned char byte;
#endif
void clearBuf(byte* buf, int n) {
for (int i = 0; i < n; i++) {
buf[i] = 0;
}
}
void printBuf(byte* in, int n) {
for (int i = 0; i < n; i++) {
printf(" %02x", in[i]);
if ((i % 16) == 15) {
printf("\n");
}
}
printf("\n");
}
Vcc
trigger
echo
gnd
Raspberry Pi
5.0 V, HDR pin 2
Gnd, HDR pin 6
  GPIO7, HDR pin 7
DHT-11
Vcc
DHT, sig
Gnd
1K

## Slide 90: Raspberry Pi code for measure temperature
const int dht_pin = 7;
const int timingDelay = 18;
const int messageDelay = 2000;
const int max_timings = 90;
const int bits_to_read = 40;
#define DATA_BUF_SIZE 10
class temp_sensor {
public:
double h_;
double c_;
double f_;
};
bool get_dht_data(byte* data, int size, temp_sensor* r) {
if (size < 5)
return false;
byte last_state = HIGH;
int counter = 0;
int i = 0;
int j = 0;
pinMode(dht_pin, OUTPUT);
digitalWrite(dht_pin, LOW);
delay(timingDelay);
pinMode(dht_pin, INPUT);

## Slide 91: Raspberry Pi code for measure temperature
// Detect change
for (i = 0; i < max_timings; i++) {
counter = 0;
while(digitalRead(dht_pin) == last_state) {
counter++;
delayMicroseconds(1);
if (counter == 255)
break;
}
last_state = digitalRead(dht_pin);
// ignore first 3 transitions
if (i>=4 && (i%2)==0) {
data[j/8] <<= 1;
if (counter > 16)
data[j/8] |= 1;
j++;
}
}
// Make sure we read 40 bits and verify checksum
if (j < bits_to_read)
return false;
byte check_sum = data[0] + data[1] + data[2] + data[3];
if (check_sum != data[4])
return false;

## Slide 92: Raspberry Pi code for measure temperature
// Make sure we read 40 bits and verify checksum
if (j < bits_to_read)
return false;
byte check_sum = data[0] + data[1] + data[2] + data[3];
if (check_sum != data[4])
return false;
// calculate readings
int t;
// humidity
t = data[0];
t <<= 8;
t += data[1];
r->h_ = ((double)t)/10.0;
if (r->h_ > 100.0)
r->h_ = ((double)data[0]);

## Slide 93: Raspberry Pi code for measure temperature
// temperature
t = data[2] & 0x7f;
t <<= 8;
t += data[3];
r->c_ = ((double)t) / 10.0;
if (r->c_ > 125)
r->c_ = ((double) data[2]);
if (data[2] & 0x80)
r->c_ = -r->c_;
r->f_ = 1.8 * r->c_ + 32.0;
return true;
}
// Program needs to be run as su
int main(int an, char** av) {
if (wiringPiSetup() < 0) {
printf("Can't initialize wiringPi\n");
return 1;
}
temp_sensor r;
byte data[DATA_BUF_SIZE];
for(;;) {
clearBuf(data, DATA_BUF_SIZE);
if (get_dht_data(data, DATA_BUF_SIZE,&r))
printf("Humidity: %7.3lf, Temperature: %7.3lf (C), %7.3lf (F)\n",
r.h, r.c, r.f);
delay(messageDelay);
}
return 0;
}

## Slide 94: Accelerometer Sensors
Accelerometers can measure acceleration on one, two, or three axes. 3-axis units are becoming more common as the cost of development for them decreases.
MEMS accelerometers contain capacitive plates internally. Some of these are fixed, while others are attached to minuscule springs that move internally as acceleration forces act upon the sensor. As these plates move in relation to each other, the capacitance between them changes. From these changes in capacitance, the acceleration can be determined.
Most accelerometers will have a selectable range of forces they can measure. These ranges can vary from ±1g up to ±250g.
Accelerometers will communicate over an analog, digital, or pulse-width modulated connection interface.
  The analog interface shows accelerations through varying voltage levels. An ADC on a microcontroller can then be used to read this value. These are generally less expensive than digital accelerometers.
  Accelerometers with a digital interface can either communicate over SPI or I2C communication protocols.
  Accelerometers that output data over pulse-width modulation (PWM) output square waves with a known period, but a duty cycle that varies with changes in acceleration.

## Slide 95: Lab: Measure Acceleration and angular velocity MPU-6050
The MPU-6050 is gyro, accelerometer and temperature sensor. Wire the Arduino as shown.
Here is sample output:
  A.009g, 0.060g)
  Temperature (C): 21.54
  Gyro: x,y,z (12.49 deg/s, -0.53 deg/s, -4.Accelerometer: x,y,z (1.027g, 0.238g, -0.080g)
  Temperature (C): 21.68
  Gyro: x,y,z (-213.01 deg/s, 3.59 deg/s, -4.07 deg/s)
  Accelerometer: x,y,z (-0.387g, 0.137g, -0.962g)
  Temperature (C): 21.68
  Gyro: x,y,z (50.60 deg/s, 147.03 deg/s, 2.34 deg/s)
  Accelerometer: x,y,z (0.718g, -0.308g, -0.134g)
  Temperature (C): 21.78
Arduino
5V
Gnd
A5
MPU-6050
Vcc
SDA
Int
Gnd
A4
D2
SCL
SparkFun

## Slide 96: Output continued
Gyro: x,y,z (25.02 deg/s, 33.97 deg/s, -250.14 deg/s)
Accelerometer: x,y,z (0.193g, 0.934g, -0.269g)
Temperature (C): 21.78
Gyro: x,y,z (4.58 deg/s, -10.77 deg/s, -6.54 deg/s)
Accelerometer: x,y,z (0.997g, 0.022g, -0.366g)
Temperature (C): 21.87
Gyro: x,y,z (21.85 deg/s, 86.79 deg/s, 64.41 deg/s)
Accelerometer: x,y,z (0.533g, -0.249g, -0.236g)
Temperature (C): 21.78
Gyro: x,y,z (11.31 deg/s, -109.04 deg/s, 63.29 deg/s)
Accelerometer: x,y,z (0.423g, -0.120g, -0.271g)
Temperature (C): 21.87
Gyro: x,y,z (14.21 deg/s, 41.51 deg/s, -42.22 deg/s)
Accelerometer: x,y,z (1.027g, 0.016g, 0.061g)
Temperature (C): 21.78
Gyro: x,y,z (12.65 deg/s, -0.35 deg/s, -4.89 deg/s)
Accelerometer: x,y,z (1.022g, 0.016g, 0.066g)
Temperature (C): 21.82
Gyro: x,y,z (12.54 deg/s, -0.21 deg/s, -4.98 deg/s)
Accelerometer: x,y,z (1.028g, 0.011g, 0.065g)
Temperature (C): 21.78
Gyro: x,y,z (12.67 deg/s, -0.40 deg/s, -4.97 deg/s)
Accelerometer: x,y,z (1.023g, 0.015g, 0.061g)
Temperature (C): 21.92

## Slide 97: Arduino code for measure acceleration
// Read accelerometer (MPU-6050)
// Manferdelli
#include <Wire.h>
typedef uint8_t byte;
const byte i2c_address= 0x68;
const byte sleep_mgmt= 0x6b;
const byte acc_x_out= 0x3b;
const int zero_pt= -512 - (340 * 35);
const double acc_normalizer= 16384.0;
const double gyro_normalizer= 131.0;
const double temp_normalizer= 340.0;
const int measurementDelay= 750;
//
// SDL --> A5
// SDA --> A4
// int --> D2

## Slide 98: Arduino code for measure acceleration
typedef uint8_t byte;
struct pdu {
int16_t x_acc;
int16_t y_acc;
int16_t z_acc;
int16_t temp;
int16_t x_gyro;
int16_t y_gyro;
int16_t z_gyro;
};
void setup() {
Serial.begin(9600);
Wire.begin();
write_i2c(sleep_mgmt, 0x00);
}
int16_t swap_bytes(int16_t in) {
return ((in << 8) & 0xff00) | ((in >> 8) & 0x00ff);
}

## Slide 99: Arduino code for measure acceleration
int read_i2c(byte r, byte* buf, int size) {
Wire.beginTransmission(i2c_address);
Wire.write(r);
Wire.endTransmission(false);
Wire.requestFrom(i2c_address, size, true);
int i= 0;
while (Wire.available() && i < size) {
buf[i++]= Wire.read();
}
return i;
}
void write_i2c(byte r, byte d) {
Wire.beginTransmission(i2c_address);
Wire.write(r);
Wire.write(d);
Wire.endTransmission(true);
}

## Slide 100: Arduino code for measure acceleration
void loop() {
pdu p_out;
read_i2c(acc_x_out, (byte*)&p_out, sizeof(pdu));
p_out.x_acc= swap_bytes(p_out.x_acc);
p_out.y_acc= swap_bytes(p_out.y_acc);
p_out.z_acc= swap_bytes(p_out.z_acc);
p_out.temp= swap_bytes(p_out.temp);
p_out.x_gyro= swap_bytes(p_out.x_gyro);
p_out.y_gyro= swap_bytes(p_out.x_gyro);
p_out.z_gyro= swap_bytes(p_out.x_gyro);
double acc_x= ((double)p_out.x_acc) / acc_normalizer;
double acc_y= ((double)p_out.y_acc) / acc_normalizer;
double acc_z= ((double)p_out.z_acc) / acc_normalizer;
double t= (p_out.temp - zero_pt) / temp_normalizer;
double gyro_x= ((double)p_out.x_gyro) / gyro_normalizer;
double gyro_y= ((double)p_out.y_gyro) / gyro_normalizer;
double gyro_z= ((double)p_out.z_gyro) / gyro_normalizer;

## Slide 101: Arduino code for measure acceleration
Serial.println("");
Serial.println("-----------------------------");
Serial.print("Acceleration (g): (");
Serial.print(acc_x);
Serial.print(", ");
Serial.print(acc_y);
Serial.print(", ");
Serial.print(acc_z);
Serial.println(")");
Serial.print("Temperature (C): ");
Serial.print(t);
Serial.println("");
Serial.print("Gyro (deg/sec): (");
Serial.print(gyro_x);
Serial.print(", ");
Serial.print(gyro_y);
Serial.print(", ");
Serial.print(gyro_z);
Serial.println(")");
Serial.println("-----------------------------");
Serial.println("");
delay(measurementDelay);
}

## Slide 102: Raspberry Pi code for measure acceleration
// Manferdelli
// Raspberry Pi, mpu-6050
#include <stdio.h>
#include <stdlib.h>
#include <stdint.h>
#include <math.h>
#include <wiringPi.h>
#include <wiringPiI2C.h>
#ifndef byte
typedef unsigned char byte;
#endif
const byte i2c_address = 0x68;
const byte x_address= 0x3b;
const byte y_address = 0x3d;
const byte z_address = 0x3f;
const double pi = 3.1415926535;
Vcc
trigger
echo
gnd
Raspberry Pi
5.0 V, HDR pin 2
MPU-6050
Vcc
Gnd
SDA, HDR pin 3
  SCL, HDR pin 5
SDA
SCL
  Gnd, HDR 6

## Slide 103: Raspberry Pi code for measure acceleration
// Connection scheme
// RP 6050
// Gnd(HDR 6) Gnd
// scl(HDR 5) scl
// 5v (HDR 1) Vcc
// sda(HDR 3) sda
Int read_int(int fd, byte address) {
int r = 0;
int v = 0;
v = wiringPiI2CReadReg8(fd, address);
v <<= 8;
v |= wiringPiI2CReadReg8(fd, address + 1);
if (v &0x8000)
v = -(65536 – v);
return v;
}
Double dist(double a, double b) {
return sqrt(a * a + b * b);
}

## Slide 104: Raspberry Pi code for measure acceleration
double get_x_rotation(double x, double y, double z) {
double s = dist(x, z);
if (s == 0.0) {
if (y < 0.0)
return -90.0;
return 90.0;
}
double r = atan(y / s);
return -(r * 180.0 / pi);
}
double get_y_rotation(double x, double y, double z) {
double s = dist(y, z);
if (s == 0.0) {
if (x < 0.0)
return -90.0;
return 90.0;
}
double r = atan(x / s);
return -(r * 180.0 / pi);
}

## Slide 105: Raspberry Pi code for measure acceleration
int main(int an, char** av) {
int fd = wiringPiI2CSetup(i2c_address);
if (fd < 0) {
printf("Can't initialize Wiring Pi\n");
return 1;
}
wiringPiI2CWriteReg8(fd, 0x6b, 0); // disable sleep
int a_x, a_y, a_z;
double scaled_x, scaled_y, scaled_z;
double rot_x, rot_y;
for(;;) {
a_x = read_int(fd, x_address);
a_y = read_int(fd, y_address);
a_z = read_int(fd, z_address);
scaled_x = ((double)a_x) / 16384.0;
scaled_y = ((double)a_y) / 16384.0;
scaled_z = ((double)a_z) / 16384.0;
rot_x = get_x_rotation(scaled_x, scaled_y, scaled_z);
rot_y = get_y_rotation(scaled_x, scaled_y, scaled_z);
printf("Scaled acceleration: (%07.2f, %07.2f, %07.2f), x-y rotation: (%07.2f, %07.2f)\n",
scaled_x, scaled_y, scaled_z, rot_x, rot_y);
delay(1000);
}
return 0;
}

## Slide 106: EEproms
EEPROM, or Electrically Erasable Programmable Read-Only Memory, is a type of device that allows you to store small chunks of data and retrieve it later even if the device has been power cycled.
Serial EEPROM devices like the Microchip 24-series EEPROM allow you to add more memory to any device that can speak I²C.
256 Kbit EEPROM contains 32000 byte addressable.
Most Significant and Least Significant Bytes
  Address is two bytes.
  First we send the Most Significant Byte (MSB) — the first 8 bits in this case.
  Then we send the Least Significant Byte (LSB) — the second 8 bits.
Most EEPROM devices have something called a “page write buffer” which allows you to write multiple bytes at a time the same way you would a single byte.

## Slide 107: Lab: Read/write an EEPROM
The 24FC515 EEProm communicates over I2C .
Wire the Arduino to the eeprom as indicated.
The code follows.
Arduino
5V
Gnd
A5
24FC515 EEPROM
Vcc (8)
SDA (5)
Gnd (4)
SCL (6)
A4
A0 (1)
A1 (2)
A2 (3)
WP (7)

## Slide 108: Arduino code for EEprom
// eeprom read/write
// Manferdelli
#include <Wire.h>
typedef uint8_t byte;
const int measurementDelay= 500;
const int initial_clock_setting= 400000;
const uint32_t maxMillis= 2000;
#define MAX_BYTES 64
// Theoretically, the 24LC256 has a 64-byte page write buffer but
// we'll write 16 at a time.
#define MAX_I2C_WRITE 16
// This address is determined by the way your address pins are wired.
// In the diagram from earlier, we connected A0 and A1 to Ground and
// A2 to 5V. To get the address, we start with the control code from
// the datasheet (1010) and add the logic state for each address pin
// in the order A2, A1, A0 (100) which gives us 0b1010100, or in
// Hexadecimal, 0x54.
const byte eeprom_address= 0x54;

## Slide 109: Arduino code for EEprom
// Read
byte readEEProm(uint32_t address) {
Wire.beginTransmission(eeprom_address);
Wire.write((int) (address >> 8)); // MSB
Wire.write((int) (address & 0xff)); // LSB
Wire.endTransmission();
Wire.requestFrom(eeprom_address, 1);
byte r = 0xff;
if (Wire.available())
r= Wire.read();
return r;
}
// Write
void writeEEProm(uint32_t address, byte* data, int size) {
Wire.beginTransmission(eeprom_address);
Wire.write((int) (address >> 8)); // MSB
Wire.write((int) (address & 0xff)); // LSB
for (byte b = 0; b < size; b++)
Wire.write(data[b]);
Wire.endTransmission();
}

## Slide 110: Arduino code for EEprom
void printHexByte(byte b) {
if (b < 16)
Serial.print("0");
Serial.print(b, HEX);
}
int readStream(byte* buf, int max) {
int num_bytes = 0;
for(;;) {
while(Serial.available()) {
if (num_bytes >= max)
return num_bytes;
}
buf[num_bytes++] = Serial.read();
}
return num_bytes;
}
int initBuf(byte* buf, int max) {
int i = 0;
for (i = 0; i < 64; i++)
buf[i] = (byte) (i + 16);
return i;
}

## Slide 111: Arduino code for EEprom
void printBytes(byte* buf, int n) {
for (int i = 0; i < n; i++) {
printHexByte(buf[i]);
Serial.print(" ");
if ((i%16) ==15)
Serial.println("");
}
}
uint32_t end_address= 0x40; //0x7d00;
void setup() {
Serial.begin(9600);
Wire.begin();
Wire.setClock(initial_clock_setting);
byte to_write[MAX_BYTES];
int current = 0;
int num_bytes= initBuf(to_write, MAX_BYTES);
int num_left= num_bytes;
int n;
Serial.println("Bytes accepted:");
printBytes(to_write, num_bytes);
Serial.println("");

## Slide 112: Arduino code for EEprom
while(num_left > 0) {
if (num_left >= MAX_I2C_WRITE)
n = MAX_I2C_WRITE;
else
n = num_left;
writeEEProm(current, &to_write[current], n);
num_left -= n;
current += n;
}
Serial.println("Bytes written");
Serial.println("");
// Read bytes to end_address
Serial.println("Bytes read:");
byte v;
for (uint32_t a = 0; a < end_address; a++) {
v= readEEProm(a);
printHexByte(v);
if ((a%16) ==15)
Serial.println("");
}
}
void loop() {
}

## Slide 113: EEprom Raspberry pi
We could simulate the I2C interface as we did with the Arduino but the Raspberry Pi has some utilities you can use instead.
  I2cdetect – detects I2C devices connected to the RP
  I2cdump – reads I2C registers
  I2cget – reads specific I2C registers
  I2cset – sets specific I2C registers
If you wire the 24FC515 just as in the Arduino case but with Vcc to RP 3.3 (pin 1), gnd to RP gnd (pin 6), sda to RP sda (pin 3) and scl to RP scl (pin 5), for example, the following command will read out the ROM. Try it on a ROM you’ve initialized with the Arduino.
  i2cdump "bcm2835 I2C adapter" 0x54

## Slide 114: GPS
For general information on GPS, see my “Electronics of Radio” Notes.
  Accuracy for C/A: 5 meters. 3 meters with WAAS
  Four sats for latitude, longitude, elevation, and time.
The following are datasheets and command sets for some of the more common chipsets. UBLOX has a chipset
  SiRF NMEA Reference Manual
  SiRF Binary Reference Manual
Serial data out of a transmit pin (TX) usually at 9600bps for 1Hz receivers but 57600bps is also common.
Channels affect time to first fix (TTFF) when 4 sats are in view.
NMEA is output data format that most GPS modules use.
  $GPRMC,235316.000,A,4003.9040,N,10512.5792,W,0.09,144.75,141112,,*19
  $GPGGA,235317.000,4003.9039,N,10512.5793,W,1,08,1.6,1577.9,M,-20.7,M,,0000*5F (time[23:53 16.0GMT], long [40.30], lat [105.12W], sats [8], alt [1577.9 meters])
  $GPGSA,A,3,22,18,21,06,03,09,24,15,,,,,2.5,1.6,1.9*3E
PPS is an output pin indicating you can synchronize your system clock to the GPS clock.
Cold start requires downloading new almanac and ephemeris data.
UAVs and other fast vehicles may require increased update rates. 5 and even 10Hz .

## Slide 115: Lab: GPS
The ATGM336H-5N GNSS module receives GPS signals and communicates through a UART interface.
  Cold start - Recapture sensitivity：-148dBm
  Tracking sensitivity：-162dBm
  Positioning Precision：2.5m（CEP50）
  The Time To First Fix:：32s
GPS code follows. The GPS module communicates over a simple serial line implemented by SoftwareSerial in the Arduino libraries.
The module uses the “NEMA message format” that reports UTC time, latitude, and longitude.
A NEMA message report for Boston is (42.361732,N,071.090595,W)is:
  $GNRMC,005536.000,A,4236.1732,N,07109.0595,W,0.00,0.00,230218,,,A*68
Arduino
3.3V
Gnd
A5
ATGM336H
Vcc
Gnd (4)
TX
A3
RX
115

## Slide 116: Arduino code for GPS
// GPS
// Manferdelli
#include <SoftwareSerial.h>
#include <Adafruit_GPS.h>
#ifndef byte
typedef uint8_t byte;
#endif
const int gpsReceivePin= 3;
const int gpsTransmitPin= 5;
const int messageDelay= 500;
// Note: GPS transmit pin is SoftwareSerial receive pin and vice-versa
SoftwareSerial serialGPS = SoftwareSerial(gpsTransmitPin, gpsReceivePin);
Adafruit_GPS GPS(&serialGPS);
void setup() {
Serial.begin(9600);
GPS.begin(9600);
GPS.sendCommand(PMTK_SET_NMEA_OUTPUT_RMCGGA);
GPS.sendCommand(PMTK_SET_NMEA_UPDATE_1HZ);
GPS.sendCommand(PGCMD_ANTENNA);
}

## Slide 117: Arduino code for GPS
void printTwoDigitInt(int x) {
if (x < 10)
Serial.print("0");
Serial.print(x);
}
void printTwoDigitDouble(double x) {
if (x < 10.0)
Serial.print("0");
Serial.print(x);
}
struct gpm_msg_values {
int hour_;
int min_;
double seconds_;
double degrees_lat_;
double degrees_long_;
int num_sats_;
};
// s: string to match, t: message string
char* strmatch(const char* s, char* t) {
for (;;) {
if (*s == 0 || *t == 0)
return NULL;
if (*s != *t)
return NULL;
s++; t++;
if (*s == 0)
return t;
}
}
char* find_string_in_msg(const char* str, char* msg) {
int l = strlen(msg);
char* s = NULL;
for (int i = 0; i < l; i++) {
s = strmatch(str, &msg[i]);
if (s != NULL)
return s;
}
return NULL;
}

## Slide 118: Arduino code for GPS
// NMEA message format
// $GNGGA,HHMMSS.SSS,DDMM.MMMM,N/S,DDDMM.MMMM,E/W,n,NS...A*20
bool parseNMEAMessage(char* msg, struct gpm_msg_values* v) {
char* time_string = find_string_in_msg("$GNGGA,", msg);
if (time_string == NULL)
return false;
sscanf(time_string, "%02d%02d", &v->hour_, &v->min_);
sscanf(time_string+4, "%f", &v->seconds_);
char* latitude_string = find_string_in_msg(",", time_string);
if (latitude_string == NULL)
return false;
int deglat;
int mlat;
int minlat;
sscanf(latitude_string, "%02d%02d.%04d", &deglat, &mlat, &minlat);
v->degrees_lat_ = ((double)deglat) + (((double)mlat) + ((double)minlat) / 10000.0) / 60.0;
char* ns_string = find_string_in_msg(",", latitude_string);
if (ns_string == NULL || (*ns_string != 'N' && *ns_string != 'S'))
return false;
if (*ns_string == 'S')
v->degrees_lat_ *= -1.0;

## Slide 119: Arduino code for GPS
char* longitude_string = ns_string + 2;
int deglong;
int mlong;
int minlong;
sscanf(longitude_string, "%03d%02d.04d", &deglong, &mlong, &minlong);
v->degrees_long_ = ((double)deglong) + (((double)mlong) + ((double)minlong)/ 10000.0) / 60.0;
char* ew_string = find_string_in_msg(",", longitude_string);
if (ew_string == NULL || (*ew_string != 'E' && *ew_string != 'W'))
return false;
if (*ew_string == 'W')
v->degrees_long_ *= -1.0;
return true;
}
void loop() {
gpm_msg_values out;
bool got_fix = false;

## Slide 120: Arduino code for GPS
while (!got_fix) {
for(;;) {
char c = GPS.read(); // causes the message to be read
if (GPS.newNMEAreceived())
break;
}
got_fix = parseNMEAMessage(GPS.lastNMEA(), &out);
if (got_fix) {
Serial.print("Time: ");
printTwoDigitInt(out.hour_);
Serial.print(":");
printTwoDigitInt(out.min_);
Serial.print(":");
printTwoDigitDouble(out.seconds_);
Serial.print(" GMT, ");
Serial.print("Position: ");
Serial.print(out.degrees_lat_);
Serial.print(" degrees latitude, ");
Serial.print(out.degrees_long_);
Serial.print(" degrees longitude");
Serial.println();
}
}
delay(messageDelay);
}

## Slide 121: Lab: Connect a Linux machine to a GPS sensor
We’ll first connect a Linux machine, from the USB port on the Linux machine, to an FDTI1232 and connect the FDTI-1232 to the GPS sensor.
  GPS module FDTI1232
  gnd gnd
  vcc vcc
  RX (configure) TX
  TX RX
You can also connect using the USB ports in the same way Raspberry Pi, well do that next.

## Slide 122: Linux code for GPS
#include <stdio.h>
#include <unistd.h>
#include <fcntl.h>
#include <termios.h>
#include <string.h>
#ifndef byte
typedef unsigned char byte;
#endif
#define uartDevice "/dev/ttyUSB0"
#define BUF_SIZE 512
void clearBuf(byte* buf, int n) {
for (int i = 0; i < n; i++) {
buf[i] = 0;
}
}
const char* eol = "\r\n";
void sendCommand(int fd, const char* command) {
write(fd, command, strlen(command));
write(fd, eol, 2);
}

## Slide 123: Linux code for GPS
#define PMTK_SET_NMEA_OUTPUT_RMCGGA "$PMTK314,0,1,0,1,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0*28"
#define PMTK_SET_NMEA_UPDATE_1HZ "$PMTK220,1000*1F"
#define PGCMD_ANTENNA "$PGCMD,33,1*6C"
void setup_gps(int fd) {
sendCommand(fd, PMTK_SET_NMEA_OUTPUT_RMCGGA);
sleep(1);
sendCommand(fd, PMTK_SET_NMEA_UPDATE_1HZ);
sleep(1);
sendCommand(fd, PGCMD_ANTENNA);
sleep(1);
}
// s: string to match, t: message string
char* strmatch(const char* s, char* t) {
for (;;) {
if (*s == 0 || *t == 0)
return NULL;
if (*s != *t)
return NULL;
s++; t++;
if (*s == 0)
return t;
}
}

## Slide 124: Linux code for GPS
char* find_string_in_msg(const char* str, char* msg) {
int l = strlen(msg);
char* s = NULL;
for (int i = 0; i < l; i++) {
s = strmatch(str, &msg[i]);
if (s != NULL)
return s;
}
return NULL;
}
// GPS value structure
struct gpm_msg_values {
int hour_;
int min_;
double seconds_;
double degrees_lat_;
double degrees_long_;
int num_sats_;
};
return 0;
}

## Slide 125: Linux code for GPS
// NMEA message format
// $GNGGA,HHMMSS.SSS,DDMM.MMMM,N/S,DDDMM.MMMM,E/W,n,NS...A*20
bool parseNMEAMessage(char* msg, struct gpm_msg_values* v) {
char* time_string = find_string_in_msg("$GNGGA,", msg);
if (time_string == NULL)
return false;
sscanf(time_string, "%02d%02d", &v->hour_, &v->min_);
sscanf(time_string+4, "%lf", &v->seconds_);
char* latitude_string = find_string_in_msg(",", time_string);
if (latitude_string == NULL)
return false;
int deglat;
int mlat;
int minlat;
sscanf(latitude_string, "%02d%02d.%04d", &deglat, &mlat, &minlat);
v->degrees_lat_ = ((double)deglat) + (((double)mlat) + ((double)minlat) / 10000.0) / 60.0;
char* ns_string = find_string_in_msg(",", latitude_string);
if (ns_string == NULL || (*ns_string != 'N' && *ns_string != 'S'))
return false;
if (*ns_string == 'S')
v->degrees_lat_ *= -1.0;
char* longitude_string = ns_string + 2;

## Slide 126: Linux code for GPS
int deglong;
int mlong;
int minlong;
sscanf(longitude_string, "%03d%02d.%04d", &deglong, &mlong, &minlong);
v->degrees_long_ = ((double)deglong) + (((double)mlong) + ((double)minlong)
/ 10000.0) / 60.0;
char* ew_string = find_string_in_msg(",", longitude_string);
if (ew_string == NULL || (*ew_string != 'E' && *ew_string != 'W'))
return false;
if (*ew_string == 'W')
v->degrees_long_ *= -1.0;
return true;
}
bool get_location(int fd) {
gpm_msg_values out;
bool got_fix = false;
byte buf[BUF_SIZE];
int n;
int msg_count = 1;

## Slide 127: Linux code for GPS
while (!got_fix) {
sleep(2);
clearBuf(buf, BUF_SIZE);
n = read(fd, buf, BUF_SIZE - 1);
if (n <= 0) {
printf("read returns %d\n", n);
continue;
}
buf[n++] = 0;
if (n > 2)
printf("Message %d: %s", msg_count++, (char*) buf);
got_fix = parseNMEAMessage((char*)buf, &out);
if (got_fix) {
printf("Time: %02d:%02d:%07.4f GMT, ", out.hour_, out.min_, out.seconds_);
printf("Position: %8.5f (lat), %8.5f (long)\n", out.degrees_lat_, out.degrees_long_);
return true;
}
}
return false;
}

## Slide 128: Linux code for GPS
int main(int an, char** av) {
int baudRate = 9600;
int fd = open(uartDevice, O_RDWR | O_NOCTTY | O_NDELAY);
if (fd < 0) {
printf("Can't open %s\n", uartDevice);
return 1;
}
// setup gps sensor and get location
setup_gps(fd);
for (int i = 0; i < 10; i++) {
get_location(fd);
printf("\n");
}
close(fd);
return 0;
}

## Slide 129: Lab: RP GPS
We can also use the code above on the Raspberry Pi to connect to a GPS sensor from a USB port on the RP. If you want to use the mini-USB port, you need to use “/dev/serial0.”

## Slide 130: Lab: UART from Raspberry Pi interface
Finally, we can connect from the Raspberry Pi Tx (pin 8) and Rx (pin 10) pins directly to the GPS sensor.
First, you’ll have to enable the RP pins RX/TX pins by adding (or editing) a line in /boot/config.txt.
We need to open the native RP UART device, /dev/ttyS0.
UARTs are important. We’ll use this for GPS and HC-12.

## Slide 131: Raspberry Pi code for UART (GPS)
// GPS Interfacing with Raspberry Pi using C (WiringPi Library)
// Raspberry Pi GPS
// 3.3V (GPIO Pin 1) VCC
// GND (GPIO Pin 6) GND
// TXD (GPIO Pin 8) RXD
// RXD (GPIO Pin 10) TXD
#define uartDevice "/dev/ttyS0”
#define BUF_SIZE 512
const int messageDelay = 50;
void clearBuf(byte* buf, int n) {
for (int i = 0; i < n; i++) {
buf[i] = 0;
}
}
ATGM336H
TX
RX
Vcc
trigger
echo
gnd
Raspberry Pi
3.3 V, HDR pin 1
Vcc
Gnd
GPIO15 (TX)
HDR pin 8
GPIO16 (RX)
HDR pin 10
Gnd, HDR pin 6

## Slide 132: Raspberry Pi code for GPS
const char* eol = "\r\n";
void sendCommand(int fd, const char* command) {
for (int i = 0; i < strlen(command); i++)
serialPutchar(fd, command[i]);
serialPutchar(fd, eol[0]);
serialPutchar(fd, eol[1]);
}
#define PMTK_SET_NMEA_OUTPUT_RMCGGA "$PMTK314,0,1,0,1,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0*28"
#define PMTK_SET_NMEA_UPDATE_1HZ "$PMTK220,1000*1F"
#define PGCMD_ANTENNA "$PGCMD,33,1*6C"
void setup_gps(int fd) {
sendCommand(fd, PMTK_SET_NMEA_OUTPUT_RMCGGA);
sendCommand(fd, PMTK_SET_NMEA_UPDATE_1HZ);
sendCommand(fd, PGCMD_ANTENNA);
}

## Slide 133: Raspberry Pi code for GPS
// s: string to match
// t: message string
char* strmatch(const char* s, char* t) {
for (;;) {
if (*s == 0 || *t == 0)
return NULL;
if (*s != *t)
return NULL;
s++; t++;
if (*s == 0)
return t;
}
}
char* find_string_in_msg(const char* str, char* msg) {
int l = strlen(msg);
char* s = NULL;
for (int i = 0; i < l; i++) {
s = strmatch(str, &msg[i]);
if (s != NULL)
return s;
}
return NULL;
}
// GPS value structure
struct gpm_msg_values {
int hour_;
int min_;
double seconds_;
double degrees_lat_;
double degrees_long_;
int num_sats_;
};

## Slide 134: Raspberry Pi code for GPS
// NMEA message format
// $GNGGA,HHMMSS.SSS,DDMM.MMMM,N/S,DDDMM.MMMM,E/W,n,NS...A*20
bool parseNMEAMessage(char* msg, struct gpm_msg_values* v) {
char* time_string = find_string_in_msg("$GNGGA,", msg);
if (time_string == NULL)
return false;
sscanf(time_string, "%02d%02d", &v->hour_, &v->min_);
sscanf(time_string+4, "%f", &v->seconds_);
char* latitude_string = find_string_in_msg(",", time_string);
if (latitude_string == NULL)
return false;
int deglat;
int mlat;
int minlat;
sscanf(latitude_string, "%02d%02d.%04d", &deglat, &mlat, &minlat);
v->degrees_lat_ = ((double)deglat) + (((double)mlat) + ((double)minlat) / 10000.0) / 60.0;
char* ns_string = find_string_in_msg(",", latitude_string);
if (ns_string == NULL || (*ns_string != 'N' && *ns_string != 'S'))
return false;
if (*ns_string == 'S')
v->degrees_lat_ *= -1.0;
char* longitude_string = ns_string + 2;

## Slide 135: Raspberry Pi code for GPS
int deglong, mlong, minlong;
sscanf(longitude_string, "%03d%02d.04d", &deglong, &mlong, &minlong);
v->degrees_long_ = ((double)deglong) + (((double)mlong) + ((double)minlong)/ 10000.0) / 60.0;
char* ew_string = find_string_in_msg(",", longitude_string);
if (ew_string == NULL || (*ew_string != 'E' && *ew_string != 'W'))
return false;
if (*ew_string == 'W')
v->degrees_long_ *= -1.0;
return true;
}
int read_serial_line(int fd, byte* buf, int size) {
int r;
int n = 0;
while (n < (size - 1)) {
r = serialGetchar(fd);
buf[n++] = r;
if (r == '\n') {
buf[n++] = 0;
return n;
}
}
return -1;
}

## Slide 136: Raspberry Pi code for GPS
bool get_location(int fd) {
gpm_msg_values out;
bool got_fix = false;
byte buf[BUF_SIZE];
int n;
while (!got_fix) {
clearBuf(buf, BUF_SIZE);
n = read_serial_line(fd, buf, BUF_SIZE);
if (n < 0) {
continue;
}
got_fix = parseNMEAMessage((char*)buf, &out);
if (got_fix) {
printf("Time: %02d:%02d:%07.4f GMT, ", out.hour_, out.min_, out.seconds_);
printf("Position: %8.5f (lat), %8.5f (long)\n", out.degrees_lat_, out.degrees_long_);
return true;
}
delay(messageDelay);
}
return false;
}

## Slide 137: Raspberry Pi code for GPS
int main(int an, char** av) {
int baudRate = 9600;
// Initialize wiringPi
if (wiringPiSetup() < 0) {
printf("wiringPiSetup failed\n");
return 0;
}
// Open the serial device
int fd = serialOpen(uartDevice, baudRate);
if (fd < 0) {
printf("Can't open serialDevice\n");
return 1;
}
// setup gps sensor and get location
setup_gps(fd);
get_location(fd);
close(fd);
return 0;
}

## Slide 138: Raspberry Pi code to SPI bus
To connect to SPI, use the following connections
SPI bus
MISO
MOSI
Vcc
trigger
echo
gnd
Raspberry Pi
3.3 V, HDR pin 1
Vcc
Gnd
GPIO 12
HDR pin 19
GPIO 13
HDR pin 21
Gnd, HDR pin 6
GPIO 11 (CE1)
HDR pin 26
SS (select)
SCLK
GPIO14
HDR pin 23

## Slide 139: Raspberry Pi code for SPI
// Manferdelli
// Raspberry Pi SPI
#include <stdio.h>
#include <stdlib.h>
#include <stdint.h>
#include <wiringPiSPI.h>
#ifndef byte
typedef unsigned char byte;
#endif
const int chip_select = 1;
const int bus_speed = 50000;
#define BUF_SIZE 128
// RP SPI connections
// RP SPI
// Gnd Gnd
// 3.3V Vcc
// CE1 SS (shift select)
// SCK SCK
// MOSI SDI
// MISO SDO

## Slide 140: Raspberry Pi code for SPI
int main(int an, char** av) {
int fd = wiringPiSPISetup(chip_select, bus_speed);
if (fd < 0) {
printf("Can't initialize SPI interface\n");
return 1;
}
int result;
byte buf[BUF_SIZE];
// clear display
buf[0] = 0x76;
result = wiringPiSPIDataRW(chip_select, buf, 1);
if (result < 0) {
printf("Initial clear failed\n");
}
sleep(5);
// Are we addressing all segments
for (int i = 1; i <= 0x7f; i++) {

## Slide 141: Raspberry Pi code for SPI
buf[0] = 0x77;
buf[1] = i;
result = wiringPiSPIDataRW(chip_select, buf, 2);
if (result < 0) {
printf("First R/W failed\n");
}
buf[0] = 0x7b;
buf[1] = i;
result = wiringPiSPIDataRW(chip_select, buf, 2);
if (result < 0) {
printf("Second R/W failed\n");
}
buf[0] = 0x7c;
buf[1] = i;
result = wiringPiSPIDataRW(chip_select, buf, 2);
if (result < 0) {
printf("Third R/W failed\n");
}
buf[0] = 0x7d;
buf[1] = i;
result = wiringPiSPIDataRW(chip_select, buf, 2);
if (result < 0) {
printf("Fourth R/W failed\n");
}

## Slide 142: Raspberry Pi code for SPI
buf[0] = 0x7e;
buf[1] = i;
result = wiringPiSPIDataRW(chip_select, buf, 2);
if (result < 0) {
printf("Fifth R/W failed\n");
}
sleep(5);
}
// clear display
buf[0] = 0x76;
result = wiringPiSPIDataRW(chip_select, buf, 1);
if (result < 0) {
printf("Final clear failed\n");
}
return 0;
}

## Slide 143: Lab: TFT Screen
Here we describe the HiLetgo 2.4 Inch TFT LCD Display Shield Touch Panel ILI9341 240X320
The TFT module uses the SPI interface. Its data sheet is here, and a supporting library is here.
Include Adafruit_GFX.h and Adafruit_TFTLCD.h libraries. Connections (use 5v for power).
  A0 RD
  A1 WR
  A2 RS
  A3CS
  A4RST
  D8D0
  D9D1
  D2 D2
  D3D3
  …
  D7D7
143
Amazon

## Slide 144: Arduino code for TFT
144
#include <Adafruit_GFX.h>
#include <Adafruit_TFTLCD.h>
#include <TouchScreen.h>
#define LCD_CS A3 // Chip Select goes to Analog 3
#define LCD_CD A2 // Command/Data goes to Analog 2
#define LCD_WR A1 // LCD Write goes to Analog 1
#define LCD_RD A0 // LCD Read goes to Analog 0
#define LCD_RESET A4
#define BLUE 0x001F
#define WHITE 0xFFFF
Adafruit_TFTLCD tft(LCD_CS, LCD_CD, LCD_WR, LCD_RD, LCD_RESET);
void setup() {
Serial.begin(9600);
Serial.println("Starting...");
tft.begin(0x9341); // SDFP5408
}
void loop() {
int k = 0;
tft.fillScreen(WHITE);
tft.setCursor(0, 2);
tft.setTextColor(BLUE);
tft.setTextSize(2);
tft.println("hello world %d", k++);
delay(2000);
}

## Slide 145: Lab: Measure pressure
We will use the GY-65 (or GY-68) to measure pressure, you can find the datasheet with pictures here. I’ve found a newer version is more accurate. See here.
The Bosch barometer is very accurate and gives both temperature and pressure.
You can use the pressure to calculate the altitude of the sensor. The details are explained in the datasheet. This could come in useful if you’re in a plane.
The sensor uses an I2C interface and each sensor comes with its own calibration data.
Wire the Arduino as shown.
Arduino
3.3 V
Gnd
A5
GY-65
Vcc
SDA
SDL
Gnd
A4

## Slide 146: Arduino code for measure pressure
// gy-65 altitude, pressure, temp
// Manferdelli, Reference: https://www.sparkfun.com/tutorials/253
#include <Wire.h>
typedef uint8_t byte;
const int dataPin= 8;
const int measurementDelay= 500;
const int i2c_address= 0x77;
const int tempDelay= 5;
struct calibration_data {
int16_t ac1_;
int16_t ac2_;
int16_t ac3_;
uint16_t ac4_;
uint16_t ac5_;
uint16_t ac6_;
int16_t b1_;
int16_t b2_;
int16_t mb_;
int16_t mc_;
int16_t md_;
// temps
long b5_;
};

## Slide 147: Arduino code for measure pressure
int16_t swap_bytes(int16_t in) {
return ((in << 8) & 0xff00) | ((in >> 8) & 0x00ff);
}
int read_i2c(byte r, byte* buf, int size) {
Wire.beginTransmission(i2c_address);
Wire.write(r);
Wire.endTransmission(false);
Wire.requestFrom(i2c_address, size, true);
int i= 0;
while (Wire.available() && i < size) {
buf[i++]= Wire.read();
}
return i;
}
byte read_i2c_byte(byte r) {
Wire.beginTransmission(i2c_address);
Wire.write(r);
Wire.endTransmission(false);
Wire.requestFrom(i2c_address, 1, true);
if (Wire.available()) {
return Wire.read();
}
}

## Slide 148: Arduino code for measure pressure
void write_i2c(byte r, byte d) {
Wire.beginTransmission(i2c_address);
Wire.write(r);
Wire.write(d);
delay(tempDelay);
Wire.endTransmission(true);
}
int read_i2c_int(byte address) {
int16_t d;
read_i2c(address, (byte*)&d, sizeof(int16_t));
d = swap_bytes(d);
return d;
}
const double pressure_at_sea_level= 101325.0; // Pa
void calibrate(calibration_data* d) {
read_i2c(0xaa, (byte*)d, sizeof(calibration_data));
int16_t* ip = (int16_t*)d;
for (int i = 0; i < 16; i++) {
ip[i]= swap_bytes(ip[i]);
}
}

## Slide 149: Arduino code for measure pressure
double calculate_altitude(long pressure) {
double normalizedP= ((double)pressure)/ pressure_at_sea_level;
double a = (1.0 - pow(normalizedP, 1 / 5.255)) * 44330.0;
return a;
}
const long OSS = 1;
long calculate_real_temperature(calibration_data& cd, long raw) {
long x1 = ((raw - ((long)cd.ac6_)) * ((long)cd.ac5_)) >> 15;
long x2 = (((long)cd.mc_) << 11) / (x1 + ((long)cd.md_));
cd.b5_ = x1 + x2;
long t = (cd.b5_ + 8) >> 4;
Serial.println("");
Serial.println("Real temperature");
Serial.print("x1: ");
Serial.println(x1);
Serial.print("x2: ");
Serial.println(x2);
Serial.print("b5: ");
Serial.println(cd.b5_);
return t / 10;
}

## Slide 150: Arduino code for measure pressure
long calculate_real_pressure(calibration_data& cd, long raw) {
long p;
long b6 = cd.b5_ - 4000;
long x1 = (((long)cd.b2_) * ((b6 * b6) >> 12)) >> 11;
long x2 = (((long)cd.ac2_) * b6) >> 11;
long x3 = x1 + x2;
long b3 = (((((long)cd.ac1_) * 4 + x3) << OSS) + 2) / 4;
x1= (((long)cd.ac3_) * b6) >> 13;
x2 = (((long)cd.b1_) * ((b6 * b6) >> 12)) >> 16;
x3 = (x1 + x2 + 2) / 4;
long b4 = (((long)cd.ac4_) * (x3 + 32768)) >> 15;
long b7 = (raw - b3) * (50000 >> OSS);
if (b7 < 0x80000000UL)
p = (b7 * 2) / b4;
else
p = (b7 / b4) * 2;
x1 = (p >> 8) * (p >> 8);
x1 = (x1 * 3038) >> 16;
x2 = (-7357 * p) >> 16;
p += (x1 + x2 + 3791) >> 4;
return p;
}

## Slide 151: Arduino code for measure pressure
long raw_temperature() {
write_i2c(0xf4, 0x2e);
delay(tempDelay);
long t = read_i2c_int(0xf6);
return t;
}
long raw_pressure() {
write_i2c(0xf4, 0x2e);
delay(tempDelay);
byte msb= read_i2c_byte(0xf6);
byte lsb1= read_i2c_byte(0xf7);
byte lsb2= read_i2c_byte(0xf8);
long rp = ((((long)msb) << 16) + (((long)lsb1) << 8) + ((long)lsb2)) >> (8 - OSS);
return rp;
}
long get_temperature(calibration_data& cd) {
long rt= raw_temperature();
Serial.print("Raw temperature: ");
Serial.print(rt);
Serial.println("");
return calculate_real_temperature(cd, rt);
}

## Slide 152: Arduino code for measure pressure
long raw_temperature() {
write_i2c(0xf4, 0x2e);
delay(tempDelay);
long t = read_i2c_int(0xf6);
return t;
}
long raw_pressure() {
write_i2c(0xf4, 0x2e);
delay(tempDelay);
byte msb= read_i2c_byte(0xf6);
byte lsb1= read_i2c_byte(0xf7);
byte lsb2= read_i2c_byte(0xf8);
long rp = ((((long)msb) << 16) + (((long)lsb1) << 8) + ((long)lsb2)) >> (8 - OSS);
return rp;
}
long get_temperature(calibration_data& cd) {
long rt= raw_temperature();
Serial.print("Raw temperature: ");
Serial.print(rt);
Serial.println("");
return calculate_real_temperature(cd, rt);
}

## Slide 153: Arduino code for measure pressure
long get_pressure(calibration_data& cd) {
long rp = raw_pressure();
long p = calculate_real_pressure(cd, rp);
return p;
}
void setup() {
Serial.begin(9600);
Wire.begin();
}

## Slide 154: Arduino code for measure pressure
void loop() {
calibration_data cd;
calibrate(&cd);
printCalibration(cd);
double temperature= (double)get_temperature(cd);
double pressure= (double)get_pressure(cd);
double altitude= calculate_altitude(pressure);
Serial.print("Temperature (C): ");
Serial.print(temperature);
Serial.print(", pressure (Pa): ");
Serial.print(pressure);
Serial.print(", altitude (m): ");
Serial.print(altitude);
Serial.println("");
delay(measurementDelay);
}

## Slide 155: Raspberry Pi code for measure pressure (bmp280)
You can download a support library for the Bosch BMP-280 but I had trouble getting it to work. For one thing, when I ordered one, I got a different chip, the “BME-280,” which is electrically identical but has a humidity sensor. It has a chip id the library doesn’t recognize. Some BMP-280’s are labeled BME-280’s.
I ended up writing my own interface library which is included in the Lab directories.
The connections from the Raspberry Pi are the usual SDA, SCL pins (HDR 3, 5). Vcc should be 3.3 volts, not 5v.

## Slide 156: Bmp-280 output
chip id: 60
Calibration data:
t1: 6f11, t2: 68c9, t3: 32
p1: 9322, p2: ffffd694, p3: bd0
p4: 15f9, p5: 32, p6: fffffff9, p7: 0x02 fine: 00 get CNTRL: 00, MEAS: 00 Config data before init: standby: 00, mode: 00filter: 00, odr: 08 samp_temp: 00, samp_press: 00 Config data after init standby: 04, mode: 03 filter: 03, odr: 05 samp_temp: 04, samp_press: 04 set CNTRL: 93, MEAS: 8c get CNTRL: 93, MEAS: 8c Configuration data after set: standby: 04, mode: 03 filter: 04, odr: 05 samp_temp: 04, samp_press: 04
Sea level pressure: 1018.0000 (Pa)
uncompensated temperature reading: 523358, 0x7fc5e uncompensated pressure reading: 344664, 0x54258 Temperature: 21.89 (C), pressure: 1015.3782 (Pa), alt: 21.7491 (m)
uncompensated temperature reading: 523374, 0x7fc6e uncompensated pressure reading: 344662, 0x54256 Temperature: 21.89 (C), pressure: 1015.3846 (Pa), alt: 21.6958 (m)
uncompensated temperature reading: 523387, 0x7fc7b uncompensated pressure reading: 344663, 0x54257 Temperature: 21.90 (C), pressure: 1015.3782 (Pa), alt: 21.7491 (m)

## Slide 157: Lab: Hall Sensor
A Hall sensor measures magnetic fields. In the configuration below, when a magnetic field of the right polarity is present, the out terminal will go to ground.
You can find a tutorial and pictures here.
Wire the Arduino as shown. Code follows.
Arduino
5 V
Gnd
A0
Hall sensor
Vcc
Gnd
out
10K
Maker

## Slide 158: Arduino code for Hall sensor
// Hall sensor
// Manferdelli
typedef uint8_t byte;
const int dataPin= A0;
const int measurementDelay= 500;
void setup() {
Serial.begin(9600);
pinMode(dataPin, INPUT);
}
const int zero_field= 527;
void loop() {
int field_strength= analogRead(dataPin);
Serial.print("Field: ");
Serial.print(field_strength);
int calibrated_field = field_strength - zero_field;
Serial.print(", calibrated field: ");
Serial.print(calibrated_field);
Serial.println("");
delay(measurementDelay);
}

## Slide 159: Raspberry Pi code for Hall sensor
Use PCF8591 ADC and I2C interface described earlier.
// Manferdelli
// Raspberry Pi read hall sensor
#include <stdio.h>
#include <wiringPi.h>
#include <pcf8591.h>
const int base = 120;
const int i2c_address = 0x48;
// const int zero_field = 527;
const int zero_field = 7; //this is better for 3.3v
const int measurement_delay = 500;
// PCF Connections
// PCF RP
// 1(ain0) analog-signal
// 5, 6, 7, 8 gnd (pin 6)
// 16 3.3 (pin 1)
// 14 3.3v
// 13 gnd
// 12 gnd
// 10(scl) 5 (scl)
// 9(sda) 3 (sda)
int main(int an, char** av) {
int strength = 0;
if (wiringPiSetup() < 0) {
printf("Can't initialize wiringPi\n");
return 1;
}
pcf8591Setup(base, i2c_address);
for(;;) {
strength = analogRead(base);
int calibrated_strength = strength - zero_field;
printf("Strength: %d, calibrated measurement: %d\n",
strength, calibrated_strength);
delay(measurement_delay);
}
return 0;
}

## Slide 160: Lab: Vibration sensor
You can find pictures of the vibration sensor and a tutorial here. The vibration sensor is a switch that is normally off, vibration causes it to conduct.
Wire the vibration sensor and the Arduino as shown.
Arduino
5 V
Gnd
Vibration sensor
Vcc
Gnd
D8
out
Freenove

## Slide 161: Arduino code for vibration
// Vibration
// Manferdelli
typedef uint8_t byte;
const int dataPin= 2;
const int measurementDelay= 20;
volatile int state = -1;
void trigger() {
state= 1;
}
void setup() {
Serial.begin(9600);
attachInterrupt(dataPin, trigger, RISING);
}
void loop() {
if (state == 1) {
Serial.println("Vibration detected");
delay(1);
state= 0;
}
delay(measurementDelay);
}

## Slide 162: Lab: Tilt sensor
You can find pictures of the tilt sensor and a tutorial here. The resistance of the tilt sensor increases with the angle of inclination from level. You can test this with a meter.
Wire the tilt sensor and the Arduino as shown.
Arduino
5 V
Gnd
Tilt sensor
Vcc
Gnd
D2
out

## Slide 163: Arduino code for Tilt sensor
// Tilt
// Manferdelli
typedef uint8_t byte;
const int dataPin= 8;
const int measurementDelay= 500;
void setup() {
Serial.begin(9600);
pinMode(dataPin, INPUT);
digitalWrite(dataPin, HIGH); // Why?
}
void loop() {
int tilted= digitalRead(dataPin);
Serial.println("");
if (tilted == 0) {
Serial.println("Tilted");
} else {
Serial.println("Not tilted");
}
delay(measurementDelay);
}

## Slide 164: Lab: LCD-1602 display
You can find pictures of the display and a tutorial in the Freenove manual here. We wire it directly but you can also buy LCD-1602 modules with I2C interfaces which saves lots of pins.
The LCD 1602 display wiring is complicated, so we don’t do it graphically.
  LCD RS pin to digital pin 12
  LCD Enable pin to digital pin 11
  LCD D4 pin to digital pin 5
  LCD D5 pin to digital pin 4
  LCD D6 pin to digital pin 3
  LCD D7 pin to digital pin 2
  LCD R/W pin to ground
  LCD VSS pin to ground
  LCD VCC pin to 5V
  10K resistor: ends to +5V and ground
  wiper to LCD VO pin (pin 3)

## Slide 165: Arduino code for LCD display
// LCD display
// Manferdelli
#include <LiquidCrystal.h>
typedef uint8_t byte;
// 16x2 LCD display. The LiquidCrystal library works with all LCD displays
// that are compatible with the Hitachi HD44780 driver.
// LCD RS pin to digital pin 12
// LCD Enable pin to digital pin 11
// LCD D4 pin to digital pin 5
// LCD D5 pin to digital pin 4
// LCD D6 pin to digital pin 3
// LCD D7 pin to digital pin 2
// LCD R/W pin to ground
// LCD VSS pin to ground
// LCD VCC pin to 5V
// 10K resistor: ends to +5V and ground
// wiper to LCD VO pin (pin 3)
// See: http://www.arduino.cc/en/Tutorial/LiquidCrystalHelloWorld
const int rs = 12, en = 11, d4 = 5, d5 = 4, d6 = 3, d7 = 2;
LiquidCrystal lcd(rs, en, d4, d5, d6, d7);

## Slide 166: Arduino code for LCD display
void setup() {
Serial.begin(9600);
lcd.begin(16, 2);
lcd.clear();
lcd.leftToRight();
lcd.setCursor(0, 1);
lcd.write("Hello, John");
lcd.setCursor(0, 0);
lcd.write("0123456789abcdef");
}
void loop() {
// set the cursor to column 0, line 1 line 1 is the second row
lcd.setCursor(0, 1);
lcd.print(millis() / 1000);
}

## Slide 167: Lab: RP LCD-1602 display
We connect the Raspberry Pi to the 1602 via a I2C connection (so your 1602 needs an i2c interface)
The connection from the RP use the same SDA, SCL connections (HDR 3, 5).
The 1602 requires a 5-volt voltage source.

## Slide 168: Raspberry Pi code for LCD display (using I2C)
// Manferdelli
// Raspberry Pi, i2c-lcd
#include <stdio.h>
#include <stdlib.h>
#include <stdint.h>
#include <string.h>
#include <wiringPi.h>
#include <wiringPiI2C.h>
#ifndef byte
typedef unsigned char byte;
#endif
const byte lcd_i2c_address = 0x27;
// Connection
// RP I2c IF
// gnd(HDR 6) Gnd
// scl(HDR 5) scl
// 5v (HDR 1) Vcc
// sda(HDR 3) sda

## Slide 169: Raspberry Pi code for LCD display (using I2C)
void write_int(int fd, int data) {
data |= 0x08;
wiringPiI2CWrite(fd, data);
return;
}
int read_int(int fd) {
return wiringPiI2CRead(fd);
}
void send_command(int fd, int c) {
int t;
// RS=0, RW=0, EN=1
t = (c & 0xf0) | 0x04;
write_int(fd, t);
delay(2);
// EN = 0
t &= 0xfb;
write_int(fd, t);
// RS=0, RW=0, EN=1
t = ((c & 0x0f) << 4) | 0x04;
write_int(fd, t);
delay(2);
// EN = 0
t &= 0xfb;
write_int(fd, t);
}
void send_data(int fd, int d) {
int t;
// RS=1, RW=0, EN=1
t = (d & 0xf0) | 0x05;
write_int(fd, t);
delay(2);
// EN = 0
t &= 0xfb;
write_int(fd, t);

## Slide 170: Raspberry Pi code for LCD display (using I2C)
void write_line(int fd, int line , int position, const char* data) {
if (line < 0 || line > 1)
return;
if (position < 0 || line > 15)
return;
int len = strlen(data);
if (len > 15)
return;
int addr = 0x40 * line + 0x80 + position;
printf("write_line %d %d, %s\n", line, position, data);
send_command(fd, addr);
for (int i = 0; i < len; i++) {
send_data(fd, data[i]);
}
}
void clearBuf(byte* buf, int n) {
for (int i = 0; i < n; i++) {
buf[i] = 0;
}
}
// RS=1, RW=0, EN=1
t = ((d & 0x0f) << 4) | 0x05;
write_int(fd, t);
delay(2);
// EN = 0
t &= 0xfb;
write_int(fd, t);
}
bool lcd_init(int fd) {
// 8 line
send_command(fd, 0x33);
delay(5);
// 4 line
send_command(fd, 0x32);
delay(5);
// 2 line
send_command(fd, 0x28);
// display enable
delay(5);
send_command(fd, 0x0c);
send_command(fd, 0x01); //clear
delay(5);
wiringPiI2CWrite(fd, 0x08);
return true;
}

## Slide 171: Raspberry Pi code for LCD display (using I2C)
int main(int an, char** av) {
int fd = wiringPiI2CSetup(lcd_i2c_address);
if (fd < 0) {
printf("Can't initialize Wiring Pi\n");
return 1;
}
if (!lcd_init(fd)) {
printf("Can't initialize LCD\n");
return 1;
}
char buf[16];
for(int j = 0; j < 20; j++) {
send_command(fd, 0x01);
delay(5);
write_line(fd, 0, 0, "Line 0");
clearBuf((byte*)buf, 16);
sprintf(buf, "Run %d", j);
write_line(fd, 1, 1, buf);
delay(5000);
}
return 0;
}

## Slide 172: Lab: RFID
You can find pictures of the RFID sensor and a tutorial in the Freenove manual here. The RC522 rfid card uses an SPI interface. You’ll also need a Mifare1 S50 card or FOB.
You’ll need to download the “RFID Library” for Arduino.
Wire the Arduino as shown.
Freenove
Newegg

## Slide 173: Arduino code for RFID
// rfid
// Manferdelli
#include <SPI.h>
#include <MFRC522.h>
typedef uint8_t byte;
const int rstPin = 9;
const int ssPin = 10;
const int measurementDelay= 500;
// Class args: slave select, reset
MFRC522 rfid(ssPin, rstPin);
void setup() {
Serial.begin(9600);
SPI.begin();
rfid.PCD_Init();
}
bool access_valid(int size, byte* id) {
// our card has id: FA-7C-63-2E
if (size != 4)
return false;
if ( id[0] != 0xfa || id[1] != 0x7c || id[2] != 0x63 || id[3] != 0x2e)
return false;
return true;
}

## Slide 174: Arduino code for RFID
void loop() {
if (rfid.PICC_IsNewCardPresent()) {
if(rfid.PICC_ReadCardSerial()) {
Serial.print("Card type: ");
for (int i = 0; i < rfid.uid.size; i++) {
if (i != 0)
Serial.print("-");
if (rfid.uid.uidByte[i] <= 0x9) {
Serial.print("0");
}
Serial.print(rfid.uid.uidByte[i], HEX);
}
Serial.println("");
if (access_valid(rfid.uid.size, rfid.uid.uidByte)) {
Serial.println("Access granted");
} else {
Serial.println("Access denied");
}
} else {
Serial.println("Can't read card serial number");
}
} else {
Serial.println("Card not present");
}
delay(measurementDelay);
}

## Slide 175: Lab: Stepper
Stepper motors advance one step in response to a signal, so turning continuously requires a sequence of pulses in a phased order.
Rather than timing the pulses with the Arduino, we use an IC that maps pulses to stepper inputs and drives more current than the Arduino can.
Wire the Arduino with the stepper controller as shown.
Freenove
Freenove

## Slide 176: Arduino code for Stepper
// Stepper
// Manferdelli
typedef uint8_t byte;
const int measurementDelay= 1000;
int out_ports[4] = {
11, 10, 9, 8
};
void setup() {
Serial.begin(9600);
for (int i = 0; i < 4; i++)
pinMode(out_ports[i], OUTPUT);
}
const int FW = 0;
const int BW = 1;

## Slide 177: Arduino code for Stepper
void move_one_step(int dir) {
static byte out = 1;
if (dir == FW) {
if (out != 0x08)
out = out << 1;
else
out = 1;
} else {
if (out != 1)
out = out >> 1;
else
out = 0x08;
}
for (int i = 0; i < 4; i++) {
digitalWrite(out_ports[i], (out & (1<<i)) ? HIGH:LOW);
}
}

## Slide 178: Arduino code for Stepper
void move_steps(int steps, byte ms_delay) {
if (steps > 0) {
for (int i = 0; i < steps; i++) {
move_one_step(FW);
delay(ms_delay);
}
} else {
for (int i = 0; i < -steps; i++) {
move_one_step(BW);
delay(ms_delay);
}
}
}
void loop() {
move_steps(2048, 4);
delay(measurementDelay);
move_steps(-2048, 4);
delay(measurementDelay);
}

## Slide 179: Lab: infrared sensor
You can find a tutorial in the Freenove manual here. The IR sensor detects an input infrared light wave modulated to blink at about 38 kHz (So constant IP sources are ignored). The output (on data pin 1) is a pulse width modulated signal.
Wire the infrared sensor and Arduino as shown.
Arduino
5 V
Gnd
IR sensor
Vcc (3)
Gnd (2)
Data (1)
D12
10K

## Slide 180: IR encoding
Uses pulse distance encoding for bits
  0: 562.5µs pulse burst followed by a 562.5µs space
  1: 562.5µs pulse burst followed by a 1.6875ms space
IR message consists of:
  a 9ms leading pulse burst
  a 4.5ms space
  the 8-bit address of receiving device followed by its 8-bit logical
  the 8-bit command followed by its 8-bit logical inverse
  a final 562.5µs pulse burst.
Figure from Altium

## Slide 181: Arduino code for infrared sensor
// Infrared
// Manferdelli
#include <IRremote.h>
typedef uint8_t byte;
const int dataPin= 12;
const int measurementDelay= 200;
IRrecv receiver(dataPin);
void setup() {
Serial.begin(9600);
receiver.enableIRIn();
}
void loop() {
decode_results results;
if (receiver.decode(&results)) {
Serial.print(results.value, HEX);
Serial.println("");
receiver.resume();
}
delay(measurementDelay);
}

## Slide 182: Infrared – Raspberry pi
You can use a library, lirc, to interface the raspberry pi.
The code is unexceptional, and I’ve included an untested version on the following page.

## Slide 183: Raspberry Pi code for infrared sensor
// Manferdelli
// Raspberry Pi, infrared
#include <stdio.h>
#include <stdlib.h>
#include <stdint.h>
#include <wiringPi.h>
#include <softPwm.h>
#include <lirc/lirc_client.h>
#include <time.h>
#ifndef byte
typedef unsigned char byte;
#endif
// Connection scheme
// Same as arduino
// sig goes to gpio 4 (pin 7)
const int sig_pin = 7;
const char* key_map[21] = {
" KEY_CHANNELDOWN ",
" KEY_CHANNEL ",
" KEY_CHANNELUP ",
" KEY_PREVIOUS ",
" KEY_NEXT ",
" KEY_PLAYPAUSE ",
" KEY_VOLUMEDOWN ",
" KEY_VOLUMEUP ",
" KEY_EQUAL ",
" KEY_NUMERIC_0 ",
" BTN_0 ",
" BTN_1 ",
" KEY_NUMERIC_1 ",
" KEY_NUMERIC_2 ",
" KEY_NUMERIC_3 ",
" KEY_NUMERIC_4 ",
" KEY_NUMERIC_5 ",
" KEY_NUMERIC_6 ",
" KEY_NUMERIC_7 ",
" KEY_NUMERIC_8 ",
" KEY_NUMERIC_9 "
};
Not tested yet

## Slide 184: Raspberry Pi code for infrared sensor
int main(int an, char** av) {
if (wiringPiSetup() < 0) {
printf("Can't initialize Wiring Pi\n");
return 1;
}
linc_config *config;
char* code;
int button_timer = millis();
if (lirc_init("lirc", 1) < 0) {
printf("Can't initialize ir library\n");
return 1;
}
if (lirc_readconfig(NULL, &config, NULL) == 0) {
while (lirc_nextcode(&code) == 0) {
if (code == NULL)
continue;
if ((millis() - button_timer) > 400) {
}
printf("Code: %s\n", code);
free(code);
}
lirc_freeconfig(config);
}
lirc_deinit();
return 0;
}

## Slide 185: Lab: seven segment display
You can find a tutorial about the seven-segment display in the Freenove manual here.
There are two types, one has COM connected to anodes, one to diodes.
The SN74hc595 is a serial to parallel shift register which conserves GPIO pins.
Wire the Arduino as shown.
Freenove
Engineer’s garage
SN54hc595
Freenove
a
b
c
d
e
f
g
h

## Slide 186: Arduino code for display
// Seven segment display
// Manferdelli
#ifndef byte
typedef uint8_t byte;
#endif
int latchPin = 12;
int clockPin = 13;
int dataPin = 11;
const int measurementDelay= 1500;
// Pin11 to SH_CP 74HC595
// Pin12 connected to ST_CP 74HC595,
// Pin13 connected to DS of 74HC595

## Slide 187: Arduino code for display
// encoding of digits
// a b c d e f g h
// 0 1 1 1 1 1 1 0 0 0xfc
// 1 0 1 1 0 0 0 0 0 0x60
// 2 1 1 0 1 1 0 1 0 0xda
// 3 1 1 1 1 0 0 1 0 0xf2
// 4 0 1 1 0 0 1 1 0 0x66
// 5 1 0 1 1 0 1 1 0 0xb6
// 6 1 0 1 1 1 1 1 0 0xbe
// 7 1 1 1 0 0 0 0 0 0xe0
// 8 1 1 1 1 1 1 1 0 0xfe
// 9 1 1 1 0 0 1 1 0 0xe6
// a 1 1 1 1 1 0 1 0 0xfa
// b 0 0 1 1 1 1 1 0 0x3e
// c 0 0 0 1 1 0 1 0 0x1a
// d 0 1 1 1 1 0 1 0 0x7a
// e 1 0 0 1 1 1 1 0 0x9e
// f 1 1 0 0 1 1 1 0 0x8e
byte digit_pattern_seg_on[] = {
0xfc, 0x60, 0xda, 0xf2,
0x66, 0xb6, 0xbe, 0xe0,
0xfe, 0xe6, 0xfa, 0x3e,
0x1a, 0x7a, 0x9e, 0x8e,
};

## Slide 188: Arduino code for display
byte digit_pattern_seg_off[] = {
0x03, 0x9f, 0x25, 0x0d,
0x99, 0x49, 0x41, 0x1f,
0x01, 0x19, 0x05, 0xc1,
0xe4, 0x85, 0x61, 0x71,
};
void setup() {
Serial.begin(9600);
pinMode(latchPin, OUTPUT);
pinMode(clockPin, OUTPUT);
pinMode(dataPin, OUTPUT);
}
void writeData(int value) {
digitalWrite(latchPin, LOW);
shiftOut(dataPin, clockPin, LSBFIRST, value);
digitalWrite(latchPin, HIGH);
}
void loop() {
for (int j = 0; j < 16; j++) {
writeData(digit_pattern_seg_off[j]);
delay(measurementDelay);
}
}

## Slide 189: Lab: Keypad
You can find a tutorial about the keypad in the Freenove manual here.
Wire the Arduino as shown.

## Slide 190: Arduino code for keypad
// Keypad
// Manferdelli
#include <Keypad.h>
const int dataPin= 8;
const int measurementDelay= 500;
typedef uint8_t byte;
byte rowPins[4] = {11, 10, 9, 8};
byte colPins[4] = {7, 6, 5, 4};
Keypad myKeypad = Keypad(makeKeymap(keys), rowPins, colPins, 4, 4);
// define the symbols on the buttons of the keypad
char keys[4][4] = {
{'1', '2', '3', 'A'},
{'4', '5', '6', 'B'},
{'7', '8', '9', 'C'},
{'*', '0', '#', 'D'}
};

## Slide 191: Arduino code for keypad
void setup() {
Serial.begin(9600);
}
void loop() {
// Get the character input
char keyPressed = myKeypad.getKey();
// If there is a character input, sent it to the serial port
if (keyPressed) {
Serial.println(keyPressed);
}
}

## Slide 192: Lab: HC-12
The HC-12 is a half-duplex 20 dBm (100 mW) transceiver with -117 dBm (2×10-15 W) sensitivity at 5000 bps. It uses an open spectrum 433-473MHz which covers 100 channels and has a range of about a 1.8 kilometers.
You can find an HC-12 tutorial here.
It uses the STM8S003F3 microcontroller and the Si4463 transceiver.
The interface is a standard UART, serial line.
Power 3.3-5V
Wire the Arduino as indicated, the capacitor is a 22 µF to 1 mF reservoir capacitor.
From All about circuits

## Slide 193: Lab: HC-12
Module parameters, like channel selection and baud rate, are changed with the “AT” command.
The HC-12 only responds to parameter changes when it’s in “command mode.” Command mode is enabled when the “set” pin on the HC-12 is set LOW. The other mode, transparent mode, is the usual mode, it is enabled when the “set” pin on the HC-12 is set HIGH.
If we send “AT” to the hc-12, it returns “OK”. (This is a test message,)
If we send AT+Bxxxxx, where xxxxx is the baud rate, the hc-12 changes baud rate. The allowable baud rates are 1200 bps, 2400 bps, 4800 bps, 9600 bps, 19200 bps, 38400 bps, 57600 bps, and 115200 bps. The default is 9600 bps. For example, if we send “AT+B38400” to the hc-12, it returns “OK+B19200”.
AT+Cxxx change wireless communication channel, where 001 <= xxx <= 100. The default is channel 1. For example, if we send “AT+C006” command to the hc-12, it will return “OK+C006”. Each channel is 400kHz higher than the previous one.

## Slide 194: HC-12 propagation
Frequency band is from 433.4 MHz to 473.0 MHz
It has a total of 100 channels with a stepping of 400 KHz between each channel
Transmitting power is from -1dBm (0.79mW) to 20dBm (100mW)
Receiving sensitivity is from -117dBm (0.019pW) to -100dBm (10pW).

## Slide 195: Arduino code for HC-12
// hc12
// Manferdelli
#include <SoftwareSerial.h>
const int deviceReceivePin= 4;
const int deviceTransmitPin= 5;
const int deviceSetPin = 6;
#ifndef byte
typedef uint8_t byte;
#endif
// Note: device transmit pin is SoftwareSerial receive pin
// and vice-versa.
SoftwareSerial hc12(deviceTransmitPin, deviceReceivePin);
void copy(char* from, char* to, int size) {
for(int i = 0; i < size; i++)
to[i] = from[i];
return;
}

## Slide 196: Arduino code for HC-12
int read_from_serial(int max, char* b) {
int i = 0;
while (hc12.available() != 0 && (i < max)) {
b[i++] = hc12.read();
}
return i;
}
void setup() {
pinMode(deviceSetPin, OUTPUT);
delay(100);
Serial.begin(9600);
hc12.begin(9600);
}

## Slide 197: Arduino code for HC-12
void loop() {
char send_buf[65];
char receive_buf[65];
copy((char*)"AT", send_buf, 3);
for (;;) {
digitalWrite(deviceSetPin, HIGH); // Transparent mode
delay(200);
hc12.listen();
int n = read_from_serial(64, receive_buf);
if (n > 0) {
receive_buf[n] = 0;
Serial.print("Received: ");
Serial.println((const char*)receive_buf);
} else {
Serial.println("nothing received");
}
digitalWrite(deviceSetPin, LOW); // Command mode
delay(500);
hc12.print(send_buf);
Serial.print("Sent ");
Serial.println((const char *)send_buf);
}
}

## Slide 198: Raspberry Pi code for HC-12
// Manferdelli, HC-12
#define PIN_ACCESS
#include <stdio.h>
#include <unistd.h>
#include <fcntl.h>
#include <termios.h>
#include <string.h>
#include <stdlib.h>
#include <sys/ioctl.h>
#ifdef PIN_ACCESS
#include <wiringPi.h>
#endif
#ifndef byte
typedef unsigned char byte;
#endif
// HC12 Interfacing with RP through Rx, Tx
// Connections
// FDMI1232 HC12
// vcc vcc
// gnd gnd
// rxd txd
// txd rxd
// RP HC12
// vcc vcc
// gnd gnd
// rxd (pin 10) txd
// txd (pin 8) rxd
#ifdef PIN_ACCESS
#define uartDevice "/dev/serial0"
#else
#define uartDevice "/dev/ttyUSB0"
#endif
#define BUF_SIZE 512
const int set_pin = 7;

## Slide 199: Raspberry Pi code for HC-12
void clearBuf(byte* buf, int n) {
for (int i = 0; i < n; i++) {
buf[i] = 0;
}
}
int bytes_available(int fd) {
int num_bytes = 0;
ioctl(fd, FIONREAD, &num_bytes);
return num_bytes;
}
const char* eol = "\r\n";
void send_command(int fd, const char* command) {
byte response[128];
printf("Command: %s\n", command);
// command mode
digitalWrite(set_pin, LOW);
delay(200);
tcflush(fd, TCIFLUSH);
write(fd, command, strlen(command));
int n = 0;
delay(200);
while (bytes_available(fd) > 0) {
clearBuf(response, 128);
n = read(fd, response, 127);
if (n > 1) {
printf("Response: %s", (char*)response);
}
tcflush(fd, TCIFLUSH);
}
digitalWrite(set_pin, HIGH);
delay(200);
}

## Slide 200: Raspberry Pi code for HC-12
bool setup(int fd, int new_baud_rate, int new_channel) {
#ifdef PIN_ACCESS
int n = 0;
byte request[128];
pinMode(set_pin, OUTPUT);
// test command, hc12 should return "OK"
clearBuf(request, 128);
send_command(fd, "AT");
// baud rate
clearBuf(request, 128);
sprintf((char*)request, "AT+B%04d", new_baud_rate);
send_command(fd, (char*)request);
// channel command
clearBuf(request, 128);
sprintf((char*)request, "AT+C%03d", new_channel);
send_command(fd, (char*)request);
// back to transparent mode
digitalWrite(set_pin, HIGH);
delay(200);
#endif
return true;
}

## Slide 201: Raspberry Pi code for HC-12
if (strcmp(av[i], "-channel") == 0) {
unsigned ls = 0;
ls = atoi(av[++i]);
new_channel = ls;
continue;
}
}
if (new_channel < 1 || new_channel>100)
new_channel = 1;
// turn off blocking for reads.
fcntl(fd, F_SETFL, 0);
// set baud rate
struct termios t;
tcgetattr(fd, &t);
cfsetispeed(&t, new_baud_rate);
tcsetattr(fd, TCSANOW, &t);
// setup hc-12
// We need pin access for this
setup(fd, new_baud_rate, new_channel);
int in_size, out_size;
int main(int an, char** av) {
byte receive_buf[BUF_SIZE];
byte send_buf[BUF_SIZE];
#ifdef PIN_ACCESS
if (wiringPiSetup() < 0) {
printf("Can't init wiringPi\n");
return 1;
}
#endif
int fd = open(uartDevice,
O_RDWR | O_NOCTTY | O_NDELAY);
if (fd < 0) {
printf("Can't open %s\n", uartDevice);
return 1;
}
speed_t new_baud_rate = 9600;
int new_channel = 6;
for (int i = 0; i < (an - 1); i++) {
if (strcmp(av[i], "-baud") == 0) {
unsigned ls = 0;
ls = atoi(av[++i]);
new_baud_rate = ls;
continue;
}

## Slide 202: Raspberry Pi code for HC-12
// setup hc-12
setup(fd, new_baud_rate, new_channel);
int in_size, out_size;
tcflush(fd, TCIFLUSH);
for(int i = 0; i < 5; i++) {
while (bytes_available(fd) > 0) {
clearBuf(receive_buf, BUF_SIZE);
in_size = read(fd, receive_buf, BUF_SIZE - 1);
receive_buf[in_size++] = 0;
printf("Received: %s", (const char*)receive_buf);
}
clearBuf(send_buf, BUF_SIZE);
sprintf((char*)send_buf,"Message %d", i);
out_size = strlen((char*)send_buf);
write(fd, send_buf, out_size);
printf("Sent: %s\n", (char*)send_buf);
#ifdef PIN_ACCESS
delay(200);
#endif
}
close(fd);
return 0;
}

## Slide 203: Lab: Rotary encoder
If the encoder is rotating clockwise the output A will be ahead of output B.
A digital device (like the Arduino) can track the speed of rotation and turn the sequence of pulses into a measured position.
Wire the Arduino as shown.
Hobby Electronics
Arduino
5 V
Gnd
Rotary encoder
Vcc (3)
Middle pin (Pin 2)
D2
10K
Pin 3
D4
Pin 1

## Slide 204: Arduino code for rotary encoder
// Rotary encoder
// Manferdelli
typedef uint8_t byte;
const int clockPin= 2;
const int dataPin= 4;
const int measurementDelay= 100;
int position = -1;
void encoder() {
if (digitalRead(clockPin) == digitalRead(dataPin))
position++;
else
position--;
}

## Slide 205: Arduino code for rotary encoder
void setup() {
Serial.begin(9600);
pinMode(clockPin, INPUT);
pinMode(dataPin, INPUT);
digitalWrite(clockPin, HIGH);
digitalWrite(dataPin, HIGH);
attachInterrupt(0, encoder, CHANGE);
}
void loop() {
Serial.println("");
Serial.print("Position: ");
Serial.print(position);
Serial.println("");
delay(measurementDelay);
}

## Slide 206: Lab: Use dead reckoning with an IMU and Google maps
Openweather API is here.
Google maps API is here.
  https://maps.googleapis.com/maps/api/staticmap?center=Brooklyn+Bridge,New+York,NY&zoom=13&size=600x300&maptype=roadmap &markers=color:blue%7Clabel:S%7C40.702147,-74.015794&markers=color:green%7Clabel:G%7C40.711614,-74.012318 &markers=color:red%7Clabel:C%7C40.718217,-73.998284 &key=YOUR_API_KEY
Google speech API is here.
206

## Slide 207: Lab: Raspberry Pi attached cameras
Get a Raspberry Pi camera here. The data sheet is here.
There are two versions of the Camera Module:
  The standard version, which is designed to take pictures in normal light
  The NoIR version, which doesn’t have an infrared filter, so you can use it with an infrared light source to take pictures in the dark
There are two command line utilities that use the camera
  raspistill -o Desktop/image.jpg
  raspivid -o Desktop/video.h264
The first takes still pictures and the second captures video.
There are also programmatic interfaces, which we describe next.
You can update and configure the camera using the following:
  sudo apt-get-update
  sudo apt-get upgrade
  sudo raspi-config
207

## Slide 208: Using Raspberry Pi with Python
Here’s some sample python code that accesses the camera to capture a still:
  from picamera import PiCamera
  from time import sleep
  camera = PiCamera()
  camera.start_preview()
  sleep(5)
  camera.capture('/home/pi/Desktop/image.jpg')
  camera.stop_preview()
208
You’ll have to install python first this way:
  sudo apt update
  sudo apt install python3-picamera

## Slide 209: Using Raspberry Pi with Python
209
This code changes some camera properties:
  camera.resolution = (2592, 1944)
  camera.framerate = 15
  camera.start_preview()
  sleep(5)
  camera.capture('/home/pi/Desktop/max.jpg')
  camera.stop_preview()
  camera.start_preview()
  camera.annotate_text = "Hello world!"
  sleep(5)
  camera.capture('/home/pi/Desktop/text.jpg')
  camera.stop_preview()

## Slide 210: Using Raspberry Pi with C++
There are several C++ camera interface libraries. Here we use raspicam which you can find here. To install raspicam, download it and install cmake:
  sudo apt-get update && sudo apt-get upgrade
  sudo apt-get install cmake. Then build the library.
To compile the following sample code, do the following:
  g++ still.cc -L /opt/vc/lib -I/usr/local/include -lraspicam -lmmal -lmmal_core -lmmal_util
210
  #include <unistd.h>
  #include <ctime>
  #include <fstream>
  #include <iostream>
  #include <raspicam/raspicam.h>
  using namespace std;
  int main (int argc, char **argv) {
  raspicam::RaspiCam Camera;
  if (!Camera.open()) {cerr<<"Error opening camera"<<endl; return -1;}
  … continued on next slide

## Slide 211: Using Raspberry Pi with C++
211
  // Wait a while until camera stabilizes
  sleep(3);
  // Capture
  Camera.grab();
  unsigned char *data=new unsigned char[
  Camera.getImageTypeSize(raspicam::RASPICAM_FORMAT_RGB)];
  Camera.retrieve (data,raspicam::RASPICAM_FORMAT_RGB );//get camera image
  // Save
  std::ofstream outFile("raspicam_image.ppm",std::ios::binary);
  outFile<<"P6\n"<<Camera.getWidth() <<" "<<Camera.getHeight() <<" 255\n";
  outFile.write ((char*) data,
  Camera.getImageTypeSize(raspicam::RASPICAM_FORMAT_RGB));
  cout<<"Image saved at raspicam_image.ppm"<<endl;
  // Free resources
  delete data;
  return 0;
  }

## Slide 212: Some of the experiments on a perf board

## Slide 213: References
Feynman’s Lectures on Physics.
Berkeley physics course volumes 1, 2, 3.
Sears, Zemansky and Young, University Physics.
Schaum’s outline in Physics for Engineering and Science.
Griffiths, Introduction to Electrodynamics.
ARRL Handbook.
Rutledge, Electronics of Radio.
Scherz, Practical Electronics for Inventors.
Bryant and O’Halleron, Computer Systems, a programmer’s perspective.
Patterson and Hennessy, Computer Architecture.

## Slide 214: References
IBM, System 360, Principles of Operation (a classic)
Intel, Intel Processor Architecture (5 volumes)
Arm Architecture manual
Tannenbaum, Operating systems
http://www.freenove.com (Sensor kit projects)
Tero Karvinen, Kimmo Karvinen, Ville Valtokari, Make: Sensors
Wallace, Richardson, Getting started with Raspberry Pi
Tero Karvinen, Kimmo Karvinen, Make: Arduino Bots and Gadgets

## Slide 215: Exercises
Get the data sheets for the processors, sensors, and memory for some IoT device.
Get the RF sources from an IoT devices (frequency, power, ...) from the FCC filings.
Get the circuit board layouts for an IoT device? What could you use them for?
Calculate the current drain on the Arduino pins for some of our experiments.
Use the Arduino to build a communication line based on infrared.
Use the Arduino to build an RFID reader.
Use the Arduino to connect a Hall (magnetic field) sensor.
Connect a small digital radio (e.g.- NRF24L01, Adafruit RFM69HCW Transceiver).
Display some of our sensor readings on a local small screen like the LCD 1602.
How would you use a gyro and accelerometer to do “dead reckoning.”
Connect a GPS module and investigate the theory of GPS positioning and accuracy.

## Slide 216: Tools and equipment
Standard Electronics tools (~$50)
De-soldering station ($99)
5 Perf boards ($10), lots of wired jumpers, clips to connect to chips (e.g.-EEPROMs) ...
2 Volt-ohm meters ($50)
Signal generator ($40)
Oscilloscope ($350)
Various parts (see Practical Electronics)
Attify Badge (to connect to I2C, SPI, UARTs and JTAGs) ($20)
Arduino ($15)
Sensor starter kits, some include Arduinos ($50-$80). These contain accelerometers, light sensors, compass, GPS modules, temp/humidity
Power supplies
More exotic: signal generator, spectrum analyzer.

## Slide 217: License
This material is licensed under Apache License, Version 2.0, January 2004.
Use, duplication or distribution of this material is subject to this license and any such use, duplication or distribution constitutes consent to license terms.
You can find the full text of the license at: http://www.apache.org/licenses/.

## Slide 218: All classical physics --- behold
,
,
, 𝜖0 = 8.854 × 10-12 C2/N-m2.

## Slide 219: Physical data and phenomenology
,
Solution to Maxwell:
  ,
  ,

## Slide 220: Physical data and phenomenology
In conductors, . , the resistivity.
Poynting: .
In materials:
  Often, , ,

## Slide 221: Raspberry Pi 3 pins

## Slide 222: Lab: Servo
You can find this in the Freenove manuals here.
Wire the servo and Arduino as shown.
Arduino
5 V
Gnd
Servo
Vcc
Gnd
D3
Signal
Freenove

## Slide 223: Arduino code for Servo
// Stepper
// Manferdelli
typedef uint8_t byte;
const int measurementDelay= 1000;
int out_ports[4] = {
11, 10, 9, 8
};
void setup() {
Serial.begin(9600);
for (int i = 0; i < 4; i++)
pinMode(out_ports[i], OUTPUT);
}
const int FW = 0;
const int BW = 1;

## Slide 224: Arduino code for Servo
void move_one_step(int dir) {
static byte out = 1;
if (dir == FW) {
if (out != 0x08)
out = out << 1;
else
out = 1;
} else {
if (out != 1)
out = out >> 1;
else
out = 0x08;
}
for (int i = 0; i < 4; i++) {
digitalWrite(out_ports[i], (out & (1<<i)) ? HIGH:LOW);
}
}

## Slide 225: Arduino code for Servo
void move_steps(int steps, byte ms_delay) {
if (steps > 0) {
for (int i = 0; i < steps; i++) {
move_one_step(FW);
delay(ms_delay);
}
} else {
for (int i = 0; i < -steps; i++) {
move_one_step(BW);
delay(ms_delay);
}
}
}
void loop() {
move_steps(2048, 4);
delay(measurementDelay);
move_steps(-2048, 4);
delay(measurementDelay);
}