## Slide 1: Electronics of Radio
Notes on David Rutledge’s book
John Manferdelli
johnmanferdelli@hotmail.com

## Slide 2: Basic concepts
Potential difference (): , energy per charge, 1V = 1 J/s
Kirkoff 1: (Conservation of energy)
Kirkoff node: (Conservation of charge)
V, I
Instantaneous power:
Average power:
Band names:
Name | Frequency
VLF | 3-30kHz
LW | 20-300kHz
MW | 300kHz-3MHz
HF | 3MHz-30MHz
VHF | 30-300MHz
Name | Frequency
UHF | 300MHz-1GHz
uW | 1-30GHz
milliW | 30-300GHz
submilliF | >300GHz

## Slide 3: Signals
Gain (G) expressed in decibels:
Mixer:
  , ,
Modulation
Name | Equation
AM | 
FM | 
FSK | , if 1 , if 0
PSK | , if 1 , if 0
Name | Equation
AM | 
FM | 
FSK | 
PSK | 

## Slide 4: Resistors, capacitors, inductors
Resistors
  Analytic model:
  Energy dissipated:
Capacitors
  Analytic model:
  Capacitor Energy stored:
Inductors
  Analytic model:
  Inductor Energy stored:
R
Credit: Make Electronics

## Slide 5: Diodes, transformers
Diodes
  Devices that allow current to flow only in one direction
  Silicon diodes, for example have, essentially infinite resistance if Vac<0, that is if the cathode is at a higher potential than the anode and very low resistance if Vac> .7V.
  The cathode is usually labelled with a band
Transformers
  AC only: =
Credit: Make Electronics

## Slide 6: Simple circuit analysis with Kirchhoff
is the equivalent resistance, replacing the top left circuit with a single resistance.
By Kirchhoff’s node rule,
thus and Adding, we get + . Dividing by and solving, we get
Again let is the equivalent resistance, replacing the bottom left circuit with a single resistance.
By Kirchhoff’s node rule,
Solving, we get.
R1
R2
V=0
V1
V2
i1
i2
i
R1
R2
V=0
V1
i1
i2
i
V=0
i1
i2
C1
C2
V1
V2
i
V=0
C1
C2
V1
i1
i2
i
is the equivalent capacitance, replacing the top right circuit with a single capacitor.
By Kirchhoff’s node rule,
and
Adding and cancelling the , we get
+ =1 and solving, we get.
is the equivalent capacitance, replacing the bottom right circuit with a single capacitor.
By Kirchhoff’s node rule,
, so

## Slide 7: Simple circuit analysis with Kirchhoff
Let be the equivalent inductance, replacing the top left circuit with a single inductor.
By Kirchhoff’s node rule,
, ,
= and
=
Let be the equivalent inductance, replacing the bottom left circuit with a , , ,
single inductor.
By Kirchhoff’s node rule,
and
L1
L2
V=0
V1
V2
i1
i2
i
L1
L2
V=0
V1
i1
i2
i
R1
R2
V=0
V1
V2
i1
i2
i
The circuit on the right, is useful and is called a voltage divider.
so ,
Thus, and so

## Slide 8: RC/RL circuit analysis with Kirchhoff
RC behavior: charging
  ,
  ,, or
  Solution is
RL behavior: charging
  , so
  Solution is
C2
L
V2
i1
i2
R
+
-
V0
C
V2
i1
i2
R
+
-
V0

## Slide 9: Phasors
Suppose and . If , we say the current leads the voltage.
, and
Now define and , so , , , and . and are called phasors and do not include time. Note that and .
Note that , for a capacitor and , for an inductor

## Slide 10: Circuit analysis and impedance
Impedance unifies the “simple” ohms law with capacitance and inductance.
, for resistors, , for inductors and , for capacitors.
In general, and all the ohm like laws hold for resistors, capacitors and inductors .
  for two components with impedance connected in series
  for two components with impedance connected in parallel
For example, for a resistor and capacitor in series has impedance

## Slide 11: Phasors, impedance and power
For the circuit on the right, is the impedance for the resistor and capacitor in series.
The phasor and the phasor
Further, , and |
For phasors , define the complex power as ; the first term is the real power, the second is called the reactive power.
The average power is . We define the reactive power as .
, where and are respectively, the energy stored in the inductor and capacitor respectively.
V0
C
V
R
I

## Slide 12: Q and phasors
Consider the series resonance on the right.
The phasor, , and the phasor , where .
So .
is maximum when. Put . When , .
, when . Note that the power through R when is half the power through R when or .
Let the frequencies where be denoted and , where .
We define .
Solving for and , we get and , or, in terms of ,
and . In fact, , and so .
Thus
From the definition of , earlier, where is the total energy stored in L and C, which is in turn the peak and peak at resonance.
V0
C
VR
R
L

## Slide 13: Phasors, impedance and power
For the circuit on the right, is the impedance for the resistor and capacitor in series.
The phasor and the phasor
Further, , and |
For phasors , define the complex power as ; the first term is the real power, the second is called the reactive power.
The average power is . We define the reactive power as .
, where and are respectively, the energy stored in the inductor and capacitor respectively.
V0
C
V
R
I

## Slide 14: Thevenin and Norton
Thevenin: Any combination of linear sources and passive elements terminating in two terminals is equivalent to a pure voltage source in series with an impedance
Norton: Any combination of linear sources and passive elements terminating in two terminals is equivalent to a pure current source in parallel with a conductance
Similar theorems for two terminal input and output devices (with transfer function)
ZTh
VTh
GTh
IN

## Slide 15: Thevenin and Norton
We can use lookback resistance to calculate the Thevenin equivalent resistance and ideal source.
To find the lookback resistance, short the source and apply the usual laws.
  Here
To find the new ideal source, notice and form a voltage divider.
  The new source voltage is
R2
R1
Is equivalent to

## Slide 16: Exercise 1: Resistors
Consider (A). Find the formula for power in the load. Find the that maximizes the power to the load.
  ,
  , which is maximum when
Find the Thevenin and Norton parameters fore (B).
Find the Thevenin and Norton parameters fore (C).
+
-
V0
R1
R3
R2
+
-
V0
R1
R3
R2
A
B
C
+
-
V0
Rs
Rl
Vl

## Slide 17: Exercise 3: Capacitors
In the circuit on the right, is a 2 volt pp ideal square wave source of frequency 20Hz, , and Period is
What is the voltage, , at the output? The scope has an input resistance of .
  About a volt at peak
Let , the time to discharge to 0V. Calculate and .
Capacitance on the scope prevents the delay from being 0. Measure the new with these changes.
Given C0 and Cp and Rp.
  , ,
Now calculate the new
  -sec
Vi
Cp
Rp
Probe
V
Cc
Co
R0
V0
C
R
Rs
V

## Slide 18: Exercise 4: Diode detectors
For AM, , Define the modulation depth
In circuit on the right, ,
Set function generator for , , ,
  Calculate for the RC circuit. .
    is period of modulating signal. So
    is period of modulating signal.
    As you change does the frequency of track it? (It better)
  Compare the max voltage of the AM signal to the max of .
  What happens when we make
Vi
C
R
Vo

## Slide 19: AM Modulator for previous exercise
2.2k
.1uF
47k
10k
10k
1nF
680
Modulation signal
4.2 Vpp, 1kHz
Carrier signal
.8 Vpp, 1MHz
12V
.1uF
I didn’t have a signal generator that produced an AM signal, so I used the modulator on the right with the indicated inputs to produce the AM needed for the detector in the previous exercise.

## Slide 20: Exercise 5: Inductors
Set function generator for square wave with 5V , a Thevenin equivalent source resistance of and frequency Connect a load, load, L=1mH
  Observe square wave with rounded corners, measure the time, to decay to 0
    About
  In the top circuit, calculate inductor current and the expected delay,
    , ,
    As phasors, , , ,
  In the second circuit, use 2 scope channels: one at input, one at output.
    . Ringing at 10MHz. .
  Note: I made the pull-up 100K.
2N2222A
12V
out
2k
2k
L
Vi
Vo
L
RL
RTh

## Slide 21: Exercise 6: Diodes and snubbers
Add indicated snubber diode.
Swing up is nearly immediate with snubber
Ringing at 10MHz. .
What is its effect on ringing?
  Ringing is uniform at 5 MHz
Diode should be on when transistor is off.
Note: I made the pull-up 100K.
2N2222A
12 V
out
2k
2k
L

## Slide 22
Exercise 7: Parallel to Series conversion
For series: ,
For parallel: , so and
If ,
If circuits (A) and (B) have the same impedance, what is the relationship between and
  , ,
  , , , set for later reference
  This shows the Q’s must be equal as stated above.
Find a formula for for large and small
Use circuit (C) to transfer a load (circuit C) to a load. What is at 7 MHz? What are C and L in that model?
  Use the parallel to series conversion to make a series equivalent circuit consisting of C and the with
Rs
jXs
Rp
jXp
A
B
C
C
L

## Slide 23
Exercise 8: Series resonance
For the circuit on the right, C, forming a bandpass filter.
If the resonant frequency is , so the
resonant frequency is
Tune the resonant frequency to and find , and and thus
Compute what these values should be
  As phasors, ,
  , Power through R at is . At resonance, . To find half power, set )/(), or .
  Solving gives , ,
  General formulas: ,
L
C
Vo
Vi
R

## Slide 24
Exercise 9: Parallel resonance
for T37-2 core so for 28 turns,
Again, find the resonant frequency, the frequencies corresponding to a 3db falloff, the bandwidth and the Q of this circuit. This circuit is in the transmit oscillator
  For , network:
  . , .
General formulas: , ,
C38
100pF
C37
5pF
L6
R
Vo
Vi

## Slide 25: Direct conversion and superhet receivers
Image frequency
Superheterodyne designs
Audio
Amp
RF
Filter
LO
RF Mixer
Direct conversion

## Slide 26
Norcal 40A
Harmonic
Filter
VFO
2.1 MHz
RF
Filter
IF Filter
AGC
Transmit
Filter
AGC
Detector
Key
Power
Amp
BFO
4.9 MHz
Transmit oscillator
4.9 MHz
Driver
Buffer
RF Mixer
Product
Detector
Transmit
Mixer
Audio
Amp
<10 MHz
7 MHz
2W
20 mW
300 uW
10 uW
7 MHz
2.8 MHz
4.9 MHz
9.1 MHz
9.8 MHz
Audio

## Slide 27
Transmission Lines
and
Solution is , which is the velocity for the forward wave
, , is the forward or “characteristic” impedance
Another solution is which is the velocity for the reverse wave
, , , is the backwards looking impedance
In
Vn
…
Ll
Cl
I+
V+
P+
I-
V-
P-

## Slide 28
Transmission Lines - continued
, in phasor notation,
To compute power, let ,
Complex power is , , , with
Suppose over a transmission line, is the distributed impedance/m, is the distributed admittance/m and suppose the forward wave is , and its phasor is Let ,
, . …(1)
(to account for attenuation), then and the forward phasor becomes is a transmission loss. . By differentiating (1), we get Solutions are all complex
Example: If for the transmission line, then and (positive real root)

## Slide 29
Transmission Lines - dispersion
and can vary with frequency; this is dispersion.
Heaviside: Adjust parameters so , then and are constants and we get:
  and ,
  We also get as with a lossless line.
  If
    and
  If
    and ,
For first transatlantic cable,
  and highly dispersive

## Slide 30
Transmission Lines-reflections
, ,
,
Consider the circuit in the upper right (A): ,
, ,
For (B):
Lookback resistance is , short circuit for (B) is
Thevenin equivalent for open circuit is (B)
, This is the total available power
V+
Z0
I
V-
Z
V
(A)
V+
Z0
Z0
V0=
V0=
(B)

## Slide 31
Transmission Lines – resonance and Q
For (A) on right, , ,
  ,
  .
, ,
In (B) to the right, the coefficient of reflection is and the generator absorbs the reverse wave. .
  is the reflection coefficient at generator.
  ,
  , , ,
  Normalized:
  ,
V
Z0
Vg
l)
Z0
l)
l)
V0
A
(B)
Z0, l

## Slide 32
Exercise 10: Coax
We’ll measure the velocity of waves in RG58U by connecting one channel of the scope to the input and one to the output.
Measure the velocity, v, in 10m coax at 7MHz. Try different frequencies. Use , using square waves at 20kHz.
Do the same with an antenna
Calculate with termination for the circuit on the right.
Remove the and measure the V and use it and to calculate L, and C for the coax
  Measured speed is . . For high impedance, and . So, and , so =1. . which is what we use in the next problem.
50
1
1:1
Function generator
10m cable
50
scope channel 1 (V)
scope channel 2 (I)
50
10m
50
Z0, l

## Slide 33
Exercise 11: Waves
Suppose we want to send voice over 100km of coax,
Measure the SWR which is the ratio of the maximum to minimum output
  , , , we get from the previous exercise.
  .
If and the distributed resistance at voice is , calculate total dB loss at 500, 1000 and 2000Hz using the high frequency approximation.
  , , ,
  High resistance approximation: ,
  For loss is
50
50
Z0, l

## Slide 34
Exercise 11: Waves
Add a 100mH inductor every 1km. Now what’s the loss?
  , ,
  High reactance approximation: ,
  ,
  For loss is =5.5 or

## Slide 35
Exercise 12: Resonance
has a capacitance of about Let be the attenuation constant and be the phase
Derive an expression for and assuming is small by finding the first resonance where is minimum.
  , . So, at ,
Find and the wave velocity by finding the resonant frequency (without the load, ) and noting the time delay with a scope on the input and output. Use to calculate .
  will be maximum at resonant frequency with unterminated line.
  is minimum when and . This gives .
  At ,
Use this to calculate the velocity, . How large is the frequency shift caused?
  . [ should be about ]
Find, as usual, , , and
  , so . , and
10m
Z0
Scope channel 2, no load
Scope channel 1 and function generator
V0

## Slide 36
Filters
Bandpass - WIkipedia
Lowpass - WIkipedia
Circuits on the left are called ladder filters.
Low pass (Butterworth equivalent): Tabled values for inductors and capacitors based on frequency and dB drop-off.
Can convert low pass into bandpass.
For low pass to high pass
Butterworth: , is 3dB cutoff
Chebyshev: , is 3dB cutoff
Normalized reactance's:
Ripple loss:
,
Example: cutoff at 10MHz, 4th order, 50ohm output, 3dB cutoff, , , ,
Yuck!
L2
L4
Low pass
C1
C2
C3
RL
High pass
L2
L4
C1
C2
C3
7 MHz bandpass
L2 (15 uH)
L4 (8nH)
C1 (34.5 pF)
C2 (6nF)
RL

## Slide 37
Norcal transmit bandpass filter
,
is 36 turns #28 on T37-2 which has
,
Resonance is when , when almost all the voltage drop is across
Q of filter is: . comes from the other components and must be measured
Note that is small for the other modulation product
L6
C37 (5pF)
C38 (100pF)
C39

## Slide 38
Exercise 13: Norcal Harmonic Filter
L7, L8 use T37-2 core, 18 turns, 1.3uH. Use termination and set function generator at 10Vpp.
Compute and compare loss at 7MHz and 14MHz.
From , calculate and
What is the spur strength at 7, 14 and 28MHz? Measure and calculate.
Need Puff (a simulator) to get losses. However, there is a 6dB drop-off at every frequency doubling
C47
330pF
C45
330pF
C46
820pF
L7
L8
Antenna
Jack out

## Slide 39
Exercise 14: Norcal IF Cohn Filter
X1 through X4 are 4.91 MHz
C10, C11, C12 are 270 pF
Set function generator to 50mVpp from function generator
Calculate R and X for filter
Measure the resonant frequency of one of the crystals
  Duh
Calculate the parameters of the crystal. Omitting
  and . We can measure and find Q using the 3dB bandwidth. is the resistance at resonance.
  If , ,
C10
C11
X1
X2
X3
X4
C12
C13
C9
Matching network
SA602 wants 1.5K
C14
47pF
L9 (18 uH)
Equivalent circuit for crystal
L
C
R
Cs

## Slide 40
Transformers
For solenoid, inside
. Since there are n turns in the solenoid, over the solenoid, , so .
This is the source of

## Slide 41
Exercise 15: Norcal Driver Transformers
, , ,
output .
Calculate
  ,
  ,
  , ,.
T1, 14:4
50
200
1K
100
50
10Vpp

## Slide 42
Exercise 15: Norcal Driver Transformers
Measure the 3dB cutoff, fc.

## Slide 43
Exercise 16: Norcal Tuned Transformers
. .
Measure 3dB bandwidth
Find P/P+
T2
  , is look forward, is look back resistance. ,
  , , , so ,
Similar calculation for T3.
T3, 23:6
T2, 1:20
50
1.5K
C4
5pF
C2
50pF
1Vpp
L4, 18uH
750
1.5K
C6
47pF
C14
47pF
10Vpp

## Slide 44
Acoustics
,
Gas moves and changes density: Displacement of undisturbed air is . At time it’s at , so , or + . So,
Change in density causes change in pressure: ), ), , or
Pressure differences cause motion: , Newton’s law gives
Substituting (1) into (3) gives , put
Solution is [Different than above].
To find, , note that the flow is adiabatic so and varies inversely as , so , and finally, using
,
Sound | Lp | Power density
rustling leaves | 10dB | 1pW/m2
broadcast studio | 20dB | 1pW/m2
classroom | 50dB | 10nW/m2
heavy truck | 90dB | 1nW/m2
Shout at 1m | 100dB | 10mW/m2
jackhammer | 110db | 100mW/m2
jet takeoff at 50m | 120dB | 1W/m2

## Slide 45
Bipolar Transistors - I
Bipolar source model
RS
vs
NPN Model
  Conducts when
  [, small signal]
  , ,
Switch
e
b
c
Bipolar model
 | Vbe | Vbc | Vce | ic
 |  |  | > | 
 | < |  | <- | 
 |  |  |  | >
 |  |  | * | 0
 | Vbe | Vbc | Vce | ic
 |  |  | * | 0
Bipolar equivalent circuit
b
e
c

## Slide 46
Bipolar Transistors - II
NPN Mode
  , ,
DC
Small signal
  Convert to AC only and simplify
  Thevienize
  Replace transistor with model
Active
<Vf
Vf
b
c
e
Saturated
Vf
Vf
b
c
e
Small signal - original
rS
Vs
Vcc
r1
rC
C
Vb
Vc
Ve
C
rL
r2
Small signal
rS
Vs
Vb
Vc
Ve
rc||rL
r1||r2
Step 1

## Slide 47
Bipolar Transistors - III
Small signal
  Convert to AC only and simplify
  Thevienize
  Replace transistor with model
    is the transistor model resistance between b and c
Small signal
rS
Vs
Vb
Vc
Ve
rc||rL
r1||r2
Small signal
rTh,in
Vth,in
rTh,out
Step 2
Small signal
rTh,in
Vth,in
rTh,out
gmVbe
Vbe
Step 3

## Slide 48: Transistor experiment
Experiment A
  , , , , 2n3904 transistor,
  With no transistor, adjusted so . A.
Experiment B
  Again, , , , , 2n3904 transistor, With no transistor, adjusted so . Put transistor in and .
  With transistor, A.
  Analyze these with our transistor model.
  Now use the Thevenin equivalents to analyze them.
RC
R1
R2
RE
VCC
Vc
Vb
Ve

## Slide 49: Transistor experiment - Thevenin equivalent DC
In Experiment A
  , .
  If , , which is close.
In Experiment B
  , .
  If , , which is also close, but a little high.
Turn this into a CE amplifier by adding 1uF input and output capacitors. Measure and calculate the voltages and gains.
RC
RE
Vc
Vb
Ve
+
-
+
-
Vcc

## Slide 50: BJT common emitter amplifier
Here’s how to design a common emitter amplifier. We use a 2n3904 transistor with 𝛽=150. This circuit will work! Build it.
  Pick the supply voltage Vcc=12V.
  Choose a gain (amplification factor), A = 5.
  Choose the “Q point” of the conducting transistor (4mA) and
  Vcc = (ic∙RC) + Vce + ie RE ∼ ie∙ (RC+RE) +Vce with ic=4mA. We get (RC+RE) = (Vcc - Vce)/(4mA) =1.75 k𝝮.
  Since A = 5 and A=RC/RE, RC= 5 RE so RE ∼ 270 𝝮 (this is a standard resistor value) and RC= 1.5k𝝮.
Credit: Ward, Hands on Radio.
Common emitter amp
RC
R1
Ci
Co
R2
RE
vs
VCC
vs

## Slide 51
ib = 4mA/𝛽 = 27 𝝁A.
Since Vbe must be greater than .7V throughout the input signal range, we want the voltage across R2 to satisfy Vbe + icRE = 1.8V.
Rule of thumb is current through R1 and is . We insert a voltage divider consisting of R1 and R2, so that R1= (12-1.8)/270 𝝁A ∼ 39 k𝝮.
Co and Ci are picked to offer small resistance to the frequency range we’re interested in and Co = Ci = 5 𝝁F.
I haven’t explained why we want RE but it provides thermal stability for the transistor over the range we care about. The fact that A=RC/RE can be calculated using Kirchhoff’s laws.
Credit: Ward, Hands on Radio.
Common emitter amp
RC
R1
Ci
Co
R2
RE
vs
VCC
vs
BJT common emitter amplifier continued

## Slide 52: Turn the transistor experiment into a CE amplifier
Add Ci and Co. Component values are:
  ,
  ,
Use a function generator to generate a , 10kHz.
The input impedance is , and the output impedance is . Add a load whose value is .
Now connect a scope to the output and measure the gain. Calculate what it should be an compare them. How do the input and output waveforms compare?
RC
R1
R2
RE
VCC
out
in
Co
Ci
RL

## Slide 53: BJT common collector amplifier
,
Q-pt: , (rule of thumb), .
(ROT), ,
,
,
, ,
Credit: Ward, Hands on Radio.
Common collector amp (Emitter Follower)
Co
RE
R1
R2
Vs
VCC
Ci

## Slide 54: BJT common base amplifier
, ,
, (ROT)
,
,
Common base amp
Ci
CB
R1
vi
RE
VCC
R2
RC

## Slide 55
JFETs
JFET circuit model (active region):
  , provided and is drain to source current when gate is at 0.
For circuit on right, and so
is cutoff voltage. When there’s no channel conduction.
For J309, , ,
DC:
AC: ,
G
S
D
V
Vi
RS
VDD
G
D
S
Vgs
G
Vgs
V
RS
AC model

## Slide 56: JFET common drain (follower) amplifier
, (if
G
S
D
out
in
RD
RS
Cout
Cin
RG
VDD

## Slide 57: JFET common source amplifier
, ,
. ,
,
From equation above, ,
G
S
D
out
in
RS
Cout
Cin
RG
VDD
RL

## Slide 58: JFET common gate amplifier
, ,
Solve for ,
Find
G
S
D
out
in
Cout
Cin
RG
RL
Vdd

## Slide 59
MOSFETs
MOSFET circuit model, is threshold voltage, is channel width, is channel length
  Ohmic:
  Saturation:
S
D
G
N channel MOSFET

## Slide 60
CMOS common emitter amplifier
Pick power
Bias around
Pick gain,
D
RD
RS
R2
R1
Ci
Co
S
VDD
CM

## Slide 61
Amplifier classes
V
t
Class D
V
t
Class E
V
t
Class F
Class Efficiency Characteristics
A 35% Full bias
B 60% Low bias
C 75% Saturating
D 75% Switch in pass-band
E 90% Voltage switch
F 80% Harmonic resonators

## Slide 62
Efficiency of class A amplifiers
Here, is the power from the supply, is the dissipated power, is the output power. is the collector resistor.
, is DC power
, where so ( is the collector resistance). Thus, .
AC load power is . So maximum efficiency .
DC load power is and so is transistor power.
Half the power in a class A is lost to load resistance. If we replace resistance with transformer, , where is the effective load resistance and , giving 50% efficiency. Transformer turns ratio controls peak-to-peak current. Maximum current is , where is the turns ratio.

## Slide 63
Amplifier gain
Let be the maximum input power (when load is matched) and is the voltage at maximum power.
V0
V
Rs
R

## Slide 64
Bipolar transistors - IV
At saturation, , so there is conduction from the collector to the base.
, is the thermal voltage, , is the base saturation current.
Note . Both increase rapidly with temperature
Base resistance
ic
ie
ib
rb
RS
V0
Vb
Vcc
Vc
R
RS
V0
Vb
Vcc
Vc
R
Vbb

## Slide 65
Emitter degeneration
To the usual transistor circuit (A), on the right, we add (B) is an equivalent circuit.
. Let be the output AC and be the input AC.
The gain is .
,
.
So (Doesn’t depend on ).
, so .
A
ic
ie
ib
rb
Vi
V
Re
Rc
B
RC
CM
RE
VCC
Vi
ic
ib
rb
V

## Slide 66
Emitter degeneration
is called a Miller capacitor and it arises from a capacitance, , between the collector and emitter. . is the maximum current between base and emitter in the equivalent circuit on the right.
With the Miller capacitor,
, is the collector resistanc.e
, is the base resistance. is the combined source resistance.
is called the collector impedance and , is specified in data sheet (8pF).
,
.
, so
ic
ie
ib
rb
Vi
V
Re
Rc
Cm
im
ic
ie
ib
V
Re
zc
Rs’
i

## Slide 67
More on emitter follower
,
RE
Rs’
VCC
Ve
Vi
Vb

## Slide 68
JFET follower
Vi
V
R
vgs

## Slide 69
Differential Amplifier
Pick power
Choose collector current () by picking
Pick gain,
Two port model
Differential amplifier
vO
vin
RC
vin
RC
RE
RE
R1

## Slide 70
Exercise 19: Norcal receiver switch
Consider the rising part of the base voltage waveform. Calculate slope.
Do the same for the falling part for voltage below .6V. Calculate t2.
Measure the switch attenuation
  When the transistor is saturated, the drop across ce is 1.4V. At full power, and , so
Measure the voltage with the switch on. Measure output voltage and calculate on-off rejection ratio R=20 log(Voff/Von)
L1 (15uH)
Harmonic filter
2N4124
8V TX
C1
50pF
R1
1.8K
C2
47nF
Antenna
P

## Slide 71
Exercise 20: NorCal transmitter switch
For transmitter switch, saturation resistance is , .
is current into the load. In Norcal, For 2n3906, to ensure saturation, .
Calculate voltage on C57. Measure time for capacitor to charge half-way. Calculate what the time should be.
  .
Calculate the approximate current ic when Q4 is on. Assume base voltage on Q1 is 700 mV. Neglect saturation voltage on Q4. Calculate base current ib required to produce this collector current assuming .
Calculate ib at key down assuming a 700 mV drop-in base-emitter of Q4 and at 600mV at D11
  , ,
Sketch collector voltage at Q4 showing where transistor is saturated. What is the delay in going active?
Use the delay to measure .
2N3906
relay
Key jack
R24 (150K)
R9 (47K)
C57 (47nF)
12V TX
12V
Vb

## Slide 72
Exercise 21: Norcal Driver
Measure the output voltage and calculate the power, P.
Calculate the power from the power supply.
Measure the voltage gain with R13 at minimum and maximum gain.
,. This is a class A amplifier.
, ,
.
,,
From text,
Gain is between 2.5 and 60
2N2222A
C56
10uF
12V
V
R11
510
T1
R12
20
R13
500
R14
100
Key jack
+
C48
10nF
Vi

## Slide 73
Exercise 22: Emitter degeneration
In Driver amplifier, add probe to R11, this allows us to measure the AC voltage,
Measure with R13 turned fully counterclockwise and then fully clockwise.
  When is fully counter clockwise ,
  When is fully clockwise ,
  Calculate the expected voltage gain for each setting of R13
Measure at the maximal gain setting
The open circuit voltage is , calculate in terms of
  , , so
Vi
Rc
CM
Re
rb
ie
im
ic
V

## Slide 74
Exercise 23: Norcal Buffer amplifier
R11 determines the bias. Adjust R13 to minimum gain. Measure the DC voltage at source of the JFET (VS).
Calculate the drain bias current. Calculate the source and drain voltages you should expect
  . DC: .
  , . ,
Calculate and measure the voltage gain of the buffer.
  , or about 1 since
Find the transconductance using the measured voltage gain.
Calculate the available power P+ from the function generator through a 1.5Kohm load. Calculate gain in dB.
1.5K
C50
25pF
C36
47nF
12V TX
Driver
R11
510
C39
50pF
R10
510
L6
3.1uF
C38
100pF
J309
Pin 4 transmit
mixer
Function
Generator
C37
5pF
D
S
VG
VS

## Slide 75
Class C amplifiers and Norcal 40 Power amp
Here is the power from the supply, is the dissipated power, is the output power. The Norcal Power amplifier is a class C amplifier. For switch model, switch represents the transistor, when the transistor is on, the switch is open.
(switch off), (switch on)
,
,
, is input filter impedance
Cap energy:
+
-
Is
+
-
Switch model for class C amp
I0
Vcc
Von
Vs
Vm
Vs
Von
Supply power
3,200 mW
Power transistor
Antenna
2500 mW
Active loss
Pa, 260 mW
Active loss
Pon, 430 mW

## Slide 76
Exercise 24: Norcal Power Amp
Harmonic
Filter
2N3553
C44
47nF
12.8V
R14
100
R14
1
RFC
18uH
IN4753A
Driver
Measure the peak-to-peak voltage across 50ohm load required for output of 2W. Calculate it and compare. Calculate the gain in dB
  , ,
  , ,
Find pp output voltages or 5, 10, 15, 20, 25 and 30V. Calculate power supply current subtracting 2mA for regulator
Calculate the output power, efficiency and and dissipation power.

## Slide 77
Thermal modelling
is heat sink temperature, is ambient temperature, is power dissipated.
, is the thermal resistance
, is the thermal capacitance
, is the junction temperature
,
, ,
, .

## Slide 78
Exercise 25: Thermal modelling
For Motorola 2N3553,
Measure ambient temperature
Turn function generator until output is 30Vpp
After 20 minutes, measure . Use this to calculate and
Plot heat sink temperature vs time. Measure and calculate
Need measurements

## Slide 79
Clapp oscillator
Oscillation condition
  Ly=x
  and
Clapp (circuit on right)
  Resonance:
  ,
  At resonance, ,
  Oscillation continues if
12v
out
C1 (1200pF)
C2 (1200 pF)
L (19uH)
C3
R
G
L
y
x

## Slide 80
Norcal Receiver Incremental Tuning (RIT)
LM393 is a comparator
RIT allows transmit and receive frequency to be offset.
If transmitter is on, TX will be 8V and the left comparator will be off, the right one on and R15 will be grounded.
For receiving, TX is <1.4V, disconnecting R15 and shorting R16 to ground.
LM393
1
2
3
4
8
7
6
5
12V
R16
1K
RIT 1
R15
510
12V
off
on
1.4V
From VFO

## Slide 81
Exercise 26: Norcal VFO
Check MVAM108 capacitor when R17 is high and low
Start resistor (R21) pulls gate to ground at start
When gain limiting diode (D9) conducts, it pulls gate negative
Oscillator keeps growing as long as gm>1/R
Measure p-p voltage, V. What should you expect?
Measure DC voltage across wiper in R17
Calculate expected V for large signal oscillation
How does the frequency change as R17 changes?
Calculate the oscillation frequency and the loss ratio |V/VI|
How would this change if you took when L9 is turned off.
TX VFO
RX VFO
C49
47pF
R17
10K
R15
510
R19
47K
R20
4.7K
C54
47nF
C7, 10nF
C32, 150 pF
RFC
1mH
R23
1.8K
C52
1200pF
C53
1200pF
D8 MVAM108
C51
390pF
R21
47K
D9
L9
C50
25pF
J309
12V
Ground

## Slide 82
VFO Problem
The figure on the right is an equivalent circuit for the oscillator. The varactor, varies from 30 to 600 pF depending on the voltage.
, , , ,
The equivalent capacitance for is .
When , the equivalent capacitance for is and . At the resonant frequency, . .
When , the equivalent capacitance for is . At the resonant frequency, . . .
These values are what we want for the tunable VFO.
L9
C5
C1
C4
C2
C3
C6

## Slide 83
Gain Limiting in Norcal 40
The gain here is limited by the diode. .
, is the forward voltage of the diode.
, or
,
Oscillation condition is
Vs
C1
C2
RFC
C3
R
Vdd
Vg

## Slide 84
Exercise 27: Gain limiting
Measure the voltage, V, on R23
In deriving the oscillation condition, we neglected the inductor resistance and drain source resistance, How does this affect the conditions. L9 has a Q of 250 and , now what is the predicted V.
Find the loss ratio and calculate what it should be.
Measure the temperature dependence of the VFO
How much does the temperature have to change to cause a 100Hz shift?
What is the oscillation change if we remove one turn of the inductor
What is the RIT tuning range?
Need measurements

## Slide 85
Gain limiting
x.

## Slide 86
Mixers
is a square wave with period . Expanding this in a Fourier series, we get:
,
+
and
We define and and and
and , is a spurious signal. and are the spurs from the th harmonic
LO
Image
IF
RF

## Slide 87
Exercise 28: Norcal RF Mixer
Measure conversion gain of the Mixer.
How much attenuation is provided by pot?
By how many dB is the image response suppressed. Look at the spur
Need measurements
SA602
1
2
3
4
8
7
6
5
C18
47nF
12V
C5
10nF
IF Filter
T2
RX VFO
C4
5pF
C6
47pF
T3
RF
Filter
C2
50pF
From VCO

## Slide 88
Exercise 29: Norcal Product Detector
620 Hz output through AF1 and AF2
AF2
AF1
SA602
1
2
3
4
8
7
6
5
C18
270 pF
12V
C15.
C17
50 pF
4.91 MHz
IF in
1.4V
Adjust C17 for minimum oscillation frequency and record it
Calculate the minimum oscillation frequency you’d expect
Measure the temperature coefficient for the BFO
Measure the gain through the receiver from the antenna through the product detector
Find the f5 spur calculate the expected f3
By how much is the if spur suppressed
Need measurements

## Slide 89
Product detector
x.

## Slide 90
Exercise 30: Norcal transmit mixer and oscillator
SA602
1
2
3
4
8
7
6
5
C36
12V
C33
C34
4.91 MHz
Buffer
Amp
TX VFO
L5
C31
How much would you expect the inductor to lower the oscillation frequency
Use the TX VFO and the voltage attenuation to calculate the input power from the transmit mixer. Calculate the gain through the entire chain
Measure the rise and fall time of keying response
There is a spurious fmn=mfvfo+nfto.
Need measurements

## Slide 91
Op Amps
Ideal op amp
  , is an op amp parameter between and .
  for negative feedback
Example 1: Inverting amp, we’ll show the gain is
  , since the op amp has infinite input impedance
  By Kirchhoff, , so
  is same as non-inverting.
Example 2: Non-inverting amp
  , so
  , , is the Thevenin resistance of the op amp
Vo
Vi
An op amp
Inverting amp
R2
R1
Vout
Vin
i1
i2
+
-
Noninverting amp
R2
R1
Vout
Vin
+
-

## Slide 92
Exercise 31: Norcal Audio Amp
+
-
386
2
3
5
6
C30 (2.2 uF)
C27 (100 uF)
+
12V
+
C55 (10 nF)
Speaker
C26 (10 uF)
AGC pt
8
1
C23
2.2uF
+
4
R22
1.8K
Audio in
R6
500
+
Calculate input Vi assuming very high input impedance
Measure the voltage gain Gv at high frequency and 3dB roll-off
Input impedance is high.
The 386 acts like a non-inverting op amp. The internal feedback resistor is . With pins 1, 8 open, , so pins 1 and 8 go across of . So, shorting them (using the non-inverting gain circuit) results in a gain of

## Slide 93
Exercise 32: Norcal AGC
Connect function generator through 300K resistor to AF2 (620Hz sine, R6 fully counterclockwise) and oscilloscope to audio output. Adjust input so output is 1V rms. Connect multimeter to P.
Plot audio output v dc control
What is the maximum control voltage we can measure? Infer cutoff voltage
What is the minimum control voltage?
Need measurements
C28
AF1
AF2
12V
Audio in
audio amp out
R5c
R5a
R5b
R5d
C55
C21
J309
R6
10K
Threshold
D6
D5
D2
D1
Audio in
P
Q

## Slide 94
NorCal power levels
log(P)
log(P)
1pW
1nW
1W
1W
1mW
1pW
1nW
1W
1W
1mW
VFO
Audio out
Buffer
Power
Driver
AGC
Detector
Crystal
Mixer
RF filter
Antenna
Space
2000km

## Slide 95
Noise
, is load resistance
, is noise power density, is bandwidth
Nyquist
  Expected energy at resonance is
  by equipartition theorem
  So,
  , ,
C
R
L
VC
Vn

## Slide 96
Antennas
From Maxwell, for a plane wave (E in x direction, H in y direction), wave is of form
Substituting and taking the restricted cross products, we
get: , so
Power density:
Impedance: , is real part of ,
Power density for isotropic antenna:
Define . is just the Poynting vector
Receiving antenna Thevenin
C
R

## Slide 97
Transmitting Antenna
Define . is just the Poynting vector
For isotropic reference: ,

## Slide 98
Receiving Antenna
              , is effective antenna length ( for short antenna)
              For dipole:
              . This is the definition of the effective area, .
    By reciprocity,
    , so
Dipole Thevenin equivalent circuit
C
R
is length of dipole

## Slide 99
Friis, blackbody and Antenna Theorem
For transmitting/receiving antenna pairs: . So
    . --- Friis radiation formula
    For us,
Antenna theorem:
For cavity on right, T is constant at thermodynamic equilibrium and the same power is transmitted and emitted, the Johnson noise is . The energy received is
  .
  Set .
  hich gives the antenna theorem
Insulated cavity
T
A

## Slide 100
Reciprocity
Reciprocity: The position of an ideal voltmeter and ideal current source can be interchanged without changing the voltmeter reading.
G1, A1, R1
G2, A2, R2
V
I

## Slide 101
Reciprocity and dipoles
For dipole (Length: )
, so
and Note we used
,
,

## Slide 102
Exercise 35: Intermodulation
Only are close enough to the rf frequency to matter for intermodulation
Find coefficients and frequencies for
Find , , and
Find the MDS and the antenna limited MDR
, is input that gives output tone +

## Slide 103
Exercise 37: Antennas
Use the relation between gain and effective area to rewrite the Friis transmission formula in terms of gain only. Consider UHF for airplanes. If the frequency makes the quarter length stub antenna have gain 2, find the maximum possible LOS at 10km height. Required receiver power is –90 dBm. Find the minimum transmission power.
  Friis radiation formula is , and , so
  requires power. , so must be at least .
  . , , and
Find the inductance to resonate with a 3m whip. Assuming the Q of the coil is 200, find the turns ratio required to give a transceiver a 50 ohm load. What is the radiation efficiency?
  For whip, . . .
  , .
  Radiation efficiency is

## Slide 104: Norcal circuit diagram, 1

## Slide 105: Norcal circuit diagram, 2

## Slide 106: Norcal circuit diagram, 3

## Slide 107: Norcal circuit diagram, 4

## Slide 108: Norcal circuit diagram, 5

## Slide 109
Appendix

## Slide 110
Exercise 17: Tuned Speaker
Connect speaker to function generator 600Hz, 25mVrms.
Sound peaks at resonance. Find resonant frequency Lp.
Measure fl, fu by noting the 3dB loss. Calculate Q.
Use voltmeter to find resonance with speaker (nominally 8ohm) to calculate impedance
Calculate the resonant frequency from a transmission line equivalent circuit.

## Slide 111: Morse
Symbol | Code | Symbol | Code | Symbol | Code
a | ._ | m | __ | y | _.__
b | _... | n | _. | z | __..
c | _._. | o | ___ | 0 | _____
d | _.. | p | .__. | 1 | .____
e | . | q | __._ | 2 | ..___
f | .._. | r | -_. | 3 | …__
g | __. | s | … | 4 | …._
h | …. | t | _ | 5 | …..
i | .. | u | .._ | 6 | _....
j | .___ | v | …_ | 7 | __...
k | _._ | w | .__ | 8 | ___..
l | ._.. | x | _.._ | 9 | ____.

## Slide 112: Color codes
Resistors markings in ohms
Capacitors markings in picoFarads
Inductors markings in microHenries

## Slide 113: Component data
IRON POWDER TOROIDS - Al Values **
* size not available in this material ** L= µH/100 turns
Core Size | 26 | 3 | 15 | 1 | 2 | 6 | 10 | 12/17 | 0
T-12-( ) | * | 60 | 50 | 48 | 20 | 17 | 12 | 7.5 | 2.4
T-16-( ) | 145 | 61 | 55 | 44 | 22 | 19 | 13 | 8 | 3
T-20-( ) | 185 | 76 | 65 | 52 | 25 | 22 | 16 | 10 | 3.5
T-25-( ) | 245 | 100 | 85 | 70 | 34 | 27 | 19 | 12 | 4.5
T-30-( ) | 335 | 140 | 93 | 85 | 43 | 36 | 25 | 16 | 6
T-37-( ) | 285 | 120 | 90 | 80 | 40 | 30 | 25 | 15 | 4.9
T-44-( ) | 370 | 180 | 160 | 105 | 52 | 42 | 33 | 18.5 | 6.5
T-50-( ) | 330 | 175 | 135 | 100 | 49 | 40 | 31 | 18 | 6.4
T-68-( ) | 435 | 195 | 180 | 115 | 57 | 47 | 32 | 21 | 7.5
T-80-( ) | 460 | 180 | 170 | 115 | 55 | 45 | 32 | 22 | 8.5
T-94-( ) | 600 | 248 | 200 | 160 | 84 | 70 | 58 | * | 10.6
T-106-( ) | 930 | 450 | 345 | 325 | 135 | 116 | * | * | 19
T-130-( ) | 810 | 350 | 250 | 200 | 110 | 96 | * | * | 15
T-157-( ) | 1000 | 420 | * | 320 | 140 | 115 | * | * | *
T-184-( ) | 1690 | 720 | * | 500 | 240 | 195 | * | * | *
T-200-( ) | 920 | 425 | * | 250 | 120 | 100 | * | * | *
T-200A-( ) | 1600 | * | * | * | 218 | * | * | * | *

## Slide 114: In the beginning…
The laws of EM according to Clerk Maxwell are:
  , ,
    Here E is the electric field, B is the magnetic field, j is the current density through a closed surface, c is the speed of light and 𝜌 is the charge density at a point.
    In non-dispersive matter, , ,
    and (1) becomes (4) becomes
The rest of classical physics, including special relativity, is:
  Newton-Einstein: , , .
  Gravity: where ur is the unit vector from m1 to m2 and F is the force on m2.

## Slide 115: Solutions to the wave equation
The solution of is where
Later, we will use this to find the ”general” solution to Maxwell’s equations
  and , where
  , , and,
You are not expected to have guessed this answer
To do this, we’ll need the “BAC-CAB” identity: (A B)
When we apply this to , we get (

## Slide 116: General solution to Maxwell’s equations
Returning to the general Maxwell equations, from , we get
Substituting into , we get
Applying “BAC-CAB”, we get (Equation 1)
Now, , so substituting for B, we get and so
Substituting into equation 1, ), or
- .
-
Now if and give and , then and give and for any function

## Slide 117: General solution to Maxwell’s equations
Thus, we can pick a solution with . Then we get
-
Substituting for into , we get
, or , or -
The solutions are and
with , with .

## Slide 118: Solution to Maxwell’s equations in free space
Free space is defined by and , so our potentials satisfy
- 0 and -
These have the usual wave equation solutions , etc
Thus, in free space 𝜙 and A and hence E and B propagate as waves.

## Slide 119: Solution to Maxwell’s equations in conductors
In conductors,
  This becomes
  , so we get (since in a conductor)
  Applying the trial solution E= E0 exp(𝜔t-kr), we get –k2-i𝜔𝜇𝜎 + 𝜔2𝜇𝜖 = 0.
  Putting k = 𝛼-𝛽i, and .
  For copper, 𝜎 = 5.78 × 107 𝞨-m. This explains the “skin effect” in conductors.

## Slide 120: Radiation, antennas
Accelerating charges radiate energy in the form of electromagnetic waves (companion E and B fields).
The radiation from accelerating charge q is .
Here, a⊥ is the acceleration ⊥ to the line from r1 to r2.
For example, applying a time varying potential V0sin(𝜔t) to an antenna will cause the antenna to radiate power since the voltage and hence charges affected accelerate within the antenna, that is, their positions have a non-zero second derivative. That’s how a transmitter “couples” to the antenna of a receiver. In the receiver, the radiated wave accelerates charges in the antenna replicating the original wave (at much reduced power).
These simple radio waves are carrier waves of frequency . To transfer information (voice, images, binary data), we modulate carrier waves combining them with an “information source” signal. Receivers demodulate the incoming wave and recreate the original “information source” signal.

## Slide 121: Maxwell’s equations in a non-dispersive media
,

## Slide 122: Radiation from a small dipole
If
Choosing gauge,
z
y
q(t)
-q(t)

## Slide 123: Radiation from a small dipole
)
z
y
q(t)
-q(t)

## Slide 124: Radiation from a small dipole
, , (u is energy density)
z
y
q(t)
-q(t)

## Slide 125: Large half wave dipole
For large half wave, add small dipoles to produce half wave antenna.

## Slide 126: Radiation from an accelerating charge
, R= |r-r’|

## Slide 127: Radiation from a single accelerating charge
Near zone

## Slide 128: Radiation loss and antenna aperture
Spreading loss:
  d in kilometers
  F in megahertz
,

## Slide 129: Antenna aperture
Deriving antenna aperture uses thermodynamic argument: black body equilibrium
(Rayleigh-Jeans)
R
T
T
PA
PR
Filter[+
A

## Slide 130: Impedance matching
L networks, and T networks
Impedance and reflection coefficients

## Slide 131
Blank
x.